Air Traffic Control Corpus
                           (ATC Corpus)

                NIST Speech Discs 16-1, 16-2, 16-3, 
                 16-4, 16-5, 16-6, 16-7, and 16-8

			  December, 1993



TABLE OF CONTENTS

1.  Summary Abstract
2.  Directories, files, and formats
3.  Design Principles
4.  Collection protocol 
5.  Transcripts
6.  The Dallas-Fort Worth (DFW) Corpus
7.  The Logan International (BOS) Corpus
8.  The Washington National (DCA) Corpus


ATTACHMENTS
A.  Equipment List
B.  Abbreviations used in DFW Transcripts




1.  Summary Abstract

The Air Traffic Control (ATC) Corpus consists of nearly 70 hours of
recorded communications between controllers and aircraft at three
major US airports.  It is really best thought of as a set of three
smaller corpora, which will be referred to by the names or
three-letter abbreviations of the airports where they were collected:
the Dallas-Fort Worth or DFW corpus, collected at Dallas-Fort Worth
International airport in Texas; the Logan or BOS corpus, collected at
Logan International Airport in Boston, Massachusetts; and the
Washington National or DCA corpus, collected at Washington National
Airport in Arlington, Virginia.

The data were collected by Texas Instruments under contract to DARPA
for the purpose of supporting research and development activities in
the area of robust speech recognition for signals like ATC -- many
speakers, noisy channels, relatively small vocabulary, constrained
language, etc.

Each corpus consists of 20 to 25 hours of voice communications traffic
between controllers and aircraft, recorded via antennas and radio
receivers in the vicinity of the airport.  The speech files are 8 kHz,
16-bit linear sampled data, representing continuous monitoring,
without squelch or silence elimination, of a single FAA frequency for
one to two hours.  Each speech file is fully transcribed, and the
transcripts include time markings to indicate the beginning and ending
of every transmission in the sampled data.

The three corpora differ in several respects, due partly to
differences in the ATC systems at the three airports, and partly to
decisions made during the more than two years of design, collection,
and processing.  For one example, the Logan and National data sets
include, for each speech file, another file indicating the amplitude
of the carrier frequency signal at regular intervals; for another, the
National recordings are from a different radio receiver than the other
two.  Thus each dataset requires some documentation of its own, and
users are advised to read the description of each corpus before
deciding which one best meets their needs.

In addition to the three airports, with their different local
terminology and details of organization, there are several ATC
functions sampled in some depth, involving takeoffs, landings,
approaches, departures, and taxiing.  Other functions are
underrepresented or absent due to limited resources.  Likewise, some
important factors affecting ATC language and protocol could not be
varied systematically in a corpus of this size.  For example, weather
conditions determine which runways are used, in which direction
traffic flows, and whether Instrument Flight Rules (IFR) prevail.  To
sample this and other such sources of variability adequately would
have required a corpus many times the size of this one.




2.  Directories, files, and formats 

Each airport corpus is on a separate set of CD-ROM, three each for DFW
and DCA, and two for BOS.  Within each corpus, the data is contained
in .wav files (sampled data), .txt files (transcripts), and .cdt files
(receiver carrier-detect signals, for the BOS and DCA airports
only) of the form aaa_pp_n.wav, aaa_pp_n.txt, and aaa_pp_n.cdt, where
aaa is the airport (dfw, bos, or dca), pp is a two-character
abbreviation of the ATC position name (which may have a digit as its
second character), and n is an integer index.  Where there are several
files from the same position, the index numbers indicate the order of
collection.  For example, in the DFW dataset there are three
recordings, each an hour long, collected from the Arrival Radar Two
position at different times, identified as dfw_a2_1, dfw_a2_2, and
dfw_a2_3.




3.  Design Principles

The initial specifications for the Air Traffic Control (ATC) corpus
were drafted in June 1989 at a DARPA meeting attended by technical
representatives of several interested government agencies and
contractors.

Tom Crystal of IDA suggested sizes and dimensions for the corpus,
based on his calculations of desired statistical properties.  These
were later circulated in a written form for review.

The fundamental consideration in determining size and dimensionality
was that there be enough "trials" so that experiments could be
conducted and the results accepted with a high degree of confidence.
A trial, in this sense, would be an event whose occurrence could be
determined by accurate recognition and interpretation of the speech:
for example, the presence in the airspace of a particular aircraft
(identified by its flight number), or the fact that a particular
aircraft was in the process of landing, taking off, taxiing, or any
other activity that is signaled by the utterances in the ATC dialogs.
Thus an hour of ATC might contain 600 transmissions, consisting of 300
dialogs, involving one controller and 80 aircraft.  This could provide
80 trials of flight id recognition, or 300 trials of dialog
recognition, or 600 trials of utterance (or "sentence") recognition.

However, at the time of these discussions the other experimental
parameters besides airports were not fixed, because not enough was
known about the application in advance.  For example, would an hour of
data each from two different departure control positions at the same
airport, or even from the same position under different weather
conditions, belong in the same experiment?  Or recordings of "feeder"
and "arrival" at DFW, where approach control is split into two
positions?  If there were standard answers to these questions, they
would help to determine the number of types and tokens in the corpus.

To discuss such issues, and to make final determinations of the
requirements of the ATC corpus, a Steering Committee made up of
representatives from ARPA (Dr. Thomas Crystal), Rome Laboratories (Dr.
Edward Cupples), and BBN (Dr. Robin Rohlicek) was set up to advise TI
on the collection and processing of the data.

Initial estimates were that 10 to 15 hours each would be required from
as many as four civilian and one or more military airports, with
emphasis on a variety of different functions and multi-function
"scenarios".  For example, it was decided at first to record
simultaneously from multiple positions dealing with the same aircraft
successively over time, so that an AI-style system could use this type
of information as a constraint to improve overall performance.  Thus
the hypothesized detection of a particular flight communicating with
the Arrival controller makes it more probable that the same flight
will be detected within ten minutes communicating with Tower, and a
few minutes later with Ground.  Accordingly, much of the DFW data was
collected in multistation one-hour sessions, in such a way that the
same aircraft often appear in two or three recordings as they progress
through different positions.

After the first few data collections at DFW, however, the complexity
of the ATC system as a speech recognition application became more
evident, and the need for homogeneous training data for speech
recognition began to dominate the assessment.  It was then decided
that about 24 hours of data from four or five "different" functions at
DFW would serve as a pilot corpus, after which the amount of data per
function and the number of functions could be determined for other
airports.

Based on _a priori_ estimates of traffic volume at DFW, it was felt
that even the least frequent event (flight id) would occur often
enough to produce reliable statistics for evaluation from a few hours
of test data.  At a hoped-for 50 events per hour, about 24 hours per
scenario (airport), divided among about four functions, was deemed
sufficient data for reliable development, testing, and evaluation in
the first round.

Although the committee never reached a definitive position on what the
"standard" subdivision of the ATC data should be, it did approve the
collection of more data per position from fewer positions at the next
two airports, in recognition of the number of other variables which
can affect performance of any speech recognition-based technology on
ATC.  Thus the 24 hours of published DFW data come from eleven
different ATC positions, which may arguably be reduced to five or four
functions; the 20 hours of BOS data cover just four positions
representing four functions, three of which have at least rough
equivalents at DFW, and the 25 hours of DCA data cover five positions
with just three functions: final approach, tower, and departure.

>From the point of view of pragmatics, therefore, DFW represents the
broadest sampling and DCA the greatest depth, with BOS in between.
See the individual corpus descriptions for more details.

4.  Collection protocol

This section describes the procedures followed in collecting all the
data, as well as some of the differences from airport to airport.
Refer to the sections on the individual datasets for more detail on
these differences.

EQUIPMENT.  At the recommendation of Rome Laboratories, TI purchased
four multipurpose Radio Shack Pro-2005 scanner/receivers (RS2005), a
discone antenna, a splitter-amplifier and other necessary hardware for
the recording.  The four receivers were needed to fulfill the
requirement for parallel data at DFW from four ATC positions at once.
Afterwards two of these receivers were used at Logan, and a different
radio at DCA.

Before any data was collected, TI Central Research Laboratories' Tests
and Measurements Lab used a signal generator and spectrum analyzer to
measure the frequency response of each individual receiver, both to
check their integrity and to rule out any significant differences
among the four.  They were all found to be within their published
specifications, and very close to each other in both frequency
response and harmonic distortion over the 200-4000 Hz range.  Figures
1-4 show their audio levels and distortions as a function of frequency.
(Figures are located in the image directory.)

For the first few sessions (about one half of the DFW data), the
recording was done on video cassette recorders with digitizers at 44.1
kHz, then converted and downsampled to 8 kHz 16-bit computer files.
When Digital Audio Tape (DAT) players became available, the remaining
data from DFW, and everything from BOS and DCA, was recorded on DATs.

PROCESSING.  All speech data are in Unix binary files, with 16-bit
values at 8 kHz sampling rate, in NIST's SPHERE format.  The digital
files for the DFW data were produced at TI; there was a slight
difference in how the data from the first three and the last two
sessions were processed, which is described in section 6.  The digital
files for BOS and DCA were produced at BBN, courtesy of Robin Rohlicek
and Manhung Siu.  Their software produced the 8 kHz versions of the
data which are included here, by downsampling and filtering directly
from the DAT tapes.

The downsampling was done using a lowpass 256 coefficient FIR filter
with the passband limited to telephone bandwidth at the upper edge.
Figure 5 shows the frequency response of the filter.  (Figures are 
located in the image directory.)

LOCATIONS.  The recording sites are described separately for each
airport.  What they have in common is that they were in buildings with
line of sight (or nearly so) from the receiving antenna to most of the
transmitters (i.e., the aircraft and the ATC tower antennas).  This
siting was always a compromise among the many factors affecting
reception.  For example, in a hotel room facing the airport antennas,
the arriving and departing aircraft will be on the other side of the
building for at least some of the time.  Close to the ATC antennas,
the reception of controllers, aircraft on the runways, and aircraft on
final approach will be better, but that of aircraft just beginning or
at the far end of their approach turns will be worse.

The DFW corpus was collected over 5 sessions, each at a
different place and time, while the Logan and DCA corpora were
collected from one location over a period of consecutive days.

PROCEDURE.  The DFW collection was designated as a "pilot corpus" from
the beginning, and minor changes in collection protocol and even
equipment were allowed between recording sessions for this reason.
They are documented in the section on the DFW corpus.  Offsetting this
is the fact that there was far more DFW data collected than could be
published, and the "worst-sounding" recordings (those with the most
out-of-band interference, usually) were set aside.  On the whole the
DFW data is probably no less uniform or more difficult to deal with
than the other two sets.

The BOS recordings used the same receivers, antenna, and DAT recorders
as the later DFW data.  They were made from a similar location, but in
three days of nearly continuous recording rather than in sessions
spread out over time.  The Logan airport layout and its ATC functions
are very different from DFW, which implies changes in vocabulary,
phrasing, and pragmatics.  This is reflected in the choice of only
four functions, none of which are exactly like any of the DFW
functions.  Files are also longer, typically two hours rather than
one.  The processing of the data also changed somewhat: BBN provided
software to downsample and filter the 48 kHz DAT signal to produce the
8 kHz speech files, avoiding the resampling step required with the DFW
data.

The DCA data is a significantly different signal from DFW and BOS; a
new, aircraft-quality receiver and matched antenna were used to improve
selectivity without loss of sensitivity.  The location, on the roof of
the ARPA building a few miles north of National Airport and close to
the flightpath in a south flow, was comparable to the Hilton location
for DFW.  Its only serious disadvantage was that signals from aircraft
on the ground were sometimes temporarily blocked when they taxied
behind the terminal buildings.  As in the case of Logan, DAT
recordings were made more or less continuously over a three day period
without moving or changing equipment.  The ATC functions were more
similar to DFW than to BOS, but not identical to either.

ATC FUNCTIONS AND POSITIONS.  The role of an air traffic controller in
a major metropolitan airport terminal is defined in terms of the
entire system for that airport, a subject too far afield for this
document.  Nevertheless a brief discussion of the terms may be useful.
The major terminal-based functions are as follows:

Ground Control (GC): Typically guides aircraft from company gate or
terminal area via taxiways to last ramp before takeoff, and from the
first off-ramp to the terminal area after landing.

Local Control (LC), also called Tower: Typically handles aircraft on
final approach, clears them to land, hands them off to Ground Control;
also takes aircraft from Ground Control, clears for takeoff, then
hands off to Departure Control.

Departure Radar Control (DR), also called Initial Departure (ID) at
BOS, Departure Low at DCA: Typically handles departing aircraft from
shortly after takeoff to a certain altitude, where they are handed off
to either a high altitude Departure Control (at DCA) or to a
"Transition" controller (at BOS), or immediately to an enroute
controller (at DFW).

Arrival Radar Control (AR), also called Final: Typically handles
aircraft during final approach maneuvers within the greater terminal
radar control area; hands off to Local Control within a few miles of
runway for landing.  May be split into Feeder and Final (normally at
DFW, rarely at DCA).

Feeder Control (FE, FW for East and West at DFW): Typically guides
aircraft approaching from various directions into a line for the
downwind leg of final approach, then hands off to Final (AR).  Same
general type of communications as Final, but first contact may be 30
miles out from runway.

Transition Control (SM) also called Plymouth at BOS: Typically guides
both departing and arriving aircraft at some distance from the
airport, like Departure High for departing aircraft at DCA, and like
Feeder for arrivals at DFW.

Positions vs. Functions: These functions may each be performed by more
than one controller at an airport, even at the same time. At DFW,
where parallel runways permit most operations to proceed independently
on two sides, there are one, two, or three controllers handling
departures, depending on a variety of factors; so at a particular
time, Departure Radar Three (DR3) may be the only one on the air.  Let
us use the term "position" for the local name associated with a
particular frequency manned by one controller.  This name generally
signifies the primary responsibility of the controller on that
frequency: Ground Control East at DFW, or Plymouth Transition at Logan
(handling both incoming and outgoing traffic near the intersection
called Plymouth.)

Note also that, although positions may be named for their principal
functions, each controller actually "owns" a defined three-dimensional
airspace, and the "arrival" and "departure" positions also deal with
any aircraft passing through their airspace, even though it may not be
arriving or departing their airport.  For example, the Feeder East
position at DFW often handles flights on their way to and from Love
Field in Dallas, in addition to those arriving at DFW.

Combined positions: It is not unusual for a controller at one position
to take over what would be done by another controller at another
position. In fact, this is routine in smaller airports and at off-peak
hours for reasons of efficiency.  Particularly during slow periods,
controllers may "combine" positions without notice, so that they can
be heard on two frequencies.  A receiver set to one of these
frequencies will hear all the controller's transmissions but only some
pilots' answers, since the others are communicating on another
frequency.  This commonly happens, for example, with the departure
positions at DFW.

The ATC positions represented in these corpora are standard in their
respective airports, and were recorded deliberately during relatively
busy traffic periods.  This strategy was dictated by the need for
training data.  Experiments with enroute and military ATC positions,
for example, yielded less than one quarter as many transmissions as
these busy metropolitan terminal positions, so that enormous numbers
of hours would have to be collected and condensed in order to provide
training data for most algorithms.

However, even major airports are organized in different ways, so one
must not assume that similar sounding positions, even those with the
same name, perform exactly the same function in different airports.
For example, at DFW there are two tower controllers, one handling
traffic landing and departing on the east side runway(s), one handling
the same on the west side.  In Boston, where the major runways
intersect, there may be two tower controllers on the air, one of whom
handles mostly takeoffs and the other mostly landings.  See the
descriptions for each airport below.


5. Transcripts

Air traffic control speech is difficult for most laymen to understand
for several reasons: channel limitations, noise, rapid pace, and
specialized jargon, for example.  Most important, however, is the
absence of contextual constraints; there actually are numerous
constraints, but only the participants know them and can exploit them.
For example, knowing the usual downwind path of arriving aircraft and
the current position of a particular one makes the controller's
direction (e.g., "turn right heading one zero seven") natural and
obvious; without that information almost any numbers could occur.
Although lay transcriptionists can and do learn to understand and
transcribe it, the process is long and difficult.

The transcriptions of the ATC recordings were therefore done by two
former air traffic controllers from the Dallas/Fort Worth area who had
spent many years working in the DFW ATC system.  They were experienced
in transcribing ATC traffic for legal and governmental purposes, such
as investigation of accidents and incidents, planning and revision of
local ATC systems, etc.  Such transcripts are designed for human
reading, and normally follow Federal Aviation Administration (FAA)
practices, which constitute a _de facto_ standard in this area.

In addition to errors which would not necessarily need correction in a
document used for legal or investigative purposes, such as spelling
mistakes, the original transcriptions had a number of inconsistencies
and arbitrary usages: hesitation sounds (spelled ah, uh, eh, ahh),
attempts to represent pronunciation (climbin', awright, 'kay), and a
variety of terms to denote problems ("unintelligible," "sounds like,"
"blocked transmission," etc.).

The FAA format was therefore unsatisfactory for electronic processing
of the text, and a set of conventions was established in cooperation
with BBN, which was the first intended consumer of the data.  These
conventions were developed over a period of several months during the
pilot phase of collection.  Some of them were then imposed on the
transcribers, while others were produced algorithmically from the
transcripts using awk scripts or macros during the process of review
and quality control at TI.

BBN requested that each transcript be in the form of a Lisp list with
four kinds of objects: a header, a tail, stand-alone comments, and
transmissions.  Transmissions are also grouped into dialogs bounded by
extra newlines for human readability, but this is not part of the
specification and not guaranteed to be consistent.  

The specification calls for every transmission to contain:

1. the party transmitting, preceded by FROM, 

2. the party addressed, preceded by TO, 

3. the text of the transmission, preceded by TEXT, 

4. the start and end times of the transmission in seconds, preceded by
TIMES, and

5. optionally, comments from transcribers or others who reviewed the
transcripts, preceded by COMMENT and enclosed in quotation marks.

Stand-alone comments, which refer to events or things not associated
with one particular transmission, are structured like the
transmission-internal COMMENT (5. above), but set off as parenthesized
Lisp objects at the same level as transmissions.  The internal
contents of COMMENT, TAPE-HEADER, and TAPE-TAIL, are informational
text strings, otherwise unspecified in format, intended mainly for
human reading.

The TEXT contains transcribed words in upper case with no punctuation
other than possessive apostrophes, and with certain reserved
expressions permitted in parentheses, such as SHORT PAUSE, LONG PAUSE,
UNINTELLIGIBLE.  

The following passage contains examples of all these kinds of objects,
including both transmission-internal and stand-alone comments:

((TAPE-HEADER "DFW ATC FEEDER EAST, 119.5 MHZ, 1-7-91, 1550 CST"))

((FROM  AAL586)
(TO FE-1 )
(TEXT   AND AMERICAN FIVE EIGHTY SIX IS WITH YOU AT AH ELEVEN)
(TIMES  4.69	7.80))
((FROM  FE-1)
(TO AAL586 )
(TEXT   CALLING APPROACH SAY AGAIN)

((FROM FE-1)
(TO TWA319)
(TEXT  T W A THREE NINETEEN DEPARTURE AT TWELVE O'CLOCK SEVEN MILES 
EASTBOUND CLIMBING TO ONE ZERO THOUSAND)
(TIMES 21.42 25.32))

((FROM FE-1)
(TO DAL265)
(TEXT  DELTA TWO SIXTY FIVE MAINTAIN SIX THOUSAND CONTACT APPROACH ON ONE ONE NINER POINT FOUR)
(TIMES 551.69 555.60))
((FROM DAL265)
(TO FE-1)
(TEXT  ONE NINETEEN FOUR DELTA)
(TIMES 555.81 557.96)
(COMMENT "SOUNDS LIKE SIXTEEN"))

((FROM FE-1)
(TO AAL633)
(TEXT  AMERICAN SIX THIRTY THREE HEAVY DESCEND AND MAINTAIN FIVE THOUSAND APPROACH NOW ONE ONE NINER POINT FOUR (LONG PAUSE) AMERICAN SIX THIRTY THREE HEAVY CONTACT APPROACH ONE ONE NINER POINT FOUR)
(TIMES 2429.33 2433.21))
((FROM AAL633)
(TO FE-1)
(TEXT  NINETEEN FOUR AMERICAN SIX THIRTY THREE HEAVY)
(TIMES 2435.83 2438.55))

((COMMENT "SOUNDS LIKE BACKGROUND CONVERSATION--COMING DOWN--AMERICAN NINE OH"))

((FROM FE-1)
(TO AAL383)
(TEXT  AMERICAN THREE EIGHTY THREE CONTACT APPROACH ONE ONE NINER POINT FOUR)
(TIMES 2526.45 2528.90))

((FROM UNK)
(TO UNK)
(TEXT (UNINTELLIGIBLE))
(TIMES 2529.39 2530.23)
(COMMENT "SOUND OF INTERFERENCE"))

((FROM FE-1)
(TO N51HC)
(TEXT  CITATION FIVE ZERO ONE HOTEL CHARLIE REGIONAL APPROACH ROGER VECTORS LOVE)
(TIMES 2530.42 2533.32)
(COMMENT "CONTROLLER APPEARS TO MISSTATE CALL SIGN -JJG"))
((FROM N51HC)
(TO FE-1)
(TEXT  RIGHT ON)
(TIMES 2534.02 2534.48))

((TAPE-TAIL "END OF TAPE"))

There were also conventions established for flight identification
numbers and a number of other ATC-related phenomena such as the names
of intersections.  Some of the technical terms for DFW are given by
way of illustration in Attachment B, "Abbreviations Used in
Transcriptions," prepared by one of the ATC consultants.  Similar
material for other airports can be obtained from the FAA.



6.  The Dallas-Fort Worth International Airport (DFW) Corpus

The DFW data is contained in 24 .wav files, each approximately one
hour long, and 24 corresponding .txt files of transcripts.  The data
was collected over a period of about a year (March 1990 to February
1991) from several locations on or near the airport grounds.  

EQUIPMENT.  The DFW recordings in the first three sessions were made
using a discone antenna, a four-way splitter, up to four scanner
receivers, two stereo digitizers, and two video cassette recorders
(VCRs).  For the last two sessions, Sony TC75ES Digital Audio Tape
Recorders (DATs) were substituted for the digitizers and VCRs.  See
the description in Attachment A.

PROCESSING.  The data in the first three sessions was collected
digitally on VCR tapes.  It was later converted to computer files by
playing back the analog version, resampling with a DSC converter and
low-pass filtering with a Vax 780.  The DAT recordings from the other
two sessions were processed by filtering and downsampling with a
PC-based DAT interface in the Consumer Products speech processing
laboratory.  Since the sampling rates of the DATs (48 kHz) and the VCR
digitizer (44.1 kHz) are both so high, any differences in the DFW
dataset due to processing should be minimal.



LOCATIONS. A diagram of the airport appears in Figure 6. (Figures are 
located in the image directory.)

The DFW data was collected in six sessions, from guest
rooms in three different hotels in the vicinity of the airport.  The
"Tape Header" item at the beginning of each transcript gives the date
and time of recording.  The recording session dates and locations
were:

1 -- 03/01/90  Hyatt E (E side), antenna on roof
2 -- 03/28/90  Hilton (SW side), antenna inside
3 -- 05/18/90  Hyatt W (W side), antenna inside
4 -- 05/19/90  Hyatt W, antenna inside
5 -- 01/07/91  Hyatt E, antenna inside
6 -- 02/13/91  Hyatt E, antenna inside

The Hyatt East and West are twin buildings actually both on the airport
grounds, less than a quarter mile from the control tower, and fronting the two
principal runway complexes on either side of the airport.  The Hilton is
approximately two miles north of the tower, directly under approaching aircraft
in a south flow.  In the following schematic layout, the runways are labeled
for a north flow; in a south flow, runways 36 Left and 36 Right (facing 360
degrees, due north) become 18 Right and 18 Left respectively (180 degrees, due
south), while 35R becomes 17L, 35L becomes 17R; 31L and 31R become 13R and 13L.



                               N 
                               o ^
                               r |
                               t |
                               h 


              Hi








               ||        ||
       \       ||        || \
        \      ||        ||  \          Hi = Hilton
         \     || HW  HW ||   \     HE, HW = Hyatt E & W
          \    ||   o    ||    \         | = Runways
           \   ||        ||     \        o = Control Tower
            \  ||        ||      \
          31L\ ||        ||        31R 
               ||        ||
               ||        ||    
            36L||36R  35L||35R





PROCEDURE.  During the first recording session, the concern was to get
a strong enough signal from aircraft which could be as far as 25 miles
away.  The antenna was placed on the hotel rooftop, and an amplifier
was inserted before the splitter to compensate for losses due to the
long antenna cable and four-way division of the signal.  However, a
review of the data showed that episodes of interference from other
signals, probably not ATC, were the principal problem, and that
sensitivity was more than adequate -- airplanes on Feeder East as far
as 25 or 30 miles away seemed quite audible.

Engineers from the TI Antenna Group were then asked to characterize
the entire receiving setup, including the antenna, splitter,
connectors, and cables.  Their report, which runs to about 100 pages
including charts and tables, concludes that problems with out-of-band
signals are inevitable because of the broad frequency range of the
multiband scanner-receivers.  As many as 25 harmonics within the ATC
band could be detected from a digital pager signal broadcast from the
Hyatt hotel roof, for example.  On the other hand, they conclude that
sensitivity is sufficient for aircraft signals up to 20 miles away,
even through buildings, and that therefore an indoor placement of the
antenna, e.g., at a window with line of sight to most of the traffic,
might make the interference problem less severe by attenuating
undesired signals, especially distortion products from out-of-band
transmissions. 

This procedure was therefore followed for all the remaining sessions:
recording equipment was set up in a room on or near the top floor,
with one or more windows facing the general direction of the majority
of the expected traffic.  The antenna was set up in the room near the
window and connected to the splitter directly without an amplifier.

Of the eight hours collected in the first session (antenna outside,
amplifier in line), the four hours from the west side, which contained
many more incidents of interference, were discarded, and the four from
the east side, which had fewer, were retained.

The ATC functions recorded at DFW were Feeder, Arrival, Local, Ground,
and Departure.  DFW operates in some respects almost as two separate
airports, symmetrical about a north-south dividing line, with the
principal traffic flow being either to the south or to the north,
depending on prevailing weather patterns.  Thus "Feeder East" and
"Feeder West", "Arrival Radar One (East)" and "Arrival Radar Two
(West)", "Local Control East" and "Local Control West", "Ground
Control East" and "Ground Control West" are nearly mirror image
functions when both sides of the airport are active.

This symmetry is not complete; in addition to the principal
north-south runways, which are called 17 and 18 in a south flow, 35
and 36 in a north flow, there are two others flanking these, called 13
and 31, which are used during very busy periods for either arrivals or
departures.  Control of this traffic falls mainly to one or the other
of the sides.  Nevertheless, it seemed advisable to collect in roughly
equal proportion from both sides of these "symmetrical" functions in
order to get data representative of the airport as a whole.  The
vocabulary associated with each side, for example, will contain
different navigational fixes, runways, and even airline names.

Departure radar (DR) control is still less symmetrical.  There are
three DR positions which may be active in any combination, with DR1
tending to handle aircraft departing on the east side (which are often
also eastbound) and DR3 those on the west, and DR2 (on the few
occasions when all three are used) handling traffic from either runway
which is neither eastbound nor westbound.  But Departure positions are
often combined so as to occupy only one controller, or a controller is
added for brief peak periods, so it is difficult to collect long
stretches with a single controller and dense traffic.  All three
departure positions are represented in the corpus.



TABLE OF CONTENTS.

The following table shows the DFW data arranged according to major
external factors--locations, recording sessions (with equipment and
location fixed), and ATC positions.  On the right, the ATC positions
are grouped at two levels: the nearly-identical East and West pairs
and the three Departures (explained above) at one level, then the
Feeder and Arrival functions, which are both "arrival" positions in a
broader sense, but are split at DFW and a few other airports.  All
recordings are approximately one hour in duration.

SESSIONS /  1    2    3    4    5    5    5    6   / hours/function
=============================================================
      FE  | XX |    |    |    | XX |    |    |    |
      ----|----|----|----|----|----|----|----|----|> 5 Feeder \
      FW  |    | XX |    | XX |    |    | XX |    |            \
      ----|----|----|----|----|----|----|----|----|-------      > 10 Arrival
      AR1 | XX |    |    |    | XX |    |    |    |            /
A     ----|----|----|----|----|----|----|----|----|> 5 Arrival/
      AR2 |    | XX |    |    |    |    | XX | XX |  
T     ----|----|----|----|----|----|----|----|----|----------
      LCE | XX |    |    |    |    | XX |    |    |
C     ----|----|----|----|----|----|----|----|----|> 5 Local
      LCW |    | XX | XX | XX |    |    |    |    |
      ----|----|----|----|----|----|----|----|----|----------
S     GCE | XX |    |    |    |    |	|    |    |	 
T     ----|----|----|----|----|----|----|----|----|> 3 Ground
A     GCW |    | XX | XX |    |    |    |    |    | 
T     ----|----|----|----|----|----|----|----|----|----------
I     DR1 |    |    |    |    | XX | XX |    | XX |
O     ----|----|----|----|----|----|----|----|----|\
N     DR2 |    |    |    |    |    |    | XX |    | >6 Departure
S     ----|----|----|----|----|----|----|----|----|/
      DR3 |    |    | XX |    | XX |    |    |    |   
      ----|----|----|----|----|----|----|----|----|----------
Date        3/1 3/28 5/18 5/19  1/7  1/7  1/7 2/13
Start      1400 1345 1815 0930 1552 1705 1800 1030
- End     -1500 1445 1915 1030 1652 1755 1900 1220
Times       CST  CST  CDT  CDT  CST  CST  CST  CST

SESSION DATES & LOCATIONS: 
1 -- 03/01/90  Hyatt E, antenna on roof
2 -- 03/28/90  Hilton SW, antenna inside
3 -- 05/18/90  Hyatt W, antenna inside
4 -- 05/19/90  Hyatt W, antenna inside
5 -- 01/07/91  Hyatt E, antenna inside
6 -- 02/13/91  Hyatt E, antenna inside

ABBREVIATIONS:

 FE, FW: Feeder East and West.
 AR1, AR2: Approach control for principal E and W runways. 
 LCE, LCW: Local (Tower) Control for principal E and W runways.
 GCE, GCW: Ground Control for E and W sides, taxiways, terminals.
 DR1, DR2, DR3: Departure Control for traffic heading E, N/S, W. 





7.  The Logan International Airport (BOS) Corpus

The Logan data is contained in 11 .wav files, 11 corresponding .txt
files of transcripts, as well as another set of 11 .cdt files which
are described below.  As mentioned in Section 3 above, it differs from
the pilot data collected at DFW in a number of ways, some of them
significant and others not.

There were a number of changes in the collection methodology.  DFW was
a pilot project, and certain dimensions of ATC were explored there
which were not worth pursuing further.  For example, collection from
multiple ATC functions for the same flight during its landing or
takeoff, or recording of Ground Control or Enroute Sectors, were
judged less valuable than more hours of a few basic functions, such as
Tower, Arrival, and Departure.

Collection in one hour sessions was also criticized by the users of
the DFW data, for the following reason.  Whenever a recording session
ends, any flights still being worked on that frequency are, as it
were, "cut off" before they have communicated with the controller the
usual number of times; the fewer examples of a flight there are, the
more difficult it is to identify that flight by speech or voice
recognition.  There is a handful of these cut off flights, i.e.,
flights with fewer than normal transmissions, at the very beginning of
a recording session and a like number at the very end.  Since the
number is approximately a constant for a given frequency, at least
during busy times of day, longer recording sessions were requested so
as to reduce the relative effect of this truncated traffic.  The Logan
recordings were therefore generally longer, up to a limit of two
hours, the length of a DAT tape.  However, there were still sessions
where this length could not be justified: traffic might drop off on
one of the channels being collected on a DAT, frequencies might be
combined, etc., making it more sensible to stop and change stations
after one hour, or to trim off the leading or trailing parts of a
recording.

All the Logan data was collected in a period of two days, June 26 and
27, 1991.  A total of about 27 hours were recorded, of which nearly 20
were acceptable for final use.  Reasons for exclusion were: not enough
traffic, unacceptable noise or distortion on the recording, ATC
function not sufficiently well represented overall.  

EQUIPMENT.  The BOS recordings were made using the same discone
antenna, and two of the four scanner receivers used at DFW.  These had
been specially modified to provide a second output signal, in addition
to the audio.  The reason for the modification was a change in the
specifications of some contractual work being performed by BBN using
the ATC data.  This change required that BBN use the radio carrier
signal as well as the audio.  Circuitry was added to the receivers at
Rome Laboratories to detect the amplitude of the carrier signal being
received and to use it to control a voltage controlled oscillator.
The oscillators were chosen so that their lowest frequency, emitted
when no carrier was detected, was between 8 and 10 kHz, and their
highest frequency, emitted when the carrier signal was at maximum
amplitude, was between 20 and 22 kHz.  Table 1 indicates the power and
frequency relationships for two of the receivers.  For a given ATC
frequency, both the audio signal and the carrier-detect FM tone were
recorded on one track of a Sony TC75ES Digital Audio Tape Recorder
(DAT).  Thus two frequencies could be recorded at the same time, using
two radios and one DAT.


Power-Frequency Relationship of Carrier Detect Signal for Two
Receivers:

	Attenuation:  0 dB		no modulation
	Frequency:    118.5 MHz   	Type - AM


	  SN 827062  		       	  SN 803676
          ---------                       ---------
  Antenna Power   Frequency       Antenna Power   Frequency

       1 uV       8.970 KHz            1 uV       9.657 KHz
       3 uV       9.500 KHz            3 uV      10.939 KHz
     .01 mV      10.141 KHz          .01 mV      12.370 KHz
     .03 mV      10.712 KHz          .03 mV      13.262 KHz
     0.1 mV      11.180 KHz          0.3 mV      13.312 KHz
     0.3 mV      11.543 KHz            1 mV      13.373 KHz
       3 mV      11.593 KHz            3 mV      13.748 KHz
      10 mV      11.630 KHz           10 mV      14.491 KHz
 

                            TABLE 1


PROCESSING.  By common agreement the DAT recordings were copied and
sent for processing to BBN, since they were to use the new signal
format in their research.  The processing involved detecting the FM
tone and recording its frequency into a 100 Hz, 32 bit computer file,
as well as filtering and downsampling the audio to an 8 kHz, 16-bit
computer file. 

LOCATION. A diagram of the airport is given in Figure 7.  (Figures are 
located in the image directory.)

The BOS data was collected from a fifth floor room in the
Hilton Hotel just outside the airport terminal.  The window and
balcony of the room overlooked the tower and runway complex, which
were less than half a mile distant.  The antenna was placed on a small
balcony outdoors, with about 2 meters of coax cable leading to a "Y"
connector and thence to the two radios.  The recording conditions were
thus quite similar to those at DFW.

PROCEDURE.  The ATC functions at Logan are as follows:

Final Approach (F1), comparable to the AR1 and AR2 positions at
DFW, controls final approach to a few miles from the runway.

Initial Departure (ID), comparable to the DR1, DR2 and DR3
positions at DFW, controls departures from a few miles off the runway
through an altitude of about ten thousand feet.

Local East (LE) and Local West (LW) are the tower positions; however,
they are significantly different from DFW in that they may, for long
periods, handle only landings or only takeoffs.  The amount of
traffic, the allocation of traffic between the shorter and the longer
runways, and between the parallel and intersecting runways, and other
factors affect this division of labor between LE and LW.  For the
corpus we chose two recordings of LW, one two hours long and one an
hour long.  During both periods, LW was mainly controlling takeoffs on
Runway 22 Right; however, during part of the second session Runway 22
Left is closed for inspection and LW controls landings as well as
takeoffs.

Lincoln (SL), Plymouth (SM), and Rockport (SR) are called "Transition"
positions.  They combine the functions of Feeder and Departure at DFW,
in the sense that they control both arriving and departing traffic in
the area.  They handle arrivals before they reach F1, and departures
after they leave ID.  Which one(s) of the three Transition controllers
are on the air depends in part on the traffic pattern in effect.  On
the two days of recording, with a predominately southwest flow, the
Plymouth Transition (SM) was most active.  The other two positions
were either not on the air or handled much less traffic.


TABLE OF CONTENTS.  

This table shows the tape identifier, ATC function, number of minutes,
and the approximate number of distinct flights and transmissions, for
each of the 11 Logan files.


Tape ID | ATC Pos | Mins |#Flights |#Transmissions 
--------|---------|------|---------|--------------
log_f1_1| F1      |  120 |  75     |  1028  
--------|---------|------|---------|--------------
log_f1_2| F1      |  120 |  73     |  1084
--------|---------|------|---------|--------------
log_id_1| ID      |  120 |  88     |   704    
--------|---------|------|---------|--------------
log_lw_1| LW      |  120 | 173     |   851
--------|---------|------|---------|--------------
log_sm_1| SM      |  120 |  69     |   693 
--------|---------|------|---------|--------------
log_id_2| ID      |  100 |  81     |   602 
--------|---------|------|---------|--------------
log_f1_3| F1      |  120 |  82     |   948 
--------|---------|------|---------|--------------
log_sm_2| SM      |  120 |  65     |   697 
--------|---------|------|---------|--------------
log_lw_2| LW      |   60 |  80     |   434    
--------|---------|------|---------|--------------
log_id_3| ID      |   64 |  43     |   266 
--------|---------|------|---------|--------------
log_f1_4| F1      |  101 |  71     |   969 
--------|---------|------|---------|--------------

KEY TO POSITIONS:   

F1:  Final Approach
ID:  Initial Departure
LW:  Local West
SM:  Plymouth Transition




8.  The Washington National Airport (DCA) Corpus
 
The DCA data is contained in 17 .wav files, 17 corresponding .txt
files of transcripts, and 17 .cdt files with carrier frequency
information.  The data was collected over a period of three days, May
26-28,1992, from a single location in northern Virginia.

EQUIPMENT.  The DCA recordings were made with a different radio
receiver and antenna than the other two datasets, although a version
from one of the same RS2005 receivers was also recorded.  

Although it was never the purpose of this project to obtain "optimal"
voice recordings, experience with the data from DFW and Logan, advice
from the TI Antenna Group engineers, and comparisons with FAA
recordings, led us to explore alternatives to the broadband
scanner-receivers originally recommended.  Our suspicion was that the
extremely wide receptive band featured by these radios, though it
provides easy access to many communications functions at a reasonable
price, might be allowing unwanted signals to mix at some stage with
the ATC audio.  Some pilot recordings (not included in this corpus)
were made at DFW with a single antenna feeding both a RS2005 and a
receiver designed to admit only frequencies in the ATC range
(approximately 118 to 132 MHz).  These recordings, made in parallel
with the output of the RS2005 scanning receivers, proved that a very
common source of interfering noise in the recordings from the RS2005s
was the reception of signals from outside the ATC band, including
harmonics of such carriers as digital pagers and FM radio broadcasts.
This led to the choice of an ATC receiver for the last corpus.

The radio chosen was a Bendix-King Model KY-97A, commonly used in
small aircraft.  An antenna designed for use in ATC communications was
also used, a portable omnidirectional VHF Model AV-1 from Antenna
Specialists.  The antenna output was split and sent to both a RS
scanner receiver and the BK Model KY-97A. 

Monitoring of the audio during the recording sessions confirmed that
the BK audio suffered significantly less interference from unwanted
signals than the RS.  In fact, due to an apparently powerful and leaky
broadcasting antenna nearby, there was one ATC frequency (119.85)
which could almost never be understood through the RS receiver, but
remained free of interference through the BK.

The receiver outputs were passed through the same mixer as at Logan,
except that the second receiver (the BK) did not have a carrier
detection signal mixed with its audio.  Thus the RS2005 carrier
signal and audio were mixed and recorded together on one track of
the DAT (the same Sony TC75ES used in the other two airports), and the
BK audio alone was recorded on the other.  In this way, comparisons
could be made between the two receiver audio signals, while either one
could be combined with the carrier signal without loss of
time registration (see below).  For the published LDC corpus, however, 
the signals chosen were the BK recording and the carrier detection
signal, reduced in a manner similar to the Logan data, as described 
below.


PROCESSING.  As with the Logan data, the DAT recordings were copied
and sent to BBN for extraction of 8 kHz .wav computer files, to insure
that the filtering and format would be identical.

Recovery of the carrier-detect signal was done at NIST, using the
identical software as that used at BBN and, as at BBN, using a
Silicon Graphics Indigo workstation to read the DATs.

For the type of DATs used, there is not a unique zero point.  Therefore,
there was a time offset between the BK audio and the carrier signal
recovered at NIST.  The Sony audio was also recovered at NIST.  By
comparing it with the BK audio, the time offset was determined.  Samples
were either deleted or added at the beginning of the carrier detect files
so that they were in time alignment with the BK signal.  The added samples
are all zeroes.  Zeroes were also added at the end, if necessary, to make
the time durations of the carrier files approximately equal to those of 
the BK files.  Users should be aware of this possible presence of zero
values.  Where speech occurs at the very beginning of a file, an initial
segment included in the BK file may have zero values in the carrier file.


LOCATION. A diagram of the airport is given in Figure 8.  (Figures are 
located in the image directory.)

The DCA data was collected over a three day period from the
computer room on the tenth floor of the ten-story ARPA headquarters
building at 3701 Wilson Blvd.  in Arlington.  The antenna was placed
on the rooftop, and since less than 30 feet of BNC cable was required
to reach the receivers in the computer room, no amplification was
used.

The ARPA building is almost directly north and slightly west of the
DCA airport, approximately 3 miles from the end of the main runway.
The runways in use during a north flow, which prevailed for the three
days of recording, are 3, 33, and 36, so all departing flights pass
within a few miles of the building on takeoff.  Arriving flights
approach from the other side of the airport, but many of them first
make the downwind leg of their approach directly to the west of this
point.


PROCEDURE.  Only three ATC functions were recorded at National
Airport, though two of them had East and West positions:

Final One (F1) and Final Two (F2), comparable to the AR1 and AR2
positions at DFW, control final approach to a few miles from the
runway, depending on whether the traffic was approaching from the West
(F1) or the East (F2).

Departure Low West (DR1) and Departure Low East (DR2), comparable to
the DR1, DR2 and DR3 positions at DFW, control departures from a few
miles off the runway through an altitude of about ten thousand feet.

Local  (LCL) is the tower position, handling both takeoffs and
landings on two or three runways at once.

As with the Logan airport data, an attempt was made to record up to
two hours at a time; shorter sessions are due to lack of traffic, or
the need to switch to another frequency for a known period of busy
traffic.  Jim Owens, consultant to the project, had determined the
"rush" and "push" times for DCA traffic in advance from FAA personnel
at the airport.

The following table contains the same information as the Logan table:
tape identifier, ATC station, length of recording, approximate number
of distinct aircraft, number of distinct transmissions.




TABLE OF CONTENTS
         
ATC at Washington National Airport (DCA)


Tape ID | ATC Pos | Mins |# Flts|# Transmissions
--------|---------|------|------|---------------
dca_f1_1| F1      |  56  |   26 |   443
--------|---------|------|------|---------------
dca_d1_1| DR1     |  90  |   38 |   396
--------|---------|------|------|---------------
dca_lc_1| LCL     | 100  |  137 |  1093
--------|---------|------|------|---------------
dca_f1_2| F1      | 120  |   29 |   485
--------|---------|------|------|---------------
dca_lc_2| LCL     | 120  |  142 |  1167
--------|---------|------|------|---------------
dca_f2_1| F2      |  60  |   24 |   383
--------|---------|------|------|---------------  
dca_lc_3| LCL     |  60  |   48 |   358
--------|---------|------|------|---------------
dca_d1_2| DR1     |  70  |   33 |   313
--------|---------|------|------|---------------
dca_d2_1| DR2     |  60  |   33 |   274
--------|---------|------|------|---------------
dca_lc_4| LCL     |  56  |   81 |   535
--------|---------|------|------|---------------
dca_f2_2| F2      |  60  |   38 |   445
--------|---------|------|------|---------------
dca_lc_5| LCL     | 120  |  118 |   939
--------|---------|------|------|---------------
dca_d2_2| DR2     |  61  |   30 |   329
--------|---------|------|------|---------------
dca_d1_3| DR1     | 120  |   50 |   539
--------|---------|------|------|---------------
dca_f2_3| F2      | 120  |   52 |   610
--------|---------|------|------|---------------
dca_d1_4| DR1     | 120  |   60 |   537
--------|---------|------|------|---------------
dca_lc_6| LCL     | 120  |  119 |   928
--------|-----|------|------|---------------

KEY TO POSITIONS:    

F1:  Feeder & Final One (West) -- 119.85 MHz
F2:  Feeder & Final Two (East) -- 124.20 MHz

DR1: Departure One Low (West)  -- 118.95 MHz
DR2: Departure Two Low (East)  -- 126.55 MHz

LCL: Local (Tower)	       -- 119.10 MHz



		ATTACHMENT A: Equipment list

Receiver/Antenna combinations:

Radio Shack Model Pro 2005 Scanner/Receivers (4)
Radio Shack Discone Antenna, Cat. No. 20-013

Bendix/King Model KY197A Aircraft Radio
Antenna Specialists Model AV-1 VHF antenna


VCR-based Recording systems (2 x 2-channel):

Panasonic A100 Video Tape Recorder
Panasonic AG-6300 Video Tape Recorder
Nakamichi DMP-100 Digital Mastering Processors (2)


DAT Recording systems:

Sony DTC-75ES Digital Audio Tape Recorder (2)


Mixer (used with modified 2005 receivers):

TASCAM M-18 Mixer





		ATTACHMENT B: Abbreviations used in DFW transcripts

The following are lists of abbreviations common in FAA terminology.
They are taken from sources for the DFW ATC system.  By understanding
how these flight IDs, military designators, intersection names, and
other terms are used at DFW, one can readily identify and understand
how the corresponding terms are used at Logan and National Airports as
well, even without knowing the exact referents of each.

In addition to the air carrier designators, which form part of the
flight IDs used in the transcripts, also listed are navigation aids,
including their names and three letter designators, intersections
along airways based on the navigation aids, Standard Terminal Arrival
Routes (STARS) and intersections designated on these routes and
intersections on the Instrument Landing Systems (ILS) serving D F W
airport.

These aids, intersections, and routings are frequently referred to in
Air Traffic communications by the D F W ATCT facility.

1.  AIR CARRIER 3 LETTER IDENTIFIERS

Three letter air carrier company designators are assigned to all air
carriers by the F A A using ICAO standards. When used in conjunction
with the flight number they serve as the aircraft identifications in
Air Traffic Communications.

3-LETTER DESIGNATOR	COMPANY				CALL SIGN
-------------------     -------                         ---------
AAL (+ flight number)	AMERICAN AIRLINES		AMERICAN
COA			CONTINENTAL AIRLINES		CONTINENTAL
DAL			DELTA AIRLINES			DELTA
EAL			EASTERN AIRLINES		EASTERN
PAA			PAN AMERICAN WORLD AIRWAYS	CLIPPER
MTR			METRO FLIGHT INC.		METRO
ASA			ATLANTIC SOUTHEAST AIRLINES	ASEA
CPL			CHAPARRAL AIRLINES		CHAPARRAL
BAW			BRITISH AIRWAYS			SPEEDBIRD
UAL			UNITED AIRLINES			UNITED
TWA			TRANS WORLD AIRLINES		T W A
MEP			MIDWEST EXPRESS			MIDEX
MID			MIDWAY AIRLINES			MIDWAY
MXA			MEXICANA AIRLINES		MEXICANA
UPS			UNITED PARCEL SERVICE		UPSCO
FDX			FEDERAL EXPRESS CORPORATION	EXPRESS
MSE			MESA AVIATION SERVICES		AIR SHUTTLE
EEC			EXEC EXPRESS			HUSTLER
TAC			THAI AIRLINES			THAI-AIR
DLH			LUFTHANSA			LUFTHANSA
AWE			AMERICAN WEST AIRLINES		CACTUS
NWA			NORTHWEST AIRLINES		NORTHWEST
SWA			SOUTHWEST AIRLINES		SOUTHWEST

2.  GENERAL AVIATION IDENTIFIERS

Aircraft are limited to a total of 7 alpha/numeric characters in the
aircraft registration.  In flight planning, Air Traffic Communications
and automation data the letter N precedes the registration number to
designate general aviation aircraft.

	EXAMPLE:  N12345B

For brevity the caller/called section of the transcription should be
reduced to N followed by the last 3 characters.

	EXAMPLE:  N45B (UNLESS THERE ARE NOT 3 CHARACTERS).
		  Radio call for this aircraft would be November 45
		  Bravo, or the type aircraft may by substituted for 
		  the word November, e.g. Cessna 45 Bravo.

The minimum number of alpha/numeric characters is 2.

	EXAMPLE:  N1

In event the aircraft is either an Air Taxi or Lifeguard flight it
would be identified as follows:

	AIR TAXI:  TN45B Radio call would be Tango November 45 Bravo

	LIFEGUARD: LN45B Radio call would be Lima November 45 Bravo 


3.  MILITARY SERVICE DESIGNATORS

Military aircraft are identified by a service designator followed by
the aircraft's serial number.

DESIGNATOR		SERVICE		CALL SIGN/DESIGNATOR EXAMPLE
----------              -------         ----------------------------
     A			AIR FORCE	A123456
     VV			NAVY		VV3456
     VM			MARINE		etc.	
     R			ARMY
     C			COAST GUARD
     G			AIR OR ARMY NATIONAL GUARD



Other military aircraft use "tactical" call signs followed by numbers
for A T C communications and flight plan information.

EXAMPLE:  SPADE 42


4.  NAVIGATION AIDS

The following navigation aids are frequently referred to in Air Traffic
Communications.

VORTAC: V H F omni directional aid with distance measuring capability.
Navigation aids are normally named after geographical locations near the
facility, for example the BRIDGEPORT VORTAC is located near Bridgeport,
Texas.

The three letter identifiers assigned to these facilities are provided
by computer and are issued on a system wide basis to ensure that no two
have the same identifier.

VORTAC NAME/3-LETTER IDENTIFIER
-------------------------------
BRIDGEPORT/BPR
BLUE RIDGE/BUJ
SCURRY/SCY
ACTON/AQN
MILLSAP/MQP
WACO/ACT
ARDMORE/ADM

5.  INTERSECTIONS

Intersections are designated along airways formed by radials from
VORTACS and are used for position determination and Air Traffic
Control separation purposes.  Intersections are assigned 5 letter
designators by computer and are also issued system wide to ensure no
duplication or confusion. In some instances the designators for
intersections are named in correlation to geographical points.
EXAMPLE: CELIN is near the town of Celina, Texas.

Intersections on Airway V66-278 between Bridgeport and Blue Ridge
VORTACS, in sequence from west to east:

MYGAL	JACKY	KORKS	CELIN	KMART

Intersection on Airway V15 between Blue Ridge and Scurry VORTACs.

	HUBBA

Intersections on Airway V16-94 between Scurry and Acton VORTACs, from
east to west:

ELLMO	RAINY	BRITY	KEEN	MANDY

Intersection on Airway V17-163 between Scurry and Bridgeport VORTACs:

	BEGGO


6.  INTERSECTIONS ON STANDARD TERMINAL ARRIVAL ROUTES (STARS)

STARS serve as arrival routes into the DFW terminal area and are used
for flight planning purposes and ATC clearances.  Intersections on
these routes are designated by 5 letter identifiers in the same manner
as other intersections.

STAR NAME             PRIMARY NAVIGATION AID  RADIAL  INTERSECTIONS ON ROUTE
---------	      ----------------------  -----   ----------------------

BOIDS 1 ARRIVAL       BRIDGEPORT VORTAC       BPR 108   RHOME
                                                        BOIDS
                                                        PIVIT
                                                        ARINA

                      BRIDGEPORT VORTAC       BPR 115   CEVEE
                                                        JURRO
                                                        JUSTY

HEAVN 3 ARRIVAL       BRIDGEPORT VORTAC       BPR 078   HEAVN
                                                        MYGAL
                                                        CELIN

BLUE RIDGE 2 ARRIVAL  BLUE RIDGE VORTAC       BUJ 230   BRAID
                                                        BATON
                                                        ALKID
                                                        HAMAK

                                              BUJ 215   DEANZ
                                                        HOLTS
                                                        WEDER

SCURRY 9 ARRIVAL      SCURRY VORTAC           SCY 313   BECKX
                                                        HERBO
                                                        CAVEN

                                              SCY 296	PORKS
                                                        SEAGO
                                                        GLADD
                                                        REFIL


ACTON 1 ARRIVAL       ACTON VORTAC            AQN 040   MARKM
                                                        BRYAR
                                                        HULEN
                                                        FLATO
                                                        CREEK

                                              AQN 033   JERRY
                                                        CRESN
                                                        RENDY

BOIDS 1 ARRIVAL       BRIDGEPORT VORTAC       BPR 108   RHOME
                                                        BOIDS
                                                        PIVIT
                                                        ARINA

                                              BPR 115   CEVEE
                                                        JURRO
                                                        JUSTY

HEAVN 3 ARRIVAL       BRIDGEPORT VORTAC       BPR 078	HEAVN
                                                        MYGAL
                                                        CELIN

BLUE RIDGE 2 ARRIVAL  BLUE RIDGE VORTAC       BUJ 230   BRAID
                                                        BATON
                                                        ALKID
                                                        HAMAK

                                              BUJ 215   DEANZ
                                                        HOLTS
                                                        WEDER

SCURRY 9 ARRIVAL      SCURRY VORTAC           SCY 313 	BECKX
                                                        HERBO
                                                        CAVEN

                                              SCY 296   PORKS
                                                        SEAGO
                                                        GLADD
                                                        REFIL

ACTON 1 ARRIVAL       ACTON VORTAC            AQN 040 	MARKM
                                                        BRYAR
                                                        HULEN
                                                        FLATO
                                                        CREEK

                                              AQN 033   JERRY
                                                        CRESN
                                                        RENDY



7.  INTERSECTIONS AND FINAL APPROACH FIXES ON I L S SYSTEMS

ILS is an acronym for Instrument Landing System.

RUNWAYS:      18 RIGHT    18 LEFT    17 LEFT    17 RIGHT    13 LEFT
              --------    -------    -------    --------    ------- 
INTERSECTIONS:  YOHAN	    ALIGN       PENNY      GARZA
                LEGRE       UDALL       ZINGG      YALTA

OUTER MARKERS:  HASTY       HASTY       JIFFY      JIFFY      GUUDE


RUNWAYS:      36 LEFT     35 RIGHT   31 RIGHT
              -------     --------   -------
INTERSECTIONS:  CHARR       DAYZZ       VANDE
                HUTEN       TUFFO       GACHO

OUTER MARKERS:  BASIN       ISSUE       RIVER


8.  STANDARD INSTRUMENT DEPARTURES (SIDS)

SIDS are used by DFW, but since they are basically radar vector
procedures to join a navigational radial, generally they are not
called out by name.  They are normally referred to by instructions for
an aircraft to "JOIN THE SID".