PILOT/CONTROLLER GLOSSARY

	This glossary was compiled to promote a common understanding
of the terms used in the Air Traffic Control system. It includes those
terms which are intended for pilot/controller communications. Those
terms most frequently used in pilot/controller communications are
printed in bold italics. The definitions are primarily defined in an
operational sense applicable to both users and operators of the
National Airspace System. Use of the glossary will preclude any
misunderstandings concerning the system's design, function, and
purpose.
	Because of the international nature of flying, terms used in
the Lexicon, published by the International Civil Aviation
Organization (ICAO), are included when they differ from FAA
definitions. These terms are followed by ``[ICAO]''. For the reader's
convenience, there are also cross references to related terms in other
parts of the Glossary and to other documents, such as the Federal
Aviation Regulations (FAR's) and the Airman's Information Manual
(AIM).
	This glossary was compiled from electronic data made available
by the FAA.  It will be revised, as necessary, to maintain a common
understanding of the system. 

AAI
(See ARRIVAL AIRCRAFT INTERVAL).

AAR
(See AIRPORT ACCEPTANCE RATE).

ABBREVIATED IFR FLIGHT PLANS 
An authorization by ATC requiring pilots
to submit only that information needed for the purpose of ATC. It
includes only a small portion of the usual IFR flight plan
information. In certain instances, this may be only aircraft
identification, location, and pilot request. Other information may be
requested if needed by ATC for separation/control purposes. It is
frequently used by aircraft which are airborne and desire an
instrument approach or by aircraft which are on the ground and desire
a climb to VFR on top.

ABEAM 
An aircraft is ``abeam'' a fix, point, or object when that fix,
point, or object is approximately 90 degrees to the right or left of
the aircraft track. Abeam indicates a general position rather than a
precise point.

ABORT
To terminate a preplanned aircraft maneuver; e.g., an aborted takeoff.

ACC [ICAO]
(See AREA CONTROL CENTER).

ACCELERATE-STOP DISTANCE AVAILABLE
 The runway plus stopway length declared available and suitable for the
acceleration and deceleration of an airplane aborting a takeoff

ACCELERATE-STOP DISTANCE AVAILABLE [ICAO]
The length of the take-off run available plus the length of the
stopway if provided.

ACDO
(See AIR CARRIER DISTRICT OFFICE).

ACKNOWLEDGE
Let me know that you have received my message.

ACKNOWLEDGE [ICAO]
Let me know that you have received and understood this message.

ACLS
(See AUTOMATIC CARRIER LANDING SYSTEM).

ACLT
(See ACTUAL CALCULATED LANDING TIME).

ACROBATIC FLIGHT 
An intentional maneuver involving an abrupt change in
an aircraft's attitude, an abnormal attitude, or abnormal acceleration
not necessary for normal flight.

ACROBATIC FLIGHT [ICAO] 
Manoeuvres intentionally performed by an
aircraft involving an abrupt change in its attitude, an abnormal
attitude, or an abnormal variation in speed.

ACTIVE RUNWAY
(See RUNWAY IN USE/ACTIVE RUNWAY/DUTY RUNWAY).

ACTUAL CALCULATED LANDING TIME 
ACLT is a flight's frozen calculated
landing time. An actual time determined at freeze calculated landing
time (FCLT) or meter list display interval (MLDI) for the adapted
vertex for each arrival aircraft based upon runway configuration,
airport acceptance rate, airport arrival delay period, and other
metered arrival aircraft. This time is either the vertex time of
arrival (VTA) of the aircraft or the tentative calculated landing time
(TCLT)/ACLT of the previous aircraft plus the arrival aircraft
interval (AAI), whichever is later. This time will not be updated in
response to the aircraft's progress.

ADDITIONAL SERVICES 
Advisory information provided by ATC which
includes but is not limited to the following: Traffic advisories.
Vectors, when requested by the pilot, to assist aircraft receiving
traffic advisories to avoid observed traffic.  Altitude deviation
information of 300 feet or more from an assigned altitude as observed
on a verified (reading correctly) automatic altitude readout (Mode C).
Advisories that traffic is no longer a factor.  Weather and chaff
information.  Weather assistance.  Bird activity information.  Holding
pattern surveillance. Additional services are provided to the extent
possible contingent only upon the controller's capability to fit them
into the performance of higher priority duties and on the basis of
limitations of the radar, volume of traffic, frequency congestion, and
controller workload. The controller has complete discretion for
determining if he is able to provide or continue to provide a service
in a particular case. The controller's reason not to provide or
continue to provide a service in a particular case is not subject to
question by the pilot and need not be made known to him.

ADF
(See AUTOMATIC DIRECTION FINDER).

ADIZ
(See AIR DEFENSE IDENTIFICATION ZONE).

ADLY
(See ARRIVAL DELAY).

ADMINISTRATOR 
The Federal Aviation Administrator or any person to whom
he has delegated his authority in the matter concerned.

ADVISE INTENTIONS
Tell me what you plan to do.

ADVISORY 
Advice and information provided to assist pilots in the safe
conduct of flight and aircraft movement.

ADVISORY FREQUENCY 
The appropriate frequency to be used for Airport Advisory Service.

ADVISORY SERVICE 
Advice and information provided by a facility to assist pilots in the
safe conduct of flight and aircraft movement.

AERIAL REFUELING
A procedure used by the military to transfer fuel from one aircraft to
another during flight.

AERODROME
A defined area on land or water (including any buildings,
installations and equipment) intended to be used either wholly or in
part for the arrival, departure, and movement of aircraft.

AERODROME BEACON [ICAO]
Aeronautical beacon used to indicate the location of an aerodrome from
the air.

AERODROME CONTROL SERVICE [ICAO]
Air traffic control service for aerodrome traffic.

AERODROME CONTROL TOWER [ICAO]
A unit established to provide air traffic control service to aerodrome
traffic.

AERODROME ELEVATION [ICAO]
The elevation of the highest point of the landing area.

AERODROME TRAFFIC CIRCUIT [ICAO]
The specified path to be flown by aircraft operating in the vicinity
of an aerodrome.

AERONAUTICAL BEACON
A visual NAVAID displaying flashes of white and/or colored light to
indicate the location of an airport, a heliport, a landmark, a certain
point of a Federal airway in mountainous terrain, or an obstruction.

AERONAUTICAL CHART
A map used in air navigation containing all or part of the following:
Topographic features, hazards and obstructions, navigation aids,
navigation routes, designated airspace, and airports. Commonly used
aeronautical charts are: Sectional Aeronautical Charts
(1:500,000). Designed for visual navigation of slow or medium speed
aircraft. Topographic information on these charts features the
portrayal of relief and a judicious selection of visual check points
for VFR flight. Aeronautical information includes visual and radio
aids to navigation, airports, controlled airspace, restricted areas,
obstructions, and related data.  VFR Terminal Area Charts
(1:250,000). Depict Class B airspace which provides for the control or
segregation of all the aircraft within Class B airspace. The chart
depicts topographic information and aeronautical information which
includes visual and radio aids to navigation, airports, controlled
airspace, restricted areas, obstructions, and related data.  World
Aeronautical Charts (WAC) (1:1,000,000). Provide a standard series of
aeronautical charts covering land areas of the world at a size and
scale convenient for navigation by moderate speed
aircraft. Topographic information includes cities and towns, principal
roads, railroads, distinctive landmarks, drainage, and
relief. Aeronautical information includes visual and radio aids to
navigation, airports, airways, restricted areas, obstructions, and
other pertinent data.  En Route Low Altitude Charts. Provide
aeronautical information for en route instrument navigation (IFR) in
the low altitude stratum. Information includes the portrayal of
airways, limits of controlled airspace, position identification and
frequencies of radio aids, selected airports, minimum en route and
minimum obstruction clearance altitudes, airway distances, reporting
points, restricted areas, and related data. Area charts, which are a
part of this series, furnish terminal data at a larger scale in
congested areas.  En Route High Altitude Charts. Provide aeronautical
information for en route instrument navigation (IFR) in the high
altitude stratum. Information includes the portrayal of jet routes,
identification and frequencies of radio aids, selected airports,
distances, time zones, special use airspace, and related information.
Instrument Approach Procedures (IAP) Charts. Portray the aeronautical
data which is required to execute an instrument approach to an
airport. These charts depict the procedures, including all related
data, and the airport diagram. Each procedure is designated for use
with a specific type of electronic navigation system including NDB,
TACAN, VOR, ILS/MLS, and RNAV. These charts are identified by the type
of navigational aid(s) which provide final approach guidance.
Standard Instrument Departure (SID) Charts. Designed to expedite
clearance delivery and to facilitate transition between takeoff and en
route operations. Each SID procedure is presented as a separate chart
and may serve a single airport or more than one airport in a given
geographical location.  Standard Terminal Arrival (STAR)
Charts. Designed to expedite air traffic control arrival procedures
and to facilitate transition between en route and instrument approach
operations. Each STAR procedure is presented as a separate chart and
may serve a single airport or more than one airport in a given
geographical location.  Airport Taxi Charts. Designed to expedite the
efficient and safe flow of ground traffic at an airport. These charts
are identified by the official airport name; e.g., Washington National
Airport.

AERONAUTICAL CHART [ICAO]
A representation of a portion of the earth, its culture and relief,
specifically designated to meet the requirements of air navigation.

AERONAUTICAL INFORMATION PUBLICATION [AIP] [ICAO]
A publication issued by or with the authority of a State and
containing aeronautical information of a lasting character essential
to air navigation.

A/FD
(See AIRPORT/FACILITY DIRECTORY).

AFFIRMATIVE
Yes.

AIM
(See AIRMAN'S INFORMATION MANUAL).

AIP [ICAO]
(See AERONAUTICAL INFORMATION PUBLICATION).

AIRBORNE DELAY
Amount of delay to be encountered in airborne holding.

AIR CARRIER DISTRICT OFFICE
An FAA field office serving an assigned geographical area, staffed
with Flight Standards personnel serving the aviation industry and the
general public on matters related to the certification and operation
of scheduled air carriers and other large aircraft operations.

AIRCRAFT
Device(s) that are used or intended to be used for flight in the air,
and when used in air traffic control terminology, may include the
flight crew.

AIRCRAFT [ICAO]
Any machine that can derive support in the atmosphere from the
reactions of the air other than the reactions of the air against the
earth's surface.

AIRCRAFT APPROACH CATEGORY
A grouping of aircraft based on a speed of 1.3 times the stall speed
in the landing configuration at maximum gross landing weight. An
aircraft shall fit in only one category. If it is necessary to
maneuver at speeds in excess of the upper limit of a speed range for a
category, the minimums for the next higher category should be
used. For example, an aircraft which falls in Category A, but is
circling to land at a speed in excess of 91 knots, should use the
approach Category B minimums when circling to land. The categories are
as follows: 
Category A. Speed less than 91 knots. 
Category B. Speed 91 knots or more but less than 121 knots.  
Category C. Speed 121 knots or more but less than 141 knots.  
Category D. Speed 141 knots or more but less than 166 knots.  
Category E. Speed 166 knots or more.

AIRCRAFT CLASSES
For the purposes of Wake Turbulence Separation Minima, ATC classifies
aircraft as Heavy, Large, and Small as follows: Heavy. Aircraft
capable of takeoff weights of 300,000 pounds or more whether or not
they are operating at this weight during a particular phase of flight.
Large. Aircraft of more than 12,500 pounds, maximum certificated
takeoff weight, up to 300,000 pounds.  Small. Aircraft of 12,500
pounds or less maximum certificated takeoff weight.

AIRCRAFT SITUATION DISPLAY
ASD is a computer system that receives radar track data from all 20
CONUS ARTCC's, organizes this data into a mosaic display, and presents
it on a computer screen. The display allows the traffic management
coordinator multiple methods of selection and high lighting of
individual aircraft or groups of aircraft. The user has the option of
superimposing these aircraft positions over any number of background
displays. These background options include ARTCC boundaries, any
stratum of en route sector boundaries, fixes, airways, military and
other special use airspace, airports, and geopolitical boundaries. By
using the ASD, a coordinator can monitor any number of traffic
situations or the entire systemwide traffic flows.

AIRCRAFT SURGE LAUNCH AND RECOVERY
Procedures used at USAF bases to provide increased launch and recovery
rates in instrument flight rules conditions.  ASLAR is based on:
Reduced separation between aircraft which is based on time or
distance.  Standard arrival separation applies between participants
including multiple flights until the DRAG point.  The DRAG point is a
published location on an ASLAR approach where aircraft landing second
in a formation slows to a predetermined airspeed.  The DRAG point is
the reference point at which MARSA applies as expanding elements
effect separation within a flight or between subsequent participating
flights.  ASLAR procedures shall be covered in a Letter of Agreement
between the responsible USAF military ATC facility and the concerned
Federal Aviation Administration facility.  Initial Approach Fix
spacing requirements are normally addressed as a minimum.

AIR DEFENSE EMERGENCY
A military emergency condition declared by a designated
authority. This condition exists when an attack upon the continental
U.S., Alaska, Canada, or U.S. installations in Greenland by hostile
aircraft or missiles is considered probable, is imminent, or is taking
place.

AIR DEFENSE IDENTIFICATION ZONE
The area of airspace over land or water, extending upward from the
surface, within which the ready identification, the location, and the
control of aircraft are required in the interest of national security.
Domestic Air Defense Identification Zone. An ADIZ within the United
States along an international boundary of the United States.  Coastal
Air Defense Identification Zone. An ADIZ over the coastal waters of
the United States.  Distant Early Warning Identification Zone
(DEWIZ). An ADIZ over the coastal waters of the State of Alaska.

AIRMAN'S INFORMATION MANUAL
A primary FAA publication whose purpose is to instruct airmen about
operating in the National Airspace System of the U.S. It provides
basic flight information, ATC Procedures and general instructional
information concerning health, medical facts, factors affecting flight
safety, accident and hazard reporting, and types of aeronautical
charts and their use.

AIRMAN'S METEOROLOGICAL INFORMATION
(See AIRMET).

AIRMET
In flight weather advisories issued only to amend the area forecast
concerning weather phenomena which are of operational interest to all
aircraft and potentially hazardous to aircraft having limited
capability because of lack of equipment, instrumentation, or pilot
qualifications. AIRMET's concern weather of less severity than that
covered by SIGMET's or Convective SIGMET's. AIRMET's cover moderate
icing, moderate turbulence, sustained winds of 30 knots or more at the
surface, widespread areas of ceilings less than 1,000 feet and/or
visibility less than 3 miles, and extensive mountain obscurement.

AIR NAVIGATION FACILITY
Any facility used in, available for use in, or designed for use in,
aid of air navigation, including landing areas, lights, any apparatus
or equipment for disseminating weather information, for signaling, for
radio directional finding, or for radio or other electrical
communication, and any other structure or mechanism having a similar
purpose for guiding or controlling flight in the air or the landing
and take off of aircraft.

AIRPORT
An area on land or water that is used or intended to be used for the
landing and takeoff of aircraft and includes its buildings and
facilities, if any.

AIRPORT ACCEPTANCE RATE
A dynamic input parameter specifying the number of arriving aircraft
which an airport or airspace can accept from the ARTCC per hour. The
AAR is used to calculate the desired interval between successive
arrival aircraft.

AIRPORT ADVISORY AREA
The area within ten miles of an airport without a control tower or
where the tower is not in operation, and on which a Flight Service
Station is located.

AIRPORT ELEVATION
The highest point of an airport's usable runways measured in feet from
mean sea level.

AIRPORT/FACILITY DIRECTORY
A publication designed primarily as a pilot's operational manual
containing all airports, seaplane bases, and heliports open to the
public including communications data, navigational facilities, and
certain special notices and procedures. This publication is issued in
seven volumes according to geographical area.

AIRPORT INFORMATION AID
(See AIRPORT INFORMATION DESK).

AIRPORT INFORMATION DESK
An airport unmanned facility designed for pilot self service briefing,
flight planning, and filing of flight plans.

AIRPORT LIGHTING
Various lighting aids that may be installed on an airport. Types of
airport lighting include: Approach Light System (ALS). An airport
lighting facility which provides visual guidance to landing aircraft
by radiating light beams in a directional pattern by which the pilot
aligns the aircraft with the extended centerline of the runway on his
final approach for landing. Condenser Discharge Sequential Flashing
Lights/Sequenced Flashing Lights may be installed in conjunction with
the ALS at some airports. Types of Approach Light Systems are:
ALSF-1. Approach Light System with Sequenced Flashing Lights in ILS
Cat I configuration.  ALSF-2. Approach Light System with Sequenced
Flashing Lights in ILS Cat II configuration. The ALSF-2 may operate as
an SSALR when weather conditions permit.  SSALF. Simplified Short
Approach Light System with Sequenced Flashing Lights.
SSALR. Simplified Short Approach Light System with Runway Alignment
Indicator Lights.  MALSF. Medium Intensity Approach Light System with
Sequenced Flashing Lights.  MALSR. Medium Intensity Approach Light
System with Runway Alignment Indicator Lights.  LDIN. Lead in light
system: Consists of one or more series of flashing lights installed at
or near ground level that provides positive visual guidance along an
approach path, either curving or straight, where special problems
exist with hazardous terrain, obstructions, or noise abatement
procedures.  RAIL. Runway Alignment Indicator Lights (Sequenced
Flashing Lights which are installed only in combination with other
light systems).  ODALS. Omnidirectional Approach Lighting System
consists of seven omnidirectional flashing lights located in the
approach area of a nonprecision runway. Five lights are located on the
runway centerline extended with the first light located 300 feet from
the threshold and extending at equal intervals up to 1,500 feet from
the threshold. The other two lights are located, one on each side of
the runway threshold, at a lateral distance of 40 feet from the runway
edge, or 75 feet from the runway edge when installed on a runway
equipped with a VASI.  Runway Lights/Runway Edge Lights. Lights having
a prescribed angle of emission used to define the lateral limits of a
runway. Runway lights are uniformly spaced at intervals of
approximately 200 feet, and the intensity may be controlled or preset.
Touchdown Zone Lighting. Two rows of tranverse light bars located
symmetrically about the runway centerline normally at 100 foot
intervals. The basic system extends 3,000 feet along the runway.
Runway Centerline Lighting. Flush centerline lights spaced at 50-foot
intervals beginning 75 feet from the landing threshold and extending
to within 75 feet of the opposite end of the runway.  Threshold
Lights. Fixed green lights arranged symmetrically left and right of
the runway centerline, identifying the runway threshold.  Runway End
Identifier Lights (REIL). Two synchronized flashing lights, one on
each side of the runway threshold, which provide rapid and positive
identification of the approach end of a particular runway.  Visual
Approach Slope Indicator (VASI). An airport lighting facility
providing vertical visual approach slope guidance to aircraft during
approach to landing by radiating a directional pattern of high
intensity red and white focused light beams which indicate to the
pilot that he is ``on path'' if he sees red/white, ``above path` if
white/white, and ``below path'' if red/red. Some airports serving
large aircraft have three bar VASIs which provide two visual glide
paths to the same runway.  Boundary Lights. Lights defining the
perimeter of an airport or landing area.

AIRPORT MARKING AIDS
Markings used on runway and taxiway surfaces to identify a specific
runway, a runway threshold, a centerline, a hold line, etc. A runway
should be marked in accordance with its present usage such as: Visual.
Nonprecision instrument.  Precision instrument.

AIRPORT RESERVATION OFFICE
Office responsible for monitoring the operation of the high density
rule. Receives and processes requests for IFR operations at high
density traffic airports.

AIRPORT ROTATING BEACON
A visual NAVAID operated at many airports. At civil airports,
alternating white and green flashes indicate the location of the
airport. At military airports, the beacons flash alternately white and
green, but are differentiated from civil beacons by dualpeaked (two
quick) white flashes between the green flashes.

AIRPORT SURFACE DETECTION EQUIPMENT
Radar equipment specifically designed to detect all principal features
on the surface of an airport, including aircraft and vehicular
traffic, and to present the entire image on a radar indicator console
in the control tower. Used to augment visual observation by tower
personnel of aircraft and/or vehicular movements on runways and
taxiways.

AIRPORT SURVEILLANCE RADAR
Approach control radar used to detect and display an aircraft's
position in the terminal area. ASR provides range and azimuth
information but does not provide elevation data. Coverage of the ASR
can extend up to 60 miles.

AIRPORT TAXI CHARTS
(See AERONAUTICAL CHART).

AIRPORT TRAFFIC CONTROL SERVICE
A service provided by a control tower for aircraft operating on the
movement area and in the vicinity of an airport.

AIRPORT TRAFFIC CONTROL TOWER
(See TOWER).

AIR ROUTE SURVEILLANCE RADAR
Air route traffic control center (ARTCC) radar used primarily to
detect and display an aircraft's position while en route between
terminal areas. The ARSR enables controllers to provide radar air
traffic control service when aircraft are within the ARSR coverage. In
some instances, ARSR may enable an ARTCC to provide terminal radar
services similar to but usually more limited than those provided by a
radar approach control.

AIR ROUTE TRAFFIC CONTROL CENTER
A facility established to provide air traffic control service to
aircraft operating on IFR flight plans within controlled airspace and
principally during the en route phase of flight. When equipment
capabilities and controller workload permit, certain
advisory/assistance services may be provided to VFR aircraft.

AIRSPACE HIERARCHY
Within the airspace classes, there is a heirarchy and, in the event of
an overlap of airspace: Class A preempts Class B, Class B preempts
Class C, Class C preempts Class D, Class D preempts Class E, and Class
E preempts Class G.

AIRSPEED
The speed of an aircraft relative to its surrounding air mass. The
unqualified term ``airspeed` means one of the following: Indicated
Airspeed. The speed shown on the aircraft airspeed indicator. This is
the speed used in pilot/controller communications under the general
term ``airspeed.''  True Airspeed. The airspeed of an aircraft
relative to undisturbed air. Used primarily in flight planning and en
route portion of flight. When used in pilot/controller communications,
it is referred to as ``true airspeed'' and not shortened to
``airspeed.''

AIRSTART
The starting of an aircraft engine while the aircraft is airborne,
preceded by engine shutdown during training flights or by actual
engine failure.

AIR TAXI
Used to describe a helicopter/VTOL aircraft movement conducted above
the surface but normally not above 100 feet AGL. The aircraft may
proceed either via hover taxi or flight at speeds more than 20
knots. The pilot is solely responsible for selecting a safe
airspeed/altitude for the operation being conducted.

AIR TRAFFIC
Aircraft operating in the air or on an airport surface, exclusive of
loading ramps and parking areas.

AIR TRAFFIC [ICAO]
All aircraft in flight or operating on the manoeuvring area of an
aerodrome.

AIR TRAFFIC CLEARANCE
An authorization by air traffic control, for the purpose of preventing
collision between known aircraft, for an aircraft to proceed under
specified traffic conditions within controlled airspace. The
pilot-in-command of an aircraft may not deviate from the provisions of
a visual flight rules (VFR) or instrument flight rules (IFR) air
traffic clearance unless an amended clearance has been obtained.
Additionally, the pilot may request a different clearance from that
which has been issued by air traffic control (ATC) if information
available to the pilot makes another course of action more practicable
or if aircraft equipment limitations or company procedures forbid
compliance with the clearance issued.  Pilots may also request
clarification or amendment, as appropriate, any time a clearance is
not fully understood, or considered unacceptable because of safety of
flight.  Controllers should, in such instances and to the extent of
operational practicality and safety, honor the pilot's request.

AIR TRAFFIC CONTROL
A service operated by appropriate authority to promote the safe,
orderly and expeditious flow of air traffic.

AIR TRAFFIC CONTROL CLEARANCE [ICAO]
Authorization for an aircraft to proceed under conditions specified by
an air traffic control unit.

AIR TRAFFIC CONTROL SERVICE
(See AIR TRAFFIC CONTROL).

AIR TRAFFIC CONTROL SERVICE [ICAO]
A service provided for the purpose of:
Preventing collisions:
Between aircraft; and
On the maneuvering area between aircraft and obstructions; and
Expediting and maintaining an orderly flow of air traffic.

AIR TRAFFIC CONTROL SPECIALIST
A person authorized to provide air traffic control service.

AIR TRAFFIC CONTROL SYSTEM COMMAND CENTER
An Air Traffic Operations Service facility consisting of four
operational units.  Central Flow Control Function (CFCF). Responsible
for coordination and approval of all major intercenter flow control
restrictions on a system basis in order to obtain maximum utilization
of the airspace.  Central Altitude Reservation Function
(CARF). Responsible for coordinating, planning, and approving special
user requirements under the Altitude Reservation (ALTRV) concept.
Airport Reservation Office (ARO). Responsible for approving IFR
flights at designated high density traffic airports (John F. Kennedy,
LaGuardia, O'Hare, and Washington National) during specified hours.
ATC Contingency Command Post. A facility which enables the FAA to
manage the ATC system when significant portions of the system's
capabilities have been lost or are threatened.

AIR TRAFFIC SERVICE
A generic term meaning:
Flight Information Service:
Alerting Service:
Air Traffic Advisory Service:
Air Traffic Control Service:
Area Control Service,
Approach Control Service, or
Airport Control Service.

AIRWAY
A Class E airspace area established in the form of a corridor, the
centerline of which is defined by radio navigational aids.

AIRWAY [ICAO]
A control area or portion thereof established in the form of corridor
equipped with radio navigational aids.

AIRWAY BEACON
Used to mark airway segments in remote mountain areas. The light
flashes Morse Code to identify the beacon site.  AIT (See AUTOMATED
INFORMATION TRANSFER).

ALERFA (Alert Phase) [ICAO]
A situation wherein apprehension exists as to the safety of an
aircraft and its occupants.

ALERT AREA
(See SPECIAL USE AIRSPACE).

ALERT NOTICE
A request originated by a flight service station (FSS) or an air route
traffic control center (ARTCC) for an extensive communication search
for overdue, unreported, or missing aircraft.

ALERTING SERVICE
A service provided to notify appropriate organizations regarding
aircraft in need of search and rescue aid and assist such
organizations as required.  ALNOT (See ALERT NOTICE).

ALPHANUMERIC DISPLAY
Letters and numerals used to show identification, altitude, beacon
code, and other information concerning a target on a radar display.

ALTERNATE AERODROME [ICAO]
An aerodrome to which an aircraft may proceed when it becomes either
impossible or inadvisable to proceed to or to land at the aerodrome of
intended landing.

ALTERNATE AIRPORT
An airport at which an aircraft may land if a landing at the intended
airport becomes inadvisable.

ALTIMETER SETTING
The barometric pressure reading used to adjust a pressure altimeter
for variations in existing atmospheric pressure or to the standard
altimeter setting (29.92).

ALTITUDE
The height of a level, point, or object measured in feet Above Ground
Level (AGL) or from Mean Sea Level (MSL).  MSL Altitude. Altitude
expressed in feet measured from mean sea level.  AGL
Altitude. Altitude expressed in feet measured above ground level.
Indicated Altitude. The altitude as shown by an altimeter. On a
pressure or barometric altimeter it is altitude as shown uncorrected
for instrument error and uncompensated for variation from standard
atmospheric conditions.

ALTITUDE [ICAO]
The vertical distance of a level, a point or an object considered as a
point, measured from mean sea level (MSL).

ALTITUDE READOUT
An aircraft's altitude, transmitted via the Mode C transponder
feature, that is visually displayed in 100-foot increments on a radar
scope having readout capability.

ALTITUDE RESERVATION
Airspace utilization under prescribed conditions normally employed for
the mass movement of aircraft or other special user requirements which
cannot otherwise be accomplished. ALTRVs are approved by the
appropriate FAA facility.

ALTITUDE RESTRICTION
An altitude or altitudes, stated in the order flown, which are to be
maintained until reaching a specific point or time. Altitude
restrictions may be issued by ATC due to traffic, terrain, or other
airspace considerations.

ALTITUDE RESTRICTIONS ARE CANCELED
Adherence to previously imposed altitude restrictions is no longer
required during a climb or descent.

ALTRV
(See ALTITUDE RESERVATION).

AMVER
(See AUTOMATED MUTUAL-ASSISTANCE VESSEL RESCUE SYSTEM

APPROACH CLEARANCE
Authorization by ATC for a pilot to conduct an instrument
approach. The type of instrument approach for which a clearance and
other pertinent information is provided in the approach clearance when
required.

APPROACH CONTROL FACILITY
A terminal ATC facility that provides approach control service in a
terminal area.

APPROACH CONTROL SERVICE
Air traffic control service provided by an approach control facility
for arriving and departing VFR/IFR aircraft and, on occasion, en route
aircraft. At some airports not served by an approach control facility,
the ARTCC provides limited approach control service.

APPROACH CONTROL SERVICE [ICAO]
Air traffic control service for arriving or departing controlled
flights.

APPROACH GATE
An imaginary point used within ATC as a basis for vectoring aircraft
to the final approach course. The gate will be established along the
final approach course 1 mile from the outer marker (or the fix used in
lieu of the outer marker) on the side away from the airport for
precision approaches and 1 mile from the final approach fix on the
side away from the airport for nonprecision approaches. In either case
when measured along the final approach course, the gate will be no
closer than 5 miles from the landing threshold.

APPROACH LIGHT SYSTEM
(See AIRPORT LIGHTING).

APPROACH SEQUENCE
The order in which aircraft are positioned while on approach or
awaiting approach clearance.

APPROACH SEQUENCE [ICAO]
The order in which two or more aircraft are cleared to approach to
land at the aerodrome.

APPROACH SPEED
The recommended speed contained in aircraft manuals used by pilots
when making an approach to landing. This speed will vary for different
segments of an approach as well as for aircraft weight and
configuration.

APPROPRIATE ATS AUTHORITY [ICAO]
The relevant authority designated by the State responsible for
providing air traffic services in the airspace concerned. In the
United States, the ``appropriate ATS authority'' is the Director,
Office of Air Traffic System Management, ATM-1.

APPROPRIATE AUTHORITY
Regarding flight over the high seas: the relevant authority is the
State of Registry.  Regarding flight over other than the high seas:
the relevant authority is the State having sovereignty over the
territory being overflown.

APPROPRIATE OBSTACLE CLEARANCE MINIMUM ALTITUDE
Any of the following:
(See Minimum IFR Altitude)
(See Minimum En Route Altitude)
(See Minimum Obstruction Clearance Altitude)
(See Minimum Vectoring Altitude)

APPROPRIATE TERRAIN CLEARANCE MINIMUM ALTITUDE
Any of the following: 
(See Minimum IFR Altitude)
(See Minimum En Route Altitude)
(See Minimum Obstruction Clearance Altitude)
(See Minimum Vectoring Altitude) 

APRON
A defined area on an airport or heliport intended to accommodate
aircraft for purposes of loading or unloading passengers or cargo,
refueling, parking, or maintenance. With regard to seaplanes, a ramp
is used for access to the apron from the water.

APRON [ICAO]
A defined area, on a land aerodrome, intended to accommodate aircraft
for purposes of loading or unloading passengers, mail or cargo,
refuelling, parking or maintenance.

ARC
The track over the ground of an aircraft flying at a constant distance
from a navigational aid by reference to distance measuring equipment
(DME).

AREA CONTROL CENTER [ICAO]
An ICAO term for an air traffic control facility primarily responsible
for ATC services being provided IFR aircraft during the en route phase
of flight. The U.S. equivalent facility is an air route traffic
control center (ARTCC).

AREA NAVIGATION
A method of navigation that permits aircraft operation on any desired
course within the coverage of station referenced navigation signals or
within the limits of a self contained system capability. Random area
navigation routes are direct routes, based on area navigation
capability, between waypoints defined in terms of latitude/longitude
coordinates, degree/distance fixes, or offsets from published or
established routes/airways at a specified distance and direction. The
major types of equipment are: VORTAC referenced or Course Line
Computer (CLC) systems, which account for the greatest number of RNAV
units in use. To function, the CLC must be within the service range of
a VORTAC.  OMEGA/VLF, although two separate systems, can be considered
as one operationally. A long range navigation system based upon Very
Low Frequency radio signals transmitted from a total of 17 stations
worldwide.  Inertial (INS) systems, which are totally self contained
and require no information from external references. They provide
aircraft position and navigation information in response to signals
resulting from inertial effects on components within the system.  MLS
Area Navigation (MLS/RNAV), which provides area navigation with
reference to an MLS ground facility.  LORAN C is a long range radio
navigation system that uses ground waves transmitted at low frequency
to provide user position information at ranges of up to 600 to 1,200
nautical miles at both en route and approach altitudes. The usable
signal coverage areas are determined by the signal to noise ratio, the
envelope to cycle difference, and the geometric relationship between
the positions of the user and the transmitting stations.

AREA NAVIGATION [ICAO] 
A method of navigation which permits aircraft operation on any desired
flight path within the coverage of station referenced navigation aids
or within the limits of the capability of self contained aids, or a
combination of these.

ARINC
An acronym for Aeronautical Radio, Inc., a corporation largely owned
by a group of airlines. ARINC is licensed by the FCC as an
aeronautical station and contracted by the FAA to provide
communications support for air traffic control and meteorological
services in portions of international airspace.

ARMY AVIATION FLIGHT INFORMATION BULLETIN
A bulletin that provides air operation data covering Army, National
Guard, and Army Reserve aviation activities.

ARO
(See AIRPORT RESERVATION OFFICE).

ARRESTING SYSTEM
A safety device consisting of two major components, namely, engaging
or catching devices and energy absorption devices for the purpose of
arresting both tailhook and/or nontailhook equipped aircraft. It is
used to prevent aircraft from overrunning runways when the aircraft
cannot be stopped after landing or during aborted takeoff. Arresting
systems have various names; e.g., arresting gear, hook device, wire
barrier cable.

ARRIVAL AIRCRAFT INTERVAL
An internally generated program in hundredths of minutes based upon
the AAR. AAI is the desired optimum interval between successive
arrival aircraft over the vertex.

ARRIVAL CENTER
The ARTCC having jurisdiction for the impacted airport.

ARRIVAL DELAY
A parameter which specifies a period of time in which no aircraft will
be metered for arrival at the specified airport.

ARRIVAL SECTOR
An operational control sector containing one or more meter fixes.

ARRIVAL SECTOR ADVISORY LIST
An ordered list of data on arrivals displayed at the PVD of the sector
which controls the meter fix.

ARRIVAL SEQUENCING PROGRAM
The automated program designed to assist in sequencing aircraft
destined for the same airport.

ARRIVAL TIME
The time an aircraft touches down on arrival.

ARSR
(See AIR ROUTE SURVEILLANCE RADAR).

ARTCC
(See AIR ROUTE TRAFFIC CONTROL CENTER).

ARTS
(See AUTOMATED RADAR TERMINAL SYSTEMS).

ASD
(See AIRCRAFT SITUATION DISPLAY).

ASDA
(See ACCELERATE-STOP DISTANCE AVAILABLE).

ASDA [ICAO]
(See ICAO Term ACCELERATE-STOP DISTANCE AVAILABLE).

ASDE
(See AIRPORT SURFACE DETECTION EQUIPMENT).

ASLAR
(See AIRCRAFT SURGE LAUNCH AND RECOVERY).

ASP
(See ARRIVAL SEQUENCING PROGRAM).

ASR
(See AIRPORT SURVEILLANCE RADAR).

ASR APPROACH
(See SURVEILLANCE APPROACH).

ATC
(See AIR TRAFFIC CONTROL).

ATCAA
(See ATC ASSIGNED AIRSPACE).

ATC ADVISES
Used to prefix a message of noncontrol information when it is relayed
to an aircraft by other than an air traffic controller.

ATC ASSIGNED AIRSPACE
Airspace of defined vertical/lateral limits, assigned by ATC, for the
purpose of providing air traffic segregation between the specified
activities being conducted within the assigned airspace and other IFR
air traffic.

ATC CLEARANCE
(See AIR TRAFFIC CLEARANCE).

ATC CLEARS
Used to prefix an ATC clearance when it is relayed to an aircraft by
other than an air traffic controller.

ATC INSTRUCTIONS
Directives issued by air traffic control for the purpose of requiring
a pilot to take specific actions; e.g., ``Turn left heading two five
zero,'' ``Go around,'' ``Clear the runway.''

ATCRBS
(See RADAR).

ATC REQUESTS
Used to prefix an ATC request when it is relayed to an aircraft by
other than an air traffic controller.

ATCSCC
(See AIR TRAFFIC CONTROL SYSTEM COMMAND CENTER).

ATCSCC DELAY FACTOR
The amount of delay calculated to be assigned prior to departure.

ATCT
(See TOWER).

ATIS
(See AUTOMATIC TERMINAL INFORMATION SERVICE).

ATIS [ICAO]
(See ICAO Term AUTOMATIC TERMINAL INFORMATION SERVICE).

ATS Route [ICAO]
A specified route designed for channelling the flow of traffic as
necessary for the provision of air traffic services.

AUTOLAND APPROACH
An autoland approach is a precision instrument approach to touchdown
and, in some cases, through the landing rollout. An autoland approach
is performed by the aircraft autopilot which is receiving position
information and/or steering commands from onboard navigation equipment

AUTOMATED INFORMATION TRANSFER
A precoordinated process, specifically defined in facility directives,
during which a transfer of altitude control and/or radar
identification is accomplished without verbal coordination between
controllers using information communicated in a full data block.

AUTOMATED MUTUAL-ASSISTANCE VESSEL RESCUE SYSTEM
A facility which can deliver, in a matter of minutes, a surface
picture (SURPIC) of vessels in the area of a potential or actual
search and rescue incident, including their predicted positions and
their characteristics.

AUTOMATED RADAR TERMINAL SYSTEMS

The generic term for the ultimate in functional capability afforded by
several automation systems. Each differs in functional capabilities
and equipment. ARTS plus a suffix roman numeral denotes a specific
system. A following letter indicates a major modification to that
system. In general, an ARTS displays for the terminal controller
aircraft identification, flight plan data, other flight associated
information; e.g., altitude, speed, and aircraft position symbols in
conjunction with his radar presentation. Normal radar co exists with
the alphanumeric display. In addition to enhancing visualization of
the air traffic situation, ARTS facilitate intra/inter facility
transfer and coordination of flight information. These capabilities
are enabled by specially designed computers and subsystems tailored to
the radar and communications equipments and operational requirements
of each automated facility. Modular design permits adoption of
improvements in computer software and electronic technologies as they
become available while retaining the characteristics unique to each
system.  ARTS II. A programmable nontracking, computer aided display
subsystem capable of modular expansion. ARTS II systems provide a
level of automated air traffic control capability at terminals having
low to medium activity. Flight identification and altitude may be
associated with the display of secondary radar targets. The system has
the capability of communicating with ARTCC's and other ATRS II, IIA,
III, and IIIA facilities.  ARTS IIA. A programmable radar tracking
computer subsystem capable of modular expansion. The ARTS IIA detects,
tracks, and predicts secondary radar targets. The targets are
displayed by means of computer generated symbols, ground speed, and
flight plan data. Although it does not track primary radar targets,
they are displayed coincident with the secondary radar as well as the
symbols and alphanumerics. The system has the capability of
communicating with ARTCC's and other ARTS II, IIA, III, and IIIA
facilities.  ARTS III. The Beacon Tracking Level of the modular
programmable automated radar terminal system in use at medium to high
activity terminals. ARTS III detects, tracks, and predicts secondary
radar derived aircraft targets. These are displayed by means of
computer generated symbols and alphanumeric characters depicting
flight identification, aircraft altitude, ground speed, and flight
plan data. Although it does not track primary targets, they are
displayed coincident with the secondary radar as well as the symbols
and alphanumerics. The system has the capability of communicating with
ARTCC's and other ARTS III facilities.  ARTS IIIA. The Radar Tracking
and Beacon Tracking Level (RT&BTL) of the modular, programmable
automated radar terminal system. ARTS IIIA detects, tracks, and
predicts primary as well as secondary radar derived aircraft
targets. This more sophisticated computer driven system upgrades the
existing ARTS III system by providing improved tracking, continuous
data recording, and fail soft capabilities.

AUTOMATIC ALTITUDE REPORT
(See ALTITUDE READOUT).

AUTOMATIC ALTITUDE REPORTING
That function of a transponder which responds to Mode C interrogations
by transmitting the aircraft's altitude in 100-foot increments.

AUTOMATIC CARRIER LANDING SYSTEM
U.S. Navy final approach equipment consisting of precision tracking
radar coupled to a computer data link to provide continuous
information to the aircraft, monitoring capability to the pilot, and a
backup approach system.

AUTOMATIC DIRECTION FINDER
An aircraft radio navigation system which senses and indicates the
direction to a L/MF nondirectional radio beacon (NDB) ground
transmitter. Direction is indicated to the pilot as a magnetic bearing
or as a relative bearing to the longitudinal axis of the aircraft
depending on the type of indicator installed in the aircraft. In
certain applications, such as military, ADF operations may be based on
airborne and ground transmitters in the VHF/UHF frequency spectrum.

AUTOMATIC TERMINAL INFORMATION SERVICE
The continuous broadcast of recorded noncontrol information in
selected terminal areas. Its purpose is to improve controller
effectiveness and to relieve frequency congestion by automating the
repetitive transmission of essential but routine information; e.g.,
``Los Angeles information Alfa. One three zero zero Coordinated
Universal Time. Weather, measured ceiling two thousand overcast,
visibility three, haze, smoke, temperature seven one, dew point five
seven, wind two five zero at five, altimeter two niner niner six. I L
S Runway Two Five Left approach in use, Runway Two Five Right closed,
advise you have Alfa.''

AUTOMATIC TERMINAL INFORMATION SERVICE [ICAO]
The provision of current, routine information to arriving and
departing aircraft by means of continuous and repetitive broadcasts
throughout the day or a specified portion of the day.

AUTOROTATION
A rotorcraft flight condition in which the lifting rotor is driven
entirely by action of the air when the rotorcraft is in motion.
Autorotative Landing/Touchdown Autorotation. Used by a pilot to
indicate that he will be landing without applying power to the rotor.
Low Level Autorotation. Commences at an altitude well below the
traffic pattern, usually below 100 feet AGL and is used primarily for
tactical military training.  180 degrees Autorotation. Initiated from
a downwind heading and is commenced well inside the normal traffic
pattern. ``Go around'' may not be possible during the latter part of
this maneuver.

AVIATION WEATHER SERVICE
A service provided by the National Weather Service (NWS) and FAA which
collects and disseminates pertinent weather information for pilots,
aircraft operators, and ATC. Available aviation weather reports and
forecasts are displayed at each NWS office and FAA FSS.

AWW
(See SEVERE WEATHER FORECAST ALERTS).

AZIMUTH (MLS)
A magnetic bearing extending from an MLS navigation facility.

BASE LEG
(See TRAFFIC PATTERN).

BEACON
(See RADAR).

BEARING
The horizontal direction to or from any point, usually measured
clockwise from true north, magnetic north, or some other reference
point through 360 degrees.

BELOW MINIMUMS
Weather conditions below the minimums prescribed by regulation for the
particular action involved; e.g., landing minimums, takeoff minimums.

BLAST FENCE
A barrier that is used to divert or dissipate jet or propeller blast.

BLIND SPEED
The rate of departure or closing of a target relative to the radar
antenna at which cancellation of the primary radar target by moving
target indicator (MTI) circuits in the radar equipment causes a
reduction or complete loss of signal.

BLIND SPOT
An area from which radio transmissions and/or radar echoes cannot be
received. The term is also used to describe portions of the airport
not visible from the control tower.

BLIND TRANSMISSION
(See TRANSMITTING IN THE BLIND).

BLIND VELOCITY [ICAO]
The radial velocity of a moving target such that the target is not
seen on primary radars fitted with certain forms of fixed echo
suppression.

BLIND ZONE
(See BLIND SPOT).

BLOCKED
Phraseology used to indicate that a radio transmission has been
distorted or interrupted due to multiple simultaneous radio
transmissions.

BOUNDARY LIGHTS
(See AIRPORT LIGHTING).

BRAKING ACTION (GOOD, FAIR, POOR, OR NIL)
A report of conditions on the airport movement area providing a pilot
with a degree/quality of braking that he might expect. Braking action
is reported in terms of good, fair, poor, or nil.

BRAKING ACTION ADVISORIES
When tower controllers have received runway braking action reports
which include the terms ``poor'' or ``nil,'' or whenever weather
conditions are conducive to deteriorating or rapidly changing runway
braking conditions, the tower will include on the ATIS broadcast the
statement, ``BRAKING ACTION ADVISORIES ARE IN EFFECT.'' During the
time Braking Action Advisories are in effect, ATC will issue the
latest braking action report for the runway in use to each arriving
and departing aircraft. Pilots should be prepared for deteriorating
braking conditions and should request current runway condition
information if not volunteered by controllers. Pilots should also be
prepared to provide a descriptive runway condition report to
controllers after landing.

BROADCAST
Transmission of information for which an acknowledgement is not
expected.

BROADCAST [ICAO]
A transmission of information relating to air navigation that is not
addressed to a specific station or stations.

CALCULATED LANDING TIME
A term that may be used in place of tentative or actual calculated
landing time, whichever applies.

CALL UP
Initial voice contact between a facility and an aircraft, using the
identification of the unit being called and the unit initiating the
call.

CALL FOR RELEASE
Wherein the overlying ARTCC requires a terminal facility to initiate
verbal coordination to secure ARTCC approval for release of a
departure into the en route environment.

CANADIAN MINIMUM NAVIGATION PERFORMANCE SPECIFICATION AIRSPACE
That portion of Canadian domestic airspace within which MNPS
separation may be applied.

CARDINAL ALTITUDES
``Odd'' or ``Even'' thousand foot altitudes or flight levels; e.g.,
5,000, 6,000, 7,000, FL 250, FL 260, FL 270.

CARDINAL FLIGHT LEVELS
(See CARDINAL ALTITUDES).

CAT
(See CLEAR AIR TURBULENCE).

CDT PROGRAMS
(See CONTROLLED DEPARTURE TIME PROGRAMS).

CEILING
The heights above the earth's surface of the lowest layer of clouds or
obscuring phenomena that is reported as ``broken,'' ``overcast,'' or
``obscuration,'' and not classified as ``thin'' or ``partial''.

CEILING [ICAO]
The height above the ground or water of the base of the lowest layer
of cloud below 6,000 metres (20,000 feet) covering more than half the
sky.

CENRAP
(See CENTER RADAR ARTS PRESENTATION/PROCESSING).

CENRAP-PLUS
(See CENTER RADAR ARTS PRESENTATION/PROCESSING-PLUS).

CENTER
(See AIR ROUTE TRAFFIC CONTROL CENTER).

CENTER'S AREA
The specified airspace within which an air route traffic control
center (ARTCC) provides air traffic control and advisory service.

CENTER RADAR ARTS PRESENTATION/PROCESSING
A computer program developed to provide a back up system for airport
surveillance radar in the event of a failure or malfunction. The
program uses air route traffic control center radar for the processing
and presentation of data on the ARTS IIA or IIIA displays.

CENTER RADAR ARTS PRESENTATION/PROCESSING PLUS
A computer program developed to provide a back up system for airport
surveillance radar in the event of a terminal secondary radar system
failure. The program uses a combination of Air Route Traffic Control
Center Radar and terminal airport surveillance radar primary targets
displayed simultaneously for the processing and presentation of data
on the ARTS IIA or IIIA displays.

CENTER WEATHER ADVISORY
An unscheduled weather advisory issued by Center Weather Service Unit
meteorologists for ATC use to alert pilots of existing or anticipated
adverse weather conditions within the next 2 hours. A CWA may modify
or redefine a SIGMET.

CENTRAL EAST PACIFIC
An organized route system between the U.S. West Coast and Hawaii.

CEP
(See CENTRAL EAST PACIFIC).

CERAP
(See COMBINED CENTER RAPCON).

CFR
(See CALL FOR RELEASE).

CHAFF
Thin, narrow metallic reflectors of various lengths and frequency
responses, used to reflect radar energy. These reflectors when dropped
from aircraft and allowed to drift downward result in large targets on
the radar display.

CHARTED VFR FLYWAYS
Charted VFR Flyways are flight paths recommended for use to bypass
areas heavily traversed by large turbine powered aircraft. Pilot
compliance with recommended flyways and associated altitudes is
strictly voluntary. VFR Flyway Planning charts are published on the
back of existing VFR Terminal Area charts.

CHARTED VISUAL FLIGHT PROCEDURE APPROACH
An approach wherein a radar controlled aircraft on an IFR flight plan,
operating in VFR conditions and having an ATC authorization, may
proceed to the airport of intended landing via visual landmarks and
altitudes depicted on a charted visual flight procedure.

CHASE
An aircraft flown in proximity to another aircraft normally to observe
its performance during training or testing.

CHASE AIRCRAFT
(See CHASE).

CIRCLE TO LAND MANEUVER
A maneuver initiated by the pilot to align the aircraft with a runway
for landing when a straight in landing from an instrument approach is
not possible or is not desirable. This maneuver is made only after ATC
authorization has been obtained and the pilot has established required
visual reference to the airport

CIRCLE TO RUNWAY (RUNWAY NUMBER)
Used by ATC to inform the pilot that he must circle to land because
the runway in use is other than the runway aligned with the instrument
approach procedure. When the direction of the circling maneuver in
relation to the airport/runway is required, the controller will state
the direction (eight cardinal compass points) and specify a left or
right downwind or base leg as appropriate; e.g., ``Cleared VOR Runway
Three Six Approach circle to Runway Two Two,'' or ``Circle northwest
of the airport for a right downwind to Runway Two Two.''

CIRCLING APPROACH
(See CIRCLE TO LAND MANEUVER).

CIRCLING MANEUVER
(See CIRCLE TO LAND MANEUVER).

CIRCLING MINIMA
(See LANDING MINIMUMS).

CLASS A AIRSPACE
(See Controlled Airspace CLASS A AIRSPACE)

CLASS B AIRSPACE
(See Controlled Airspace CLASS B AIRSPACE)

CLASS C AIRSPACE
(See Controlled Airspace CLASS C AIRSPACE)

CLASS D AIRSPACE
(See Controlled Airspace CLASS D AIRSPACE)

CLASS E AIRSPACE
(See Controlled Airspace CLASS E AIRSPACE)

CLASS G AIRSPACE
That airspace not designated as Class A, B, C, D or E.

CLEAR AIR TURBULENCE
Turbulence encountered in air where no clouds are present. This term
is commonly applied to high level turbulence associated with wind
shear. CAT is often encountered in the vicinity of the jet stream.

CLEAR OF THE RUNWAY
A taxiing aircraft, which is approaching a runway, is clear of the
runway when all parts of the aircraft are held short of the applicable
holding position marking.  A pilot or controller may consider an
aircraft, which is exiting or crossing a runway, to be clear of the
runway when all parts of the aircraft are beyond the runway edge and
there is no ATC restriction to its continued movement beyond the
applicable holding position marking.  Pilots and controllers shall
exercise good judgement to ensure that adequate separation exists
between all aircraft on runways and taxiways at airports with
inadequate runway edge lines or holding position markings.

CLEARANCE
(See AIR TRAFFIC CLEARANCE).

CLEARANCE LIMIT
The fix, point, or location to which an aircraft is cleared when
issued an air traffic clearance.

CLEARANCE LIMIT [ICAO]
The point of which an aircraft is granted an air traffic control
clearance.

CLEARANCE VOID IF NOT OFF BY (TIME)
Used by ATC to advise an aircraft that the departure clearance is
automatically canceled if takeoff is not made prior to a specified
time. The pilot must obtain a new clearance or cancel his IFR flight
plan if not off by the specified time.

CLEARANCE VOID TIME [ICAO]
A time specified by an air traffic control unit at which a clearance
ceases to be valid unless the aircraft concerned has already taken
action to comply therewith.

CLEARED AS FILED
Means the aircraft is cleared to proceed in accordance with the route
of flight filed in the flight plan. This clearance does not include
the altitude, SID, or SID Transition.

CLEARED (Type Of) APPROACH
ATC authorization for an aircraft to execute a specific instrument
approach procedure to an airport; e.g., ``Cleared ILS Runway Three Six
Approach.''

CLEARED APPROACH
ATC authorization for an aircraft to execute any standard or special
instrument approach procedure for that airport. Normally, an aircraft
will be cleared for a specific instrument approach procedure.

CLEARED FOR TAKEOFF
ATC authorization for an aircraft to depart. It is predicated on known
traffic and known physical airport conditions.

CLEARED FOR THE OPTION 
ATC authorization for an aircraft to make a touch and go, low
approach, missed approach, stop and go, or full stop landing at the
discretion of the pilot. It is normally used in training so that an
instructor can evaluate a student's performance under changing
situations.

CLEARED THROUGH
ATC authorization for an aircraft to make intermediate stops at
specified airports without refiling a flight plan while en route to
the clearance limit.

CLEARED TO LAND
ATC authorization for an aircraft to land. It is predicated on known
traffic and known physical airport conditions.

CLEARWAY
An area beyond the takeoff runway under the control of airport
authorities within which terrain or fixed obstacles may not extend
above specified limits. These areas may be required for certain
turbine powered operations and the size and upward slope of the
clearway will differ depending on when the aircraft was certificated.

CLIMBOUT
That portion of flight operation between takeoff and the initial
cruising altitude.

CLIMB TO VFR
ATC authorization for an aircraft to climb to VFR conditions within
Class B, C, D, and E surface areas when the only weather limitation is
restricted visibility. The aircraft must remain clear of clouds while
climbing to VFR.

CLOSED RUNWAY
A runway that is unusable for aircraft operations. Only the airport
management/military operations office can close a runway.

CLOSED TRAFFIC
Successive operations involving takeoffs and landings or low
approaches where the aircraft does not exit the traffic pattern.

CLT
(See CALCULATED LANDING TIME).

CLUTTER
In radar operations, clutter refers to the reception and visual
display of radar returns caused by precipitation, chaff, terrain,
numerous aircraft targets, or other phenomena. Such returns may limit
or preclude ATC from providing services based on radar.

CMNPS
(See CANADIAN MINIMUM NAVIGATION PERFORMANCE SPECIFICATION AIRSPACE).

COASTAL FIX
A navigation aid or intersection where an aircraft transitions between
the domestic route structure and the oceanic route structure.

CODES
The number assigned to a particular multiple pulse reply signal
transmitted by a transponder.

COMBINED CENTER RAPCON
An air traffic facility which combines the functions of an ARTCC and a
radar approach control facility.

COMMON POINT
A significant point over which two or more aircraft will report
passing or have reported passing before proceeding on the same or
diverging tracks. To establish/maintain longitudinal separation, a
controller may determine a common point not originally in the
aircraft's flight plan and then clear the aircraft to fly over the
point. See significant point.

COMMON PORTION
(See COMMON ROUTE).

COMMON ROUTE
That segment of a North American Route between the inland navigation
facility and the coastal fix.

COMMON TRAFFIC ADVISORY FREQUENCY
A frequency designed for the purpose of carrying out airport advisory
practices while operating to or from an uncontrolled airport. The CTAF
may be a UNICOM, Multicom, FSS, or tower frequency and is identified
in appropriate aeronautical publications.

COMPASS LOCATOR
A low power, low or medium frequency (L/MF) radio beacon installed at
the site of the outer or middle marker of an instrument landing system
(ILS). It can be used for navigation at distances of approximately 15
miles or as authorized in the approach procedure.  Outer Compass
Locator (LOM). A compass locator installed at the site of the outer
marker of an instrument landing system.  Middle Compass Locator
(LMM). A compass locator installed at the site of the middle marker of
an instrument landing system.

COMPASS ROSE
A circle, graduated in degrees, printed on some charts or marked on
the ground at an airport. It is used as a reference to either true or
magnetic direction.

COMPOSITE FLIGHT PLAN
A flight plan which specifies VFR operation for one portion of flight
and IFR for another portion. It is used primarily in military
operations.

COMPOSITE ROUTE SYSTEM
An organized oceanic route structure, incorporating reduced lateral
spacing between routes, in which composite separation is authorized.

COMPOSITE SEPARATION
A method of separating aircraft in a composite route system where, by
management of route and altitude assignments, a combination of half
the lateral minimum specified for the area concerned and half the
vertical minimum is applied.

COMPULSORY REPORTING POINTS
Reporting points which must be reported to ATC. They are designated on
aeronautical charts by solid triangles or filed in a flight plan as
fixes selected to define direct routes. These points are geographical
locations which are defined by navigation aids/fixes. Pilots should
discontinue position reporting over compulsory reporting points when
informed by ATC that their aircraft is in ``radar contact.''

CONFLICT ALERT
A function of certain air traffic control automated systems designed
to alert radar controllers to existing or pending situations between
tracked targets (known IFR or VFR aircraft) that require his immediate
attention/action.

CONFLICT RESOLUTION 
The resolution of potential conflictions between aircraft that are
radar identified and in communication with ATC by ensuring that radar
targets do not touch. Pertinent traffic advisories shall be issued
when this procedure is applied.

CONSOLAN
A low frequency, long distance NAVAID used principally for
transoceanic navigations.

CONTACT
Establish communication with (followed by the name of the facility
and, if appropriate, the frequency to be used).  A flight condition
wherein the pilot ascertains the attitude of his aircraft and
navigates by visual reference to the surface.

CONTACT APPROACH
An approach wherein an aircraft on an IFR flight plan, having an air
traffic control authorization, operating clear of clouds with at least
1 mile flight visibility and a reasonable expectation of continuing to
the destination airport in those conditions, may deviate from the
instrument approach procedure and proceed to the destination airport
by visual reference to the surface. This approach will only be
authorized when requested by the pilot and the reported ground
visibility at the destination airport is at least 1 statute mile.

CONTERMINOUS U.S.
The 48 adjoining States and the District of Columbia.

CONTINENTAL UNITED STATES
The 49 States located on the continent of North America and the
District of Columbia.

CONTROL AREA [ICAO]
A controlled airspace extending upwards from a specified limit above
the earth.

CONTROLLED AIRSPACE
An airspace of defined dimensions within which air traffic control
service is provided to IFR flights and to VFR flights in accordance
with the airspace classification.  Note 1 - Controlled airspace is a
generic term that covers Class A, Class B, Class C, Class D, and Class
E airspace.  Note 2 - Controlled airspace is also that airspace within
which all aircraft operators are subject to certain pilot
qualifications, operating rules, and equipment requirements in Part 91
(for specific operating requirements, please refer to Part 91).  For
IFR operations in any class of controlled airspace, a pilot must file
an IFR flight plan and receive an appropriate ATC clearance.  Each
Class B, Class C, and Class D airspace area designated for an airport
contains at least one primary airport around which the airspace is
designated (for specific designations and descriptions of the airspace
classes, please refer to Part 71).  Controlled airspace in the United
States is designated as follows: CLASS A: Generally, that airspace
from 18,000 feet MSL up to and including FL600, including the airspace
overlying the waters within 12 nautical miles of the coast of the 48
contiguous States and Alaska.  Unless otherwise authorized, all
persons must operate their aircraft under IFR.  CLASS B: Generally,
that airspace from the surface to 10,000 feet MSL surrounding the
nation's busiest airports in terms of airport operations or passenger
enplanements.  The configuration of each Class B airspace area is
individually tailored and consists of a surface area and two or more
layers (some Class B airspaces areas resemble upside-down wedding
cakes), and is designed to contain all published instrument procedures
once an aircraft enters the airspace.  An ATC clearance is required
for all aircraft to operate in the area, and all aircraft that are so
cleared receive separation services within the airspace.  The cloud
clearance requirement for VFR operations is ``clear of clouds.''
CLASS C: Generally, that airspace from the surface to 4,000 feet above
the airport elevation (charted in MSL) surrounding those airports that
have an operational control tower, are serviced by a radar approach
control, and that have a certain number of IFR operations or passenger
enplanements.  Although the configuration of each Class C airspace
area is individually tailored, the airspace usually consists of a
surface area with a 5 nm radius, and an outer area with a 10 nm radius
that extends from 1,200 feet to 4,000 feet above the airport
elevation.  Each person must establish two-way radio communications
with the ATC facility providing air traffic services prior to entering
the airspace and thereafter maintain those communications while within
the airspace.  VFR aircraft are only separated from IFR aircraft
within the airspace.  CLASS D: Generally, that airspace from the
surface to 2,500 feet above the airport elevation (charted in MSL)
surrounding those airports that have an operational control tower.
The configuration of each Class D airspace area is individually
tailored and when instrument procedures are published, the airspace
will normally be designed to contain the procedures.  Arrival
extensions for instrument approach procedures may be Class D or Class
E airspace.  Unless otherwise authorized, each person must establish
two-way radio communications with the ATC facility providing air
traffic services prior entering the airspace and thereafter maintain
those communications while in the airspace.  No separation services
are provided to VFR aircraft.  CLASS E: Generally, if the airspace is
not Class A, Class B, Class C, or Class D, and it is controlled
airspace, it is Class E airspace.  Class E airspace extends upward
from either the surface or a designated altitude to the overlying or
adjacent controlled airspace.  When designated as a surface area, the
airspace will be configured to contain all instrument procedures.
Also in this class are Federal airways, airspace beginning at either
700 or 1,200 feet AGL used to transition to/from the terminal or
enroute environment, enroute domestic, and offshore airspace areas
designated below 18,000 feet MSL.  Unless designated at a lower
altitude, Class E airspace begins at 14,500 MSL over the United
States, including that airspace overlying the waters within 12
nautical miles of the coast of the 48 contiguous States and Alaska, up
to, but not including 18,000 feet MSL, and the airspace above FL 600.

CONTROLLED AIRSPACE [ICAO]
An airspace of defined dimensions within which air traffic control
service is provided to IFR flights and to VFR flights in accordance
with the airspace classification. Note-Controlled airspace is a
generic term which covers ATS airspace Classes A, B, C, D, and E.

CONTROLLED DEPARTURE TIME PROGRAMS
These programs are the flow control process whereby aircraft are held
on the ground at the departure airport when delays are projected to
occur in either the en route system or the terminal of intended
landing. The purpose of these programs is to reduce congestion in the
air traffic system or to limit the duration of airborne holding in the
arrival center or terminal area. A CDT is a specific departure slot
shown on the flight plan as an expected departure clearance time
(EDCT).

CONTROLLED TIME OF ARRIVAL
The original estimated time of arrival adjusted by the ATCSCC ground
delay factor.

CONTROLLER
(See AIR TRAFFIC CONTROL SPECIALIST).

CONTROLLER [ICAO]
A person authorized to provide air traffic control services.

CONTROL SECTOR
An airspace area of defined horizontal and vertical dimensions for
which a controller or group of controllers has air traffic control
responsibility, normally within an air route traffic control center or
an approach control facility. Sectors are established based on
predominant traffic flows, altitude strata, and controller
workload. Pilot communications during operations within a sector are
normally maintained on discrete frequencies assigned to the sector.

CONTROL SLASH
A radar beacon slash representing the actual position of the
associated aircraft. Normally, the control slash is the one closest to
the interrogating radar beacon site. When ARTCC radar is operating in
narrowband (digitized) mode, the control slash is converted to a
target symbol.

CONVECTIVE SIGMET
A weather advisory concerning convective weather significant to the
safety of all aircraft. Convective SIGMET's are issued for tornadoes,
lines of thunderstorms, embedded thunderstorms of any intensity level,
areas of thunderstorms greater than or equal to VIP level 4 with an
area coverage of 4/10 (40%) or more, and hail 3/4 inch or greater.

CONVECTIVE SIGNIFICANT METEOROLOGICAL INFORMATION
(See CONVECTIVE SIGMET).

COORDINATES
The intersection of lines of reference, usually expressed in
degrees/minutes/seconds of latitude and longitude, used to determine
position or location.

COORDINATION FIX
The fix in relation to which facilities will handoff, transfer control
of an aircraft, or coordinate flight progress data. For terminal
facilities, it may also serve as a clearance for arriving aircraft.

COPTER
(See HELICOPTER).

CORRECTION
An error has been made in the transmission and the correct version
follows.

COUPLED APPROACH
A coupled approach is an instrument approach performed by the aircraft
autopilot which is receiving position information and/or steering
commands from onboard navigation equipment. In general, coupled
nonprecision approaches must be discontinued and flown manually at
altitudes lower than 50 feet below the minimum descent altitude, and
coupled precision approaches must be flown manually below 50 feet ALG

COURSE

The intended direction of flight in the horizontal plane measured in
degrees from north.  The ILS localizer signal pattern usually
specified as the front course or the back course.  The intended track
along a straight, curved, or segmented MLS path.

CPL [ICAO]
(See CURRENT FLIGHT PLAN)

CRITICAL ENGINE
The engine which, upon failure, would most adversely affect the
performance or handling qualities of an aircraft.

CROSS (FIX) AT (ALTITUDE)
Used by ATC when a specific altitude restriction at a specified fix is
required.

CROSS (FIX) AT OR ABOVE (ALTITUDE)
Used by ATC when an altitude restriction at a specified fix is
required. It does not prohibit the aircraft from crossing the fix at a
higher altitude than specified; however, the higher altitude may not
be one that will violate a succeeding altitude restriction or altitude
assignment.

CROSS (FIX) AT OR BELOW (ALTITUDE)
Used by ATC when a maximum crossing altitude at a specific fix is
required. It does not prohibit the aircraft from crossing the fix at a
lower altitude; however, it must be at or above the minimum IFR
altitude.

CROSSWIND
When used concerning the traffic pattern, the word means ``crosswind
leg.''  When used concerning wind conditions, the word means a wind
not parallel to the runway or the path of an aircraft.

CROSSWIND COMPONENT
The wind component measured in knots at 90 degrees to the longitudinal
axis of the runway.

CRUISE
Used in an ATC clearance to authorize a pilot to conduct flight at any
altitude from the minimum IFR altitude up to and including the
altitude specified in the clearance. The pilot may level off at any
intermediate altitude within this block of airspace. Climb/descent
within the block is to be made at the discretion of the
pilot. However, once the pilot starts descent and verbally reports
leaving an altitude in the block, he may not return to that altitude
without additional ATC clearance. Further, it is approval for the
pilot to proceed to and make an approach at destination airport and
can be used in conjunction with: An airport clearance limit at
locations with a standard/special instrument approach procedure. The
FAR's require that if an instrument letdown to an airport is
necessary, the pilot shall make the letdown in accordance with a
standard/special instrument approach procedure for that airport, or An
airport clearance limit at locations that are within/below/outside
controlled airspace and without a standard/special instrument approach
procedure. Such a clearance is NOT AUTHORIZATION for the pilot to
descend under IFR conditions below the applicable minimum IFR altitude
nor does it imply that ATC is exercising control over aircraft in
Class G airspace; however, it provides a means for the aircraft to
proceed to destination airport, descend, and land in accordance with
applicable FAR's governing VFR flight operations. Also, this provides
search and rescue protection until such time as the IFR flight plan is
closed.

CRUISING ALTITUDE
An altitude or flight level maintained during en route level
flight. This is a constant altitude and should not be confused with a
cruise clearance.

CRUISING LEVEL [ICAO]
A level maintained during a significant portion of a flight.

CRUISE CLIMB
A climb technique employed by aircraft, usually at a constant power
setting, resulting in an increase of altitude as the aircraft weight
decreases.

CRUISING LEVEL
(See CRUISING ALTITUDE).

CT MESSAGE
An EDCT time generated by the ATCSCC to regulate traffic at arrival
airports. Normally, a CT message is automatically transferred from the
Traffic Management System computer to the NAS en route computer and
appears as an EDCT. In the event of a communication failure between
the TMS and the NAS, the CT message can be manually entered by the TMC
at the en route facility.

CTA
(See CONTROLLED TIME OF ARRIVAL).

CTA
(See CONTROL AREA [ICAO]).

CTAF
(See COMMON TRAFFIC ADVISORY FREQUENCY).

CURRENT FLIGHT PLAN [ICAO]
The flight plan, including changes, 

CVFP APPROACH
(See CHARTED VISUAL FLIGHT PROCEDURE APPROACH).

CWA
(See CENTER WEATHER ADVISORY).

DA [ICAO]
(See ICAO Term DECISION ALTITUDE/DECISION HEIGHT).

DAIR
(See DIRECT ALTITUDE AND IDENTITY READOUT).

DANGER AREA [ICAO]
An airspace of defined dimensions within which activities dangerous to
the flight of aircraft may exist at specified times.

DATA BLOCK
(See ALPHANUMERIC DISPLAY).

DEAD RECKONING
Dead reckoning, as applied to flying, is the navigation of an airplane
solely by means of computations based on airspeed, course, heading,
wind direction, and speed, groundspeed, and elapsed time.

DECISION ALTITUDE/DECISION HEIGHT [ICAO]
A specified altitude or height (A/H) in the precision approach at
which a missed approach must be initiated if the required visual
reference to continue the approach has not been established.

DECISION HEIGHT
With respect to the operation of aircraft, means the height at which a
decision must be made during an ILS, MLS, or PAR instrument approach
to either continue the approach or to execute a missed approach.

DECODER
The device used to decipher signals received from ATCRBS transponders
to effect their display as select codes.

DEFENSE VISUAL FLIGHT RULES
Rules applicable to flights within an ADIZ conducted under the visual
flight rules in Part 91.

DELAY INDEFINITE (REASON IF KNOWN) EXPECT FURTHER CLEARANCE (TIME)
Used by ATC to inform a pilot when an accurate estimate of the delay
time and the reason for the delay cannot immediately be determined;
e.g., a disabled aircraft on the runway, terminal or center area
saturation, weather below landing minimums, etc.

DELAY TIME
The amount of time that the arrival must lose to cross the meter fix
at the assigned meter fix time. This is the difference between ACLT
and VTA.

DEPARTURE CENTER
The ARTCC having jurisdiction for the airspace that generates a flight
to the impacted airport.

DEPARTURE CONTROL
A function of an approach control facility providing air traffic
control service for departing IFR and, under certain conditions, VFR
aircraft.

DEPARTURE SEQUENCING PROGRAM
A program designed to assist in achieving a specified interval over a
common point for departures.

DEPARTURE TIME
The time an aircraft becomes airborne.

DESCENT SPEED ADJUSTMENTS
Speed deceleration calculations made to determine an accurate
VTA. These calculations start at the transition point and use arrival
speed segments to the vertex.

DETRESFA (DISTRESS PHASE) [ICAO]
The code word used to designate an emergency phase wherein there is
reasonable certainty that an aircraft and its occupants are threatened
by grave and imminent danger or require immediate assistance.

DEVIATIONS
A departure from a current clearance, such as an off course maneuver
to avoid weather or turbulence.  Where specifically authorized in the
FAR's and requested by the pilot, ATC may permit pilots to deviate
from certain regulations.

DF
(See DIRECTION FINDER).

DF APPROACH PROCEDURE
Used under emergency conditions where another instrument approach
procedure cannot be executed. DF guidance for an instrument approach
is given by ATC facilities with DF capability.

DF FIX
The geographical location of an aircraft obtained by one or more
direction finders.

DF GUIDANCE
Headings provided to aircraft by facilities equipped with direction
finding equipment. These headings, if followed, will lead the aircraft
to a predetermined point such as the DF station or an airport. DF
guidance is given to aircraft in distress or to other aircraft which
request the service. Practice DF guidance is provided when workload
permits.

DF STEER
(See DF GUIDANCE).

DH
(See DECISION HEIGHT).

DH [ICAO]
(See ICAO Term DECISION ALTITUDE/DECISION HEIGHT).

DIRECT
Straight line flight between two navigational aids, fixes, points, or
any combination thereof. When used by pilots in describing off airway
routes, points defining direct route segments become compulsory
reporting points unless the aircraft is under radar contact.

DIRECT ALTITUDE AND IDENTITY READOUT
The DAIR System is a modification to the AN/TPX-42 Interrogator
System. The Navy has two adaptations of the DAIR System Carrier Air
Traffic Control Direct Altitude and Identification Readout System for
Aircraft Carriers and Radar Air Traffic Control Facility Direct
Altitude and Identity Readout System for land based terminal
operations. The DAIR detects, tracks, and predicts secondary radar
aircraft targets. Targets are displayed by means of computer generated
symbols and alphanumeric characters depicting flight identification,
altitude, ground speed, and flight plan data. The DAIR System is
capable of interfacing with ARTCC's.

DIRECTION FINDER
A radio receiver equipped with a directional sensing antenna used to
take bearings on a radio transmitter. Specialized radio direction
finders are used in aircraft as air navigation aids. Others are ground
based, primarily to obtain a ``fix'' on a pilot requesting orientation
assistance or to locate downed aircraft. A location ``fix'' is
established by the intersection of two or more bearing lines plotted
on a navigational chart using either two separately located Direction
Finders to obtain a fix on an aircraft or by a pilot plotting the
bearing indications of his DF on two separately located ground based
transmitters, both of which can be identified on his chart. UDF's
receive signals in the ultra high frequency radio broadcast band;
VDF's in the very high frequency band; and UVDF's in both bands. ATC
provides DF service at those air traffic control towers and flight
service stations listed in the Airport/Facility Directory and the DOD
FLIP IFR En Route Supplement.

DISCRETE BEACON CODE
(See DISCRETE CODE).

DISCRETE CODE
As used in the Air Traffic Control Radar Beacon System (ATCRBS), any
one of the 4096 selectable Mode 3/A aircraft transponder codes except
those ending in zero zero; e.g., discrete codes: 0010, 1201, 2317,
7777; nondiscrete codes: 0100, 1200, 7700. Nondiscrete codes are
normally reserved for radar facilities that are not equipped with
discrete decoding capability and for other purposes such as
emergencies (7700), VFR aircraft (1200), etc.

DISCRETE FREQUENCY
A separate radio frequency for use in direct pilot controller
communications in air traffic control which reduces frequency
congestion by controlling the number of aircraft operating on a
particular frequency at one time. Discrete frequencies are normally
designated for each control sector in en route/terminal ATC
facilities. Discrete frequencies are listed in the Airport/Facility
Directory and the DOD FLIP IFR En Route Supplement.

DISPLACED THRESHOLD
A threshold that is located at a point on the runway other than the
designated beginning of the runway.

DISTANCE MEASURING EQUIPMENT
Equipment (airborne and ground) used to measure, in nautical miles,
the slant range distance of an aircraft from the DME navigational aid.

DISTRESS
A condition of being threatened by serious and/or imminent danger and
of requiring immediate assistance.

DIVE BRAKES
(See SPEED BRAKES).

DIVERSE VECTOR AREA
In a radar environment, that area in which a prescribed departure
route is not required as the only suitable route to avoid
obstacles. The area in which random radar vectors below the MVA/MIA,
established in accordance with the TERPS criteria for diverse
departures obstacles and terrain avoidance, may be issued to departing
aircraft.

DME
(See DISTANCE MEASURING EQUIPMENT).

DME FIX
A geographical position determined by reference to a navigational aid
which provides distance and azimuth information. It is defined by a
specific distance in nautical miles and a radial, azimuth, or course
(i.e., localizer) in degrees magnetic from that aid.

DME SEPARATION
Spacing of aircraft in terms of distances (nautical miles) determined
by reference to distance measuring equipment (DME).

DOD FLIP
Department of Defense Flight Information Publications used for flight
planning, en route, and terminal operations. FLIP is produced by the
Defense Mapping Agency for world wide use. United States Government
Flight Information Publications (en route charts and instrument
approach procedure charts) are incorporated in DOD FLIP for use in the
National Airspace System (NAS).

DOMESTIC AIRSPACE
Airspace which overlies the continental land mass of the United States
plus Hawaii and U.S. possessions. Domestic airspace extends to 12
miles offshore.

DOWNBURST
A strong downdraft which induces an outburst of damaging winds on or
near the ground. Damaging winds, either straight or curved, are highly
divergent. The sizes of downbursts vary from 1/2 mile or less to more
than 10 miles. An intense down burst often causes widespread
damage. Damaging winds, lasting 5 to 30 minutes, could reach speeds as
high as 120 knots.

DOWNWIND LEG
(See TRAFFIC PATTERN).

DRAG CHUTE
A parachute device installed on certain aircraft which is deployed on
landing roll to assist in deceleration of the aircraft.

DSP
(See DEPARTURE SEQUENCING PROGRAM).

DT
(See DELAY TIME).

DUE REGARD
A phase of flight wherein an aircraft commander of a State operated
aircraft assumes responsibility to separate his aircraft from all
other aircraft.

DUTY RUNWAY
(See RUNWAY IN USE/ACTIVE RUNWAY/DUTY RUNWAY).

DVA
(See DIVERSE VECTOR AREA).

DVFR
(See DEFENSE VISUAL FLIGHT RULES).

DVFR FLIGHT PLAN
A flight plan filed for a VFR aircraft which intends to operate in
airspace within which the ready identification, location, and control
of aircraft are required in the interest of national security.

DYNAMIC
Continuous review, evaluation, and change to meet demands.

DYNAMIC RESTRICTIONS
Those restrictions imposed by the local facility on an ~``as needed''
basis to manage unpredictable fluctuations in traffic demands.

EARTS
(See EN ROUTE AUTOMATED RADAR TRACKING SYSTEM).

EDCT
(See EXPECTED DEPARTURE CLEARANCE TIME).

EFC
(See EXPECT FURTHER CLEARANCE (TIME)).

ELT
(See EMERGENCY LOCATOR TRANSMITTER).

EMERGENCY
A distress or an urgency condition.

EMERGENCY LOCATOR TRANSMITTER
A radio transmitter attached to the aircraft structure which operates
from its own power source on 121.5 mHz and 243.0 mHz. It aids in
locating downed aircraft by radiating a downward sweeping audio tone,
2-4 times per second. It is designed to function without human action
after an accident.

EMERGENCY SAFE ALTITUDE
(See MINIMUM SAFE ALTITUDE).

ERMSAW
(See EN ROUTE MINIMUM SAFE ALTITUDE WARNING).

ENTRY POINT 
The point at which an aircraft transitions from an offshore control
area to oceanic airspace.

ENGINEERED PERFORMANCE STANDARDS
A mathematically derived runway capacity standard. EPS's are
calculated for each airport on an individual basis and reflect that
airport's aircraft mix, operating procedures, runway layout, and
specific weather conditions. EPS's do not give consideration to
staffing, experience levels, equipment outages, and in trail
restrictions as does the AAR.

EN ROUTE AIR TRAFFIC CONTROL SERVICES
Air traffic control service provided aircraft on IFR flight plans,
generally by centers, when these aircraft are operating between
departure and destination terminal areas. When equipment,
capabilities, and controller workload permit, certain
advisory/assistance services may be provided to VFR aircraft.

EN ROUTE AUTOMATED RADAR TRACKING SYSTEM
An automated radar and radar beacon tracking system. Its functional
capabilities and design are essentially the same as the terminal ARTS
IIIA system except for the EARTS capability of employing both short
range (ASR) and long range (ARSR) radars, use of full digital radar
displays, and fail safe design.

EN ROUTE CHARTS
(See AERONAUTICAL CHART).

EN ROUTE DESCENT
Descent from the en route cruising altitude which takes place along
the route of flight.

EN ROUTE FLIGHT ADVISORY SERVICE
A service specifically designed to provide, upon pilot request, timely
weather information pertinent to his type of flight, intended route of
flight, and altitude. The FSS's providing this service are listed in
the Airport/Facility Directory.

EN ROUTE HIGH ALTITUDE CHARTS
(See AERONAUTICAL CHART).

EN ROUTE LOW ALTITUDE CHARTS
(See AERONAUTICAL CHART).

EN ROUTE MINIMUM SAFE ALTITUDE WARNING
A function of the NAS Stage A en route computer that aids the
controller by alerting him when a tracked aircraft is below or
predicted by the computer to go below a predetermined minimum IFR
altitude (MIA).

EN ROUTE SPACING PROGRAM
A program designed to assist the exit sector in achieving the required
in trail spacing.

EPS
(See ENGINEERED PERFORMANCE STANDARDS).

ESP
(See EN ROUTE SPACING PROGRAM).

ESTIMATED ELAPSED TIME [ICAO]
The estimated time required to proceed from one significant point to
another.

ESTIMATED OFF BLOCK TIME [ICAO]
The estimated time at which the aircraft will commence movement
associated with departure.

ESTIMATED TIME OF ARRIVAL
The time the flight is estimated to arrive at the gate (scheduled
operators) or the actual runway on times for nonscheduled operators.

ESTIMATED TIME EN ROUTE
The estimated flying time from departure point to destination (lift
off to touchdown).

ETA
(See ESTIMATED TIME OF ARRIVAL).

ETE
(See ESTIMATED TIME EN ROUTE).

EXECUTE MISSED APPROACH 
Instructions issued to a pilot making an instrument approach which
means continue inbound to the missed approach point and execute the
missed approach procedure as described on the Instrument Approach
Procedure Chart or as previously assigned by ATC. The pilot may climb
immediately to the altitude specified in the missed approach procedure
upon making a missed approach. No turns should be initiated prior to
reaching the missed approach point. When conducting an ASR or PAR
approach, execute the assigned missed approach procedure immediately
upon receiving instructions to ``execute missed approach.''

EXPECT (ALTITUDE) AT (TIME) or (FIX)
Used under certain conditions to provide a pilot with an altitude to
be used in the event of two way communications failure. It also
provides altitude information to assist the pilot in planning.

EXPECTED DEPARTURE CLEARANCE TIME
The runway release time assigned to an aircraft in a controlled
departure time program and shown on the flight progress strip as an
EDCT.

EXPECT FURTHER CLEARANCE (TIME)
The time a pilot can expect to receive clearance beyond a clearance
limit.

EXPECT FURTHER CLEARANCE VIA (AIRWAYS, ROUTES OR FIXES)
Used to inform a pilot of the routing he can expect if any part of the
route beyond a short range clearance limit differs from that filed.

EXPEDITE
Used by ATC when prompt compliance is required to avoid the
development of an imminent situation.

FAF
(See FINAL APPROACH FIX).

FA MESSAGE
The data entered into the ARTCC computers that activates delay
processing for an impacted airport. The FA data includes the delay
factor for flight plans that have not been assigned delays under CT
message processing. The delay factor appears on flight progress strips
in the form of an EDCT (e.g., EDCT 1820). FA processing assigns delays
in 15-minute time blocks. FA's control numbers of aircraft within a
specified time block but do not spread aircraft out evenly throughout
the time block.

FAP
(See FINAL APPROACH POINT).

FAST FILE
A system whereby a pilot files a flight plan via telephone that is
tape recorded and then transcribed for transmission to the appropriate
air traffic facility. Locations having a fast file capability are
contained in the Airport/Facility Directory.

FCLT
(See FREEZE CALCULATED LANDING TIME).

FEATHERED PROPELLER
A propeller whose blades have been rotated so that the leading and
trailing edges are nearly parallel with the aircraft flight path to
stop or minimize drag and engine rotation. Normally used to indicate
shutdown of a reciprocating or turboprop engine due to malfunction.

FEDERAL AIRWAYS
(See LOW ALTITUDE AIRWAY STRUCTURE).

FEEDER FIX
The fix depicted on Instrument Approach Procedure Charts which
establishes the starting point of the feeder route.

FEEDER ROUTE
A route depicted on instrument approach procedure charts to designate
routes for aircraft to proceed from the en route structure to the
initial approach fix (IAF).

FERRY FLIGHT
A flight for the purpose of:
Returning an aircraft to base.
Delivering an aircraft from one location to another.
Moving an aircraft to and from a maintenance base.
Ferry flights, under certain conditions, may be conducted under terms
of a special flight permit.

FIELD ELEVATION
(See AIRPORT ELEVATION).

FILED
Normally used in conjunction with flight plans, meaning a flight plan
has been submitted to ATC.

FILED EN ROUTE DELAY
Any of the following preplanned delays at points/areas along the route
of flight which require special flight plan filing and handling
techniques.  Terminal Area Delay. A delay within a terminal area for
touch and go, low approach, or other terminal area activity.  Special
Use Airspace Delay. A delay within a Military Operating Area,
Restricted Area, Warning Area, or ATC Assigned Airspace.  Aerial
Refueling Delay. A delay within an Aerial Refueling Track or Anchor.

FILED FLIGHT PLAN
The flight plan as filed with an ATS unit by the pilot or his
designated representative without any subsequent changes or
clearances.

FINAL
Commonly used to mean that an aircraft is on the final approach course
or is aligned with a landing area.

FINAL APPROACH [ICAO]
That part of an instrument approach procedure which commences at the
specified final approach fix or point, or where such a fix or point is
not specified, a) At the end of the last procedure turn, base turn or
inbound turn of a racetrack procedure, if specified; or b) At the
point of interception of the last track specified in the approach
procedure; and ends at a point in the vicinity of an aerodrome from
which: 1)A landing can be made; or 2)A missed approach procedure is
initiated.

FINAL APPROACH COURSE
A published MLS course, a straight line extension of a localizer, a
final approach radial/bearing, or a runway centerline all without
regard to distance.

FINAL APPROACH FIX
The fix from which the final approach (IFR) to an airport is executed
and which identifies the beginning of the final approach segment. It
is designated on Government charts by the Maltese Cross symbol for
nonprecision approaches and the lightning bolt symbol for precision
approaches; or when ATC directs a lower than published Glideslope/path
Intercept Altitude, it is the resultant actual point of the
glideslope/path intercept.

FINAL APPROACH IFR
The flight path of an aircraft which is inbound to an airport on a
final instrument approach course, beginning at the final approach fix
or point and extending to the airport or the point where a circle to
land maneuver or a missed approach is executed.

FINAL APPROACH POINT
The point, applicable only to a nonprecision approach with no depicted
FAF (such as an on airport VOR), where the aircraft is established
inbound on the final approach course from the procedure turn and where
the final approach descent may be commenced. The FAP serves as the FAF
and identifies the beginning of the final approach segment.

FINAL APPROACH SEGMENT
(See SEGMENTS OF AN INSTRUMENT APPROACH PROCEDURE).

FINAL APPROACH SEGMENT [ICAO]
That segment of an instrument approach procedure in which alignment
and descent for landing are accomplished.

FINAL APPROACH VFR
(See TRAFFIC PATTERN).

FINAL CONTROLLER
The controller providing information and final approach guidance
during PAR and ASR approaches utilizing radar equipment.

FINAL MONITOR AID
A high resolution color display that is equipped with the controller
alert system hardware/software which is used in the precision runway
monitor (PRM) system.  The display includes alert algorithms providing
the target predictors, a color change alert when a target penetrates
or is predicted to penetrate the no transgression zone (NTZ), a color
change alert if the aircraft transponder becomes inoperative,
synthesized voice alerts, digital mapping, and like features contained
in the PRM system.

FIR
(See FLIGHT INFORMATION REGION).

FIRST TIER CENTER
The ARTCC immediately adjacent to the impacted center.

FIX
A geographical position determined by visual reference to the surface,
by reference to one or more radio NAVAIDs, by celestial plotting, or
by another navigational device.

FIX BALANCING
A process whereby aircraft are evenly distributed over several
available arrival fixes reducing delays and controller workload.

FLAG
A warning device incorporated in certain airborne navigation and
flight instruments indicating that: Instruments are inoperative or
otherwise not operating satisfactorily, or Signal strength or quality
of the received signal falls below acceptable values.

FLAG ALARM
(See FLAG).

FLAMEOUT
Unintended loss of combustion in turbine engines resulting in the loss
of engine power.

FLIGHT CHECK
A call sign prefix used by FAA aircraft engaged in flight
inspection/certification of navigational aids and flight
procedures. The word ``recorded'' may be added as a suffix; e.g.,
``Flight Check 320 recorded'' to indicate that an automated flight
inspection is in progress in terminal areas.

FLIGHT FOLLOWING
(See TRAFFIC ADVISORIES).

FLIGHT INFORMATION REGION
An airspace of defined dimensions within which Flight Information
Service and Alerting Service are provided.  Flight Information
Service. A service provided for the purpose of giving advice and
information useful for the safe and efficient conduct of flights.
Alerting Service. A service provided to notify appropriate
organizations regarding aircraft in need of search and rescue aid and
to assist such organizations as required.

FLIGHT INFORMATION SERVICE
A service provided for the purpose of giving advice and information
useful for the safe and efficient conduct of flights.

FLIGHT INSPECTION
Inflight investigation and evaluation of a navigational aid to
determine whether it meets established tolerances.

FLIGHT LEVEL
A level of constant atmospheric pressure related to a reference datum
of 29.92 inches of mercury. Each is stated in three digits that
represent hundreds of feet. For example, flight level 250 represents a
barometric altimeter indication of 25,000 feet; flight level 255, an
indication of 25,500 feet.

FLIGHT LEVEL [ICAO]
A surface of constant atmospheric pressure which is related to a
specific pressure datum, 1013.2 hPa (1013.2 mb), and is separated from
other such surfaces by specific pressure intervals.  a)When set to a
QNH altimeter setting, will indicate altitude; b)When set to a QFE
altimeter setting, will indicate height above the QFE reference datum;
and c)When set to a pressure of 1013.2 hPa (1013.2 mb), may be used to
indicate flight levels.

FLIGHT LINE 
A term used to describe the precise movement of a civil
photogrammetric aircraft along a predetermined course(s) at a
predetermined altitude during the actual photographic run.

FLIGHT MANAGEMENT SYSTEMS
A computer system that uses a large data base to allow routes to be
preprogrammed and fed into the system by means of a data loader. The
system is constantly updated with respect to position accuracy by
reference to conventional navigation aids. The sophisticated program
and its associated data base insures that the most appropriate aids
are automatically selected during the information update cycle.

FLIGHT PATH
A line, course, or track along which an aircraft is flying or intended
to be flown.

FLIGHT PLAN
Specified information relating to the intended flight of an aircraft
that is filed orally or in writing with an FSS or an ATC facility.

FLIGHT PLAN AREA
The geographical area assigned by regional air traffic divisions to a
flight service station for the purpose of search and rescue for VFR
aircraft, issuance of notams, pilot briefing, in flight services,
broadcast, emergency services, flight data processing, international
operations, and aviation weather services. Three letter identifiers
are assigned to every flight service station and are annotated in
AFD's and Order 7350.6 as tie in facilities.

FLIGHT RECORDER
A general term applied to any instrument or device that records
information about the performance of an aircraft in flight or about
conditions encountered in flight. Flight recorders may make records of
airspeed, outside air temperature, vertical acceleration, engine RPM,
manifold pressure, and other pertinent variables for a given flight.

FLIGHT RECORDER [ICAO]
Any type of recorder installed in the aircraft for the purpose of
complementing accident/incident investigation.

FLIGHT SERVICE STATION
Air traffic facilities which provide pilot briefing, en route
communications and VFR search and rescue services, assist lost
aircraft and aircraft in emergency situations, relay ATC clearances,
originate Notices to Airmen, broadcast aviation weather and NAS
information, receive and process IFR flight plans, and monitor
NAVAID's. In addition, at selected locations, FSS's provide Enroute
Flight Advisory Service (Flight Watch), take weather observations,
issue airport advisories, and advise Customs and Immigration of
transborder flights.

FLIGHT STANDARDS DISTRICT OFFICE
An FAA field office serving an assigned geographical area and staffed
with Flight Standards personnel who serve the aviation industry and
the general public on matters relating to the certification and
operation of air carrier and general aviation aircraft. Activities
include general surveillance of operational safety, certification of
airmen and aircraft, accident prevention, investigation, enforcement,
etc.

FLIGHT TEST
A flight for the purpose of:
Investigating the operation/flight characteristics of an aircraft or
aircraft component.  Evaluating an applicant for a pilot certificate
or rating.

FLIGHT VISIBILITY
(See VISIBILITY).

FLIGHT WATCH
A shortened term for use in air ground contacts to identify the flight
service station providing En Route Flight Advisory Service; e.g.,
``Oakland Flight Watch.''

FLIP
(See DOD FLIP).

FLOW CONTROL
Measures designed to adjust the flow of traffic into a given airspace,
along a given route, or bound for a given aerodrome (airport) so as to
ensure the most effective utilization of the airspace.

FLY HEADING (DEGREES)
Informs the pilot of the heading he should fly. The pilot may have to
turn to, or continue on, a specific compass direction in order to
comply with the instructions. The pilot is expected to turn in the
shorter direction to the heading unless otherwise instructed by ATC.

FMA
(See FINAL MONITOR AID).

FMS
(See FLIGHT MANAGEMENT SYSTEM).

FORMATION FLIGHT
More than one aircraft which, by prior arrangement between the pilots,
operate as a single aircraft with regard to navigation and position
reporting. Separation between aircraft within the formation is the
responsibility of the flight leader and the pilots of the other
aircraft in the flight. This includes transition periods when aircraft
within the formation are maneuvering to attain separation from each
other to effect individual control and during join up and breakaway.
A standard formation is one in which a proximity of no more than 1
mile laterally or longitudinally and within 100 feet vertically from
the flight leader is maintained by each wingman.  Nonstandard
formations are those operating under any of the following conditions:
 When the flight leader has requested and ATC has approved other than
standard formation dimensions.
 When operating within an authorized altitude reservation (ALTRV) or
under the provisions of a letter of agreement.
 When the operations are conducted in airspace specifically designed
for a special activity.

FRC
(See REQUEST FULL ROUTE CLEARANCE).

FREEZE/FROZEN
Terms used in referring to arrivals which have been assigned ACLT's
and to the lists in which they are displayed.

FREEZE CALCULATED LANDING TIME
A dynamic parameter number of minutes prior to the meter fix
calculated time of arrival for each aircraft when the TCLT is frozen
and becomes an ACLT (i.e., the VTA is updated and consequently the
TCLT is modified as appropriate until FCLT minutes prior to meter fix
calculated time of arrival, at which time updating is suspended and an
ACLT and a frozen meter fix crossing time (MFT) is assigned).

FREEZE SPEED PARAMETER
A speed adapted for each aircraft to determine fast and slow
aircraft. Fast aircraft freeze on parameter FCLT and slow aircraft
freeze on parameter MLDI.

FSDO
(See FLIGHT STANDARDS DISTRICT OFFICE).

FSPD
(See FREEZE SPEED PARAMETER).

FSS
(See FLIGHT SERVICE STATION).

FUEL DUMPING
Airborne release of usable fuel. This does not include the dropping of
fuel tanks.

FUEL REMAINING
A phrase used by either pilots or controllers when relating to the
fuel remaining on board until actual fuel exhaustion. When
transmitting such information in response to either a controller
question or pilot initiated cautionary advisory to air traffic
control, pilots will state the APPROXIMATE NUMBER OF MINUTES the
flight can continue with the fuel remaining. All reserve fuel SHOULD
BE INCLUDED in the time stated, as should an allowance for established
fuel gauge system error.

FUEL SIPHONING
Unintentional release of fuel caused by overflow, puncture, loose cap,
etc.

FUEL VENTING
(See FUEL SIPHONING).

GADO
(See GENERAL AVIATION DISTRICT OFFICE).

GATE HOLD PROCEDURES
Procedures at selected airports to hold aircraft at the gate or other
ground location whenever departure delays exceed or are anticipated to
exceed 15 minutes. The sequence for departure will be maintained in
accordance with initial call up unless modified by flow control
restrictions. Pilots should monitor the ground control/clearance
delivery frequency for engine start/taxi advisories or new proposed
start/taxi time if the delay changes.

GCA
(See GROUND CONTROLLED APPROACH).

GENERAL AVIATION
That portion of civil aviation which encompasses all facets of
aviation except air carriers holding a certificate of public
convenience and necessity from the Civil Aeronautics Board and large
aircraft commercial operators.

GENERAL AVIATION [ICAO]
All civil aviation operations other than scheduled air services and
nonscheduled air transport operations for remuneration or hire.

GENERAL AVIATION DISTRICT OFFICE
An FAA field office serving a designated geographical area and staffed
with Flight Standards personnel who have the responsibility for
serving the aviation industry and the general public on all matters
relating to the certification and operation of general aviation
aircraft.

GEO MAP
The digitized map markings associated with the ASR-9 Radar System.

GLIDEPATH
(See GLIDESLOPE).

GLIDEPATH INTERCEPT ALTITUDE
(See GLIDESLOPE INTERCEPT ALTITUDE).

GLIDESLOPE
Provides vertical guidance for aircraft during approach and
landing. The glideslope/glidepath is based on the following:
Electronic components emitting signals which provide vertical guidance
by reference to airborne instruments during instrument approaches such
as ILS/MLS, or Visual ground aids, such as VASI, which provide
vertical guidance for a VFR approach or for the visual portion of an
instrument approach and landing.  PAR. Used by ATC to inform an
aircraft making a PAR approach of its vertical position (elevation)
relative to the descent profile.

GLIDEPATH [ICAO]
A descent profile determined for vertical guidance during a final
approach.

GLIDESLOPE INTERCEPT ALTITUDE
The minimum altitude to intercept the glideslope/path on a precision
approach. The intersection of the published intercept altitude with
the glideslope/path, designated on Government charts by the lightning
bolt symbol, is the precision FAF; however, when ATC directs a lower
altitude, the resultant lower intercept position is then the FAF.

GLOBAL POSITIONING SYSTEM
A space base radio positioning, navigation, and time transfer system
being developed by Department of Defense. When fully deployed, the
system is intended to provide highly accurate position and velocity
information, and precise time, on a continuous global basis, to an
unlimited number of properly equipped users. The system will be
unaffected by weather, and will provide a worldwide common grid
reference system. The GPS concept is predicated upon accurate and
continuous knowledge of the spatial position of each satellite in the
system with respect to time and distance from a transmitting satellite
to the user. The GPS receiver automatically selects appropriate
signals from the satellites in view and translates these into a three
dimensional position, velocity, and time. Predictable system accuracy
for civil users is projected to be 100 meters
horizontally. Performance standards and certification criteria have
not yet been established.

GO AHEAD
Proceed with your message. Not to be used for any other purpose.

GO AROUND
Instructions for a pilot to abandon his approach to
landing. Additional instructions may follow. Unless otherwise advised
by ATC, a VFR aircraft or an aircraft conducting visual approach
should overfly the runway while climbing to traffic pattern altitude
and enter the traffic pattern via the crosswind leg. A pilot on an IFR
flight plan making an instrument approach should execute the published
missed approach procedure or proceed as instructed by ATC; e.g., ``Go
around'' (additional instructions if required).

GPS
(See Global Positioning System).

GROUND CLUTTER
A pattern produced on the radar scope by ground returns which may
degrade other radar returns in the affected area. The effect of ground
clutter is minimized by the use of moving target indicator (MTI)
circuits in the radar equipment resulting in a radar presentation
which displays only targets which are in motion.

GROUND CONTROLLED APPROACH
A radar approach system operated from the ground by air traffic
control personnel transmitting instructions to the pilot by radio. The
approach may be conducted with surveillance radar (ASR) only or with
both surveillance and precision approach radar (PAR). Usage of the
term ``GCA'' by pilots is discouraged except when referring to a GCA
facility. Pilots should specifically request a ``PAR'' approach when a
precision radar approach is desired or request an ``ASR'' or
``surveillance'' approach when a nonprecision radar approach is
desired.

GROUND DELAY
The amount of delay attributed to ATC, encountered prior to departure,
usually associated with a CDT program.

GROUND SPEED
The speed of an aircraft relative to the surface of the earth.

GROUND STOP
Normally, the last initiative to be utilized; this method mandates
that the terminal facility will not allow any departures to enter the
ARTCC airspace until further notified.

GROUND VISIBILITY
(See VISIBILITY).

HAA
(See HEIGHT ABOVE AIRPORT).

HAL
(See HEIGHT ABOVE LANDING).

HANDOFF
An action taken to transfer the radar identification of an aircraft
from one controller to another if the aircraft will enter the
receiving controller's airspace and radio communications with the
aircraft will be transferred.

HAT
(See HEIGHT ABOVE TOUCHDOWN).

HAVE NUMBERS
Used by pilots to inform ATC that they have received runway, wind, and
altimeter information only.

HAZARDOUS INFLIGHT WEATHER ADVISORY SERVICE
Continuous recorded hazardous inflight weather forecasts broadcasted
to airborne pilots over selected VOR outlets defined as an HIWAS
BROADCAST AREA.

HAZARDOUS WEATHER INFORMATION
Summary of significant meteorological information (SIGMET/WS),
convective significant meteorological information (convective
SIGMET/WST), urgent pilot weather reports (urgent PIREP/UUA), center
weather advisories (CWA), airmen's meteorological information
(AIRMET/WA) and any other weather such as isolated thunderstorms that
are rapidly developing and increasing in intensity, or low ceilings
and visibilities that are becoming widespread which is considered
significant and are not included in a current hazardous weather
advisory.

HEAVY (AIRCRAFT)
(See AIRCRAFT CLASSES).

HEIGHT ABOVE AIRPORT
The height of the Minimum Descent Altitude above the published airport
elevation. This is published in conjunction with circling minimums.

HEIGHT ABOVE LANDING
The height above a designated helicopter landing area used for
helicopter instrument approach procedures.

HEIGHT ABOVE TOUCHDOWN
The height of the Decision Height or Minimum Descent Altitude above
the highest runway elevation in the touchdown zone (first 3,000 feet
of the runway). HAT is published on instrument approach charts in
conjunction with all straight in minimums.

HELICOPTER
Rotorcraft that, for its horizontal motion, depends principally on its
engine driven rotors.

HELICOPTER [ICAO]
A heavier than air aircraft supported in flight chiefly by the
reactions of the air on one or more power driven rotors on
substantially vertical axes.

HELIPAD
A small, designated area, usually with a prepared surface, on a
heliport, airport, landing/takeoff area, apron/ramp, or movement area
used for takeoff, landing, or parking of helicopters.

HELIPORT
An area of land, water, or structure used or intended to be used for
the landing and takeoff of helicopters and includes its buildings and
facilities if any.

HERTZ
The standard radio equivalent of frequency in cycles per second of an
electromagnetic wave. Kilohertz (kHz) is a frequency of one thousand
cycles per second. Megahertz (mHz) is a frequency of one million
cycles per second.

HF
(See HIGH FREQUENCY).

HF COMMUNICATIONS
(See HIGH FREQUENCY COMMUNICATIONS).

HIGH FREQUENCY
The frequency band between 3 and 30 mHz.

HIGH FREQUENCY COMMUNICATIONS
High radio frequencies (HF) between 3 and 30 mHz used for air to
ground voice communication in overseas operations.

HIGH SPEED EXIT
(See HIGH SPEED TAXIWAY).

HIGH SPEED TAXIWAY
A long radius taxiway designed and provided with lighting or marking
to define the path of aircraft, traveling at high speed (up to 60
knots), from the runway center to a point on the center of a
taxiway. Also referred to as long radius exit or turn off taxiway. The
high speed taxiway is designed to expedite aircraft turning off the
runway after landing, thus reducing runway occupancy time.

HIGH SPEED TURNOFF
(See HIGH SPEED TAXIWAY).

HIWAS
(See HAZARDOUS INFLIGHT WEATHER ADVISORY SERVICE).

HIWAS AREA
(See HAZARDOUS INFLIGHT WEATHER ADVISORY SERVICE).

HIWAS BROADCAST AREA
A geographical area of responsibility including one or more HIWAS
outlet areas assigned to an AFSS/FSS for hazardous weather advisory
broadcasting.

HIWAS OUTLET AREA
An area defined as a 150 NM radius of a HIWAS outlet, expanded as
necessary to provide coverage.

HOLDING PROCEDURE
(See HOLD PROCEDURE).

HOLD PROCEDURE
A predetermined maneuver which keeps aircraft within a specified
airspace while awaiting further clearance from air traffic
control. Also used during ground operations to keep aircraft within a
specified area or at a specified point while awaiting further
clearance from air traffic control.

HOLDING FIX
A specified fix identifiable to a pilot by NAVAID's or visual
reference to the ground used as a reference point in establishing and
maintaining the position of an aircraft while holding.

HOLDING POINT [ICAO]
A specified location, identified by visual or other means, in the
vicinity of which the position of an aircraft in flight is maintained
in accordance with air traffic control clearances.

HOLD FOR RELEASE
Used by ATC to delay an aircraft for traffic management reasons; i.e.,
weather, traffic volume, etc. Hold for release instructions (including
departure delay information) are used to inform a pilot or a
controller (either directly or through an authorized relay) that an
IFR departure clearance is not valid until a release time or
additional instructions have been received.

HOMING
Flight toward a NAVAID, without correcting for wind, by adjusting the
aircraft heading to maintain a relative bearing of zero degrees.

HOMING [ICAO]
The procedure of using the direction finding equipment of one radio
station with the emission of another radio station, where at least one
of the stations is mobile, and whereby the mobile station proceeds
continuously towards the other station.

HOVER CHECK 
Used to describe when a helicopter/VTOL aircraft requires a stabilized
hover to conduct a performance/power check prior to hover taxi, air
taxi, or takeoff. Altitude of the hover will vary based on the purpose
of the check.

HOVER TAXI
Used to describe a helicopter/VTOL aircraft movement conducted above
the surface and in ground effect at airspeeds less than approximately
20 knots. The actual height may vary, and some helicopters may require
hover taxi above 25 feet AGL to reduce ground effect turbulence or
provide clearance for cargo slingloads.

HOW DO YOU HEAR ME?

A question relating to the quality of the transmission or to determine
how well the transmission is being received.

HZ
(See HERTZ).

IAF
(See INITIAL APPROACH FIX).

IAP
(See INSTRUMENT APPROACH PROCEDURE).

ICAO
(See INTERNATIONAL CIVIL AVIATION ORGANIZATION).

ICAO [ICAO]
(See ICAO Term INTERNATIONAL CIVIL AVIATION ORGANIZATION).

IDENT
A request for a pilot to activate the aircraft transponder
identification feature. This will help the controller to confirm an
aircraft identity or to identify an aircraft.

IDENT FEATURE
The special feature in the Air Traffic Control Radar Beacon System
(ATCRBS) equipment. It is used to immediately distinguish one
displayed beacon target from other beacon targets.

IF
(See INTERMEDIATE FIX).

IFIM
(See INTERNATIONAL FLIGHT INFORMATION MANUAL).

IF NO TRANSMISSION RECEIVED FOR (TIME)
Used by ATC in radar approaches to prefix procedures which should be
followed by the pilot in event of lost communications.

IFR
(See INSTRUMENT FLIGHT RULES).

IFR AIRCRAFT
An aircraft conducting flight in accordance with instrument flight
rules.

IFR CONDITIONS
Weather conditions below the minimum for flight under visual flight
rules.

IFR DEPARTURE PROCEDURE
(See IFR TAKEOFF MINIMUMS AND DEPARTURE PROCEDURES).

IFR FLIGHT
(See IFR AIRCRAFT).

IFR LANDING MINIMUMS
(See LANDING MINIMUMS).

IFR MILITARY TRAINING ROUTES (IR)
Routes used by the Department of Defense and associated Reserve and
Air Guard units for the purpose of conducting low altitude navigation
and tactical training in both IFR and VFR weather conditions below
10,000 feet MSL at airspeeds in excess of 250 knots IAS.

IFR TAKEOFF MINIMUMS AND DEPARTURE PROCEDURES
Federal Aviation Regulations, Part 91, prescribes standard takeoff
rules for certain civil users. At some airports, obstructions or other
factors require the establishment of nonstandard takeoff minimums,
departure procedures, or both to assist pilots in avoiding obstacles
during climb to the minimum en route altitude. Those airports are
listed in NOS/DOD Instrument Approach Charts (IAP's) under a section
entitled ``IFR Takeoff Minimums and Departure Procedures.'' The
NOS/DOD IAP chart legend illustrates the symbol used to alert the
pilot to nonstandard takeoff minimums and departure procedures. When
departing IFR from such airports or from any airports where there are
no departure procedures, SID's, or ATC facilities available, pilots
should advise ATC of any departure limitations. Controllers may query
a pilot to determine acceptable departure directions, turns, or
headings after takeoff. Pilots should be familiar with the departure
procedures and must assure that their aircraft can

ILS
(See INSTRUMENT LANDING SYSTEM).

ILS CATEGORIES 
1.ILS Category I. An ILS approach procedure which provides for
approach to a height above touchdown of not less than 200 feet and
with runway visual range of not less than 1,800 feet.
2.ILS Category II. An ILS approach procedure which provides for
approach to a height above touchdown of not less than 100 feet and
with runway visual range of not less than 1,200 feet.
3.ILS Category III: IIIA. An ILS approach procedure which provides for
approach without a decision height minimum and with runway visual
range of not less than 700 feet.
 IIIB. An ILS approach procedure which provides for approach without a
decision height minimum and with runway visual range of not less than
150 feet.
 IIIC. An ILS approach procedure which provides for approach without a
decision height minimum and without runway visual range minimum.

IM
(See INNER MARKER).

IMC
(See INSTRUMENT METEOROLOGICAL CONDITIONS).

IMMEDIATELY
Used by ATC when such action compliance is required to avoid an
imminent situation.

INCERFA Uncertainty Phase) [ICAO]
A situation wherein uncertainty exists as to the safety of an aircraft
and its occupants.

INCREASE SPEED TO (SPEED)
(See SPEED ADJUSTMENT).

INERTIAL NAVIGATION SYSTEM
An RNAV system which is a form of self contained navigation. Q02

INFLIGHT REFUELING
(See AERIAL REFUELING).

INFLIGHT WEATHER ADVISORY
(See WEATHER ADVISORY).

INFORMATION REQUEST
A request originated by an FSS for information concerning an overdue
VFR aircraft.

INITIAL APPROACH FIX
The fixes depicted on instrument approach procedure charts that
identify the beginning of the initial approach segment(s).

INITIAL APPROACH SEGMENT
(See SEGMENTS OF AN INSTRUMENT APPROACH PROCEDURE).

INITIAL APPROACH SEGMENT [ICAO]
That segment of an instrument approach procedure between the initial
approach fix and the intermediate approach fix or, where applicable,
the final approach fix or point.

INLAND NAVIGATION FACILITY
A navigation aid on a North American Route at which the common route
and/or the noncommon route begins or ends.

INNER MARKER
A marker beacon used with an ILS (CAT II) precision approach located
between the middle marker and the end of the ILS runway, transmitting
a radiation pattern keyed at six dots per second and indicating to the
pilot, both aurally and visually, that he is at the designated
decision height (DH), normally 100 feet above the touchdown zone
elevation, on the ILS CAT II approach. It also marks progress during a
CAT III approach.

INNER MARKER BEACON
(See INNER MARKER).

INREQ
(See INFORMATION REQUEST).

INS
(See INERTIAL NAVIGATION SYSTEM).

INSTRUMENT APPROACH
(See INSTRUMENT APPROACH PROCEDURE).

INSTRUMENT APPROACH PROCEDURE
A series of predetermined maneuvers for the orderly transfer of an
aircraft under instrument flight conditions from the beginning of the
initial approach to a landing or to a point from which a landing may
be made visually. It is prescribed and approved for a specific airport
by competent authority.  U.S. civil standard instrument approach
procedures are approved by the FAA as prescribed under Part 97 and are
available for public use.  U.S. military standard instrument approach
procedures are approved and published by the Department of Defense.
Special instrument approach procedures are approved by the FAA for
individual operators but are not published in Part 97 for public use.

INSTRUMENT APPROACH PROCEDURE [ICAO]
A series of predetermined manoeuvres by reference to flight
instruments with specified protection from obstacles from the initial
approach fix, or where applicable, from the beginning of a defined
arrival route to a point from which a landing can be completed and
thereafter, if a landing is not completed, to a position at which
holding or en route obstacle clearance criteria apply.

INSTRUMENT APPROACH PROCEDURES CHARTS
(See AERONAUTICAL CHART).

INSTRUMENT FLIGHT RULES
Rules governing the procedures for conducting instrument flight. Also
a term used by pilots and controllers to indicate type of flight plan.

INSTRUMENT FLIGHT RULES [ICAO]
A set of rules governing the conduct of flight under instrument
meteorological conditions.

INSTRUMENT LANDING SYSTEM
A precision instrument approach system which normally consists of the
following electronic components and visual aids: Localizer.
Glideslope.  Outer Marker.  Middle Marker.  Approach Lights.

INSTRUMENT METEOROLOGICAL CONDITIONS
Meteorological conditions expressed in terms of visibility, distance
from cloud, and ceiling less than the minima specified for visual
meteorological conditions.

INSTRUMENT RUNWAY
A runway equipped with electronic and visual navigation aids for which
a precision or nonprecision approach procedure having straight in
landing minimums has been approved.

INSTRUMENT RUNWAY [ICAO]
One of the following types of runways intended for the operation of
aircraft using instrument approach procedures: a)Nonprecision Approach
Runway. An instrument runway served by visual aids and a nonvisual aid
providing at least directional guidance adequate for a straight in
approach.  b)Precision Approach Runway, Category I. An instrument
runway served by ILS and visual aids intended for operations down to
60 m (200 feet) decision height and down to an RVR of the order of 800
m.  c)Precision Approach Runway, Category II. An instrument runway
served by ILS and visual aids intended for operations down to 30 m
(100 feet) decision height and down to an RVR of the order of 400 m.
d)Precision Approach Runway, Category III. An instrument runway served
by ILS to and along the surface of the runway and: A. Intended for
operations down to an RVR of the order of 200 m (no decision height
being applicable) using visual aids during the final phase of landing;
B. Intended for operations down to an RVR of the order of 50 m (no
decision height being applicable) using visual aids for taxiing;
C. Intended for operations without reliance on visual reference for
landing or taxiing.

INTERMEDIATE APPROACH SEGMENT
(See SEGMENTS OF AN INSTRUMENT APPROACH PROCEDURE).

INTERMEDIATE APPROACH SEGMENT [ICAO]
That segment of an instrument approach procedure between either the
intermediate approach fix and the final approach fix or point, or
between the end of a reversal, race track or dead reckoning track
procedure and the final approach fix or point, as appropriate.

INTERMEDIATE FIX
The fix that identifies the beginning of the intermediate approach
segment of an instrument approach procedure. The fix is not normally
identified on the instrument approach chart as an intermediate fix
(IF).

INTERMEDIATE LANDING
On the rare occasion that this option is requested, it should be
approved. The departure center, however, must advise the ATCSCC so
that the appropriate delay is carried over and assigned at the
intermediate airport. An intermediate landing airport within the
arrival center will not be accepted without coordination with and the
approval of the ATCSCC.

INTERNATIONAL AIRPORT
Relating to international flight, it means: An airport of entry which
has been designated by the Secretary of Treasury or Commissioner of
Customs as an international airport for customs service.  A landing
rights airport at which specific permission to land must be obtained
from customs authorities in advance of contemplated use.  Airports
designated under the Convention on International Civil Aviation as an
airport for use by international commercial air transport and/or
international general aviation.

INTERNATIONAL AIRPORT [ICAO]
Any airport designated by the Contracting State in whose territory it
is situated as an airport of entry and departure for international air
traffic, where the formalities incident to customs, immigration,
public health, animal and plant quarantine and similar procedures are
carried out.

INTERNATIONAL CIVIL AVIATION ORGANIZATION [ICAO]
A specialized agency of the United Nations whose objective is to
develop the principles and techniques of international air navigation
and to foster planning and development of international civil air
transport.  ICAO Regions include: AFI African Indian Ocean Region CAR
Caribbean Region EUR European Region MID/ASIA Middle East/Asia Region
NAM North American Region NAT North Atlantic Region PAC Pacific Region
SAM South American Region

INTERNATIONAL FLIGHT INFORMATION MANUAL
A publication designed primarily as a pilot's preflight planning guide
for flights into foreign airspace and for flights returning to the
U.S. from foreign locations.

INTERROGATOR
The ground based surveillance radar beacon transmitter receiver, which
normally scans in synchronism with a primary radar, transmitting
discrete radio signals which repetitiously request all transponders on
the mode being used to reply. The replies received are mixed with the
primary radar returns and displayed on the same plan position
indicator (radar scope). Also, applied to the airborne element of the
TACAN/DME system.

INTERSECTING RUNWAYS
Two or more runways which cross or meet within their lengths.

INTERSECTION
A point defined by any combination of courses, radials, or bearings of
two or more navigational aids.  Used to describe the point where two
runways, a runway and a taxiway, or two taxiways cross or meet.

INTERSECTION DEPARTURE
A departure from any runway intersection except the end of the runway.

INTERSECTION TAKEOFF
(See INTERSECTION DEPARTURE).

IR
(See IFR MILITARY TRAINING ROUTES).

I SAY AGAIN
The message will be repeated.

JAMMING
Electronic or mechanical interference which may disrupt the display of
aircraft on radar or the transmission/reception of radio
communications/navigation.

JET BLAST
Jet engine exhaust (thrust stream turbulence).

JET ROUTE
A route designed to serve aircraft operations from 18,000 feet MSL up
to and including flight level 450. The routes are referred to as ``J''
routes with numbering to identify the designated route; e.g., J105.

JET STREAM
A migrating stream of high speed winds present at high altitudes.

JETTISONING OF EXTERNAL STORES
Airborne release of external stores; e.g., tiptanks, ordnance.

JOINT USE RESTRICTED AREA
(See RESTRICTED AREA).

KNOWN TRAFFIC
With respect to ATC clearances, means aircraft whose altitude,
position, and intentions are known to ATC.

LAA
(See LOCAL AIRPORT ADVISORY).

LAAS
(See LOW ALTITUDE ALERT SYSTEM).

LANDING AREA
Any locality either on land, water, or structures, including
airports/heliports and intermediate landing fields, which is used, or
intended to be used, for the landing and takeoff of aircraft whether
or not facilities are provided for the shelter, servicing, or for
receiving or discharging passengers or cargo.

LANDING AREA [ICAO]
That part of a movement area intended for the landing or takeoff of
aircraft.

LANDING DIRECTION INDICATOR
A device which visually indicates the direction in which landings and
takeoffs should be made.

LANDING DISTANCE AVAILABLE [ICAO]
The length of runway which is declared available and suitable for the
ground run of an aeroplane landing.

LANDING MINIMUMS
The minimum visibility prescribed for landing a civil aircraft while
using an instrument approach procedure. The minimum applies with other
limitations set forth in Part 91 with respect to the Minimum Descent
Altitude (MDA) or Decision Height (DH) prescribed in the instrument
approach procedures as follows: Straight in landing minimums. A
statement of MDA and visibility, or DH and visibility, required for a
straight in landing on a specified runway, or Circling minimums. A
statement of MDA and visibility required for the circle to land
maneuver.

LANDING ROLL
The distance from the point of touchdown to the point where the
aircraft can be brought to a stop or exit the runway.

LANDING SEQUENCE
The order in which aircraft are positioned for landing.

LAST ASSIGNED ALTITUDE
The last altitude/flight level assigned by ATC and acknowledged by the
pilot.

LATERAL SEPARATION
The lateral spacing of aircraft at the same altitude by requiring
operation on different routes or in different geographical locations.

LDA
(See LOCALIZER TYPE DIRECTIONAL AID).

LDA [ICAO]
(See ICAO Term LANDING DISTANCE AVAILABLE).

LF
(See LOW FREQUENCY).

LIGHTED AIRPORT
An airport where runway and obstruction lighting is available.

LIGHT GUN
A handheld directional light signaling device which emits a brilliant
narrow beam of white, green, or red light as selected by the tower
controller. The color and type of light transmitted can be used to
approve or disapprove anticipated pilot actions where radio
communication is not available. The light gun is used for controlling
traffic operating in the vicinity of the airport and on the airport
movement area.

LOCALIZER
The component of an ILS which provides course guidance to the runway.

LOCALIZER COURSE [ICAO]
The locus of points, in any given horizontal plane, at which the DDM
(difference in depth of modulation) is zero.

LOCALIZER TYPE DIRECTIONAL AID
A NAVAID used for nonprecision instrument approaches with utility and
accuracy comparable to a localizer but which is not a part of a
complete ILS and is not aligned with the runway.

LOCALIZER USABLE DISTANCE
The maximum distance from the localizer transmitter at a specified
altitude, as verified by flight inspection, at which reliable course
information is continuously received.

LOCAL AIRPORT ADVISORY [LAA]
A service provided by flight service stations or the military at
airports not serviced by an operating control tower. This service
consists of providing information to arriving and departing aircraft
concerning wind direction and speed, favored runway, altimeter
setting, pertinent known traffic, pertinent known field conditions,
airport taxi routes and traffic patterns, and authorized instrument
approach procedures. This information is advisory in nature and does
not constitute an ATC clearance.

LOCAL TRAFFIC
Aircraft operating in the traffic pattern or within sight of the
tower, or aircraft known to be departing or arriving from flight in
local practice areas, or aircraft executing practice instrument
approaches at the airport.

LOCATOR [ICAO]
An LM/MF NDB used as an aid to final approach.

LONGITUDINAL SEPARATION
The longitudinal spacing of aircraft at the same altitude by a minimum
distance expressed in units of time or miles.

LONG RANGE NAVIGATION
(See LORAN).

LORAN
An electronic navigational system by which hyperbolic lines of
position are determined by measuring the difference in the time of
reception of synchronized pulse signals from two fixed
transmitters. Loran A operates in the 1750-1950 kHz frequency
band. Loran C and D operate in the 100-110 kHz frequency band.

LOST COMMUNICATIONS
Loss of the ability to communicate by radio. Aircraft are sometimes
referred to as NORDO (No Radio). Standard pilot procedures are
specified in Part 91. Radar controllers issue procedures for pilots to
follow in the event of lost communications during a radar approach
when weather reports indicate that an aircraft will likely encounter
IFR weather conditions during the approach.

LOW ALTITUDE AIRWAY STRUCTURE
The network of airways serving aircraft operations up to but not
including 18,000 feet MSL.

LOW ALTITUDE ALERT, CHECK YOUR ALTITUDE IMMEDIATELY
(See SAFETY ALERT).

LOW ALTITUDE ALERT SYSTEM
An automated function of the TPX-42 that alerts the controller when a
Mode C transponder equipped aircraft on an IFR flight plan is below a
predetermined minimum safe altitude. If requested by the pilot, LAAS
monitoring is also available to VFR Mode C transponder equipped
aircraft.

LOW APPROACH
An approach over an airport or runway following an instrument approach
or a VFR approach including the go around maneuver where the pilot
intentionally does not make contact with the runway.

LOW FREQUENCY
The frequency band between 30 and 300 kHz.

MAA
(See MAXIMUM AUTHORIZED ALTITUDE).

MACH NUMBER
The ratio of true airspeed to the speed of sound; e.g., MACH .82, MACH
1.6.

MACH TECHNIQUE [ICAO]
Describes a control technique used by air traffic control whereby
turbojet aircraft operating successively along suitable routes are
cleared to maintain appropriate MACH numbers for a relevant portion of
the en route phase of flight. The principle objective is to

MAINTAIN
Concerning altitude/flight level, the term means to remain at the
altitude/flight level specified. The phrase ``climb and'' or ``descend
and'' normally precedes ``maintain'' and the altitude assignment;
e.g., ``descend and maintain 5,000.''  Concerning other ATC
instructions, the term is used in its literal sense; e.g., maintain
VFR.

MAKE SHORT APPROACH
Used by ATC to inform a pilot to alter his traffic pattern so as to
make a short final approach.

MANDATORY ALTITUDE
An altitude depicted on an instrument Approach Procedure Chart
requiring the aircraft to maintain altitude at the depicted value.

MAP
(See MISSED APPROACH POINT).

MARKER BEACON
An electronic navigation facility transmitting a 75 mHz vertical fan
or boneshaped radiation pattern. Marker beacons are identified by
their modulation frequency and keying code, and when received by
compatible airborne equipment, indicate to the pilot, both aurally and
visually, that he is passing over the facility.

MARSA
(See MILITARY AUTHORITY ASSUMES RESPONSIBILITY FOR SEPARATION OF
AIRCRAFT).

MAXIMUM AUTHORIZED ALTITUDE
A published altitude representing the maximum usable altitude or
flight level for an airspace structure or route segment. It is the
highest altitude on a Federal airway, jet route, area navigation low
or high route, or other direct route for which an MEA is designated in
Part 95 at which adequate reception of navigation aid signals is
assured.

MAYDAY
The international radiotelephony distress signal. When repeated three
times, it indicates imminent and grave danger and that immediate
assistance is requested.

MCA
(See MINIMUM CROSSING ALTITUDE).

MDA
(See MINIMUM DESCENT ALTITUDE).

MEA
(See MINIMUM EN ROUTE IFR ALTITUDE).

METEOROLOGICAL IMPACT STATEMENT
An unscheduled planning forecast describing conditions expected to
begin within 4 to 12 hours which may impact the flow of air traffic in
a specific center's (ARTCC) area.

METER FIX TIME/SLOT TIME
A calculated time to depart the meter fix in order to cross the vertex
at the ACLT. This time reflects descent speed adjustment and any
applicable time that must be absorbed prior to crossing the meter fix.

METER LIST DISPLAY INTERVAL
A dynamic parameter which controls the number of minutes prior to the
flight plan calculated time of arrival at the meter fix for each
aircraft, at which time the TCLT is frozen and becomes an ACLT; i.e.,
the VTA is updated and consequently the TCLT modified as appropriate
until frozen at which time updating is suspended and an ACLT is
assigned. When frozen, the flight entry is inserted into the arrival
sector's meter list for display on the sector PVD. MLDI is used if
filed true airspeed is less than or equal to freeze speed parameters
(FSPD).

METERING
A method of time regulating arrival traffic flow into a terminal area
so as not to exceed a predetermined terminal acceptance rate.

METERING AIRPORTS
Airports adapted for metering and for which optimum flight paths are
defined. A maximum of 15 airports may be adapted.

METERING FIX
A fix along an established route from over which aircraft will be
metered prior to entering terminal airspace. Normally, this fix should
be established at a distance from the airport which will facilitate a
profile descent 10,000 feet above airport elevation [AAE] or above.

METERING POSITION(S)
Adapted PVD's and associated ``D'' positions eligible for display of a
metering position list. A maximum of four PVD's may be adapted.

METERING POSITION LIST
An ordered list of data on arrivals for a selected metering airport
displayed on a metering position PVD.

MFT
(See METER FIX TIME/SLOT TIME).

MHA
(See MINIMUM HOLDING ALTITUDE).

MIA
(See MINIMUM IFR ALTITUDES).

MICROBURST
A small downburst with outbursts of damaging winds extending 2.5 miles
or less. In spite of its small horizontal scale, an intense microburst
could induce wind speeds as high as 150 knots

MICROWAVE LANDING SYSTEM
A precision instrument approach system operating in the microwave
spectrum which normally consists of the following components: Azimuth
Station.  Elevation Station.  Precision Distance Measuring Equipment.

MIDDLE COMPASS LOCATOR
(See COMPASS LOCATOR).

MIDDLE MARKER
A marker beacon that defines a point along the glideslope of an ILS
normally located at or near the point of decision height (ILS Category
I). It is keyed to transmit alternate dots and dashes, with the
alternate dots and dashes keyed at the rate of 95 dot/dash
combinations per minute on a 1300 Hz tone, which is received aurally
and visually by compatible airborne equipment.

MID RVR
(See VISIBILITY).

MILES IN TRAIL
A specified distance between aircraft, normally, in the same stratum
associated with the same destination or route of flight.

MILITARY AUTHORITY ASSUMES RESPONSIBILITY FOR SEPARATION OF AIRCRAFT
A condition whereby the military services involved assume
responsibility for separation between participating military aircraft
in the ATC system. It is used only for required IFR operations which
are specified in letters of agreement or other appropriate FAA or
military documents.

MILITARY OPERATIONS AREA
(See SPECIAL USE AIRSPACE).

MILITARY TRAINING ROUTES
Airspace of defined vertical and lateral dimensions established for
the conduct of military flight training at airspeeds in excess of 250
knots IAS.

MINIMA
(See MINIMUMS).

MINIMUM CROSSING ALTITUDE
The lowest altitude at certain fixes at which an aircraft must cross
when proceeding in the direction of a higher minimum en route IFR
altitude (MEA).

MINIMUM DESCENT ALTITUDE
The lowest altitude, expressed in feet above mean sea level, to which
descent is authorized on final approach or during circle to land
maneuvering in execution of a standard instrument approach procedure
where no electronic glideslope is provided.

MINIMUM EN ROUTE IFR ALTITUDE
The lowest published altitude between radio fixes which assures
acceptable navigational signal coverage and meets obstacle clearance
requirements between those fixes. The MEA prescribed for a Federal
airway or segment thereof, area navigation low or high route, or other
direct route applies to the entire width of the airway, segment, or
route between the radio fixes defining the airway, segment, or route.

MINIMUM FUEL
Indicates that an aircraft's fuel supply has reached a state where,
upon reaching the destination, it can accept little or no delay. This
is not an emergency situation but merely indicates an emergency
situation is possible should any undue delay occur.

MINIMUM HOLDING ALTITUDE
The lowest altitude prescribed for a holding pattern which assures
navigational signal coverage, communications, and meets obstacle
clearance requirements.

MINIMUM IFR ALTITUDES
Minimum altitudes for IFR operations as prescribed in Part 91. These
altitudes are published on aeronautical charts and prescribed in Part
95 for airways and routes, and in Part 97 for standard instrument
approach procedures. If no applicable minimum altitude is prescribed
in FAR 95 or FAR 97, the following minimum IFR altitude applies: In
designated mountainous areas, 2,000 feet above the highest obstacle
within a horizontal distance of 4 nautical miles from the course to be
flown; or Other than mountainous areas, 1,000 feet above the highest
obstacle within a horizontal distance of 4 nautical miles from the
course to be flown; or As otherwise authorized by the Administrator or
assigned by ATC.

MINIMUM NAVIGATION PERFORMANCE SPECIFICATION
A set of standards which require aircraft to have a minimum navigation
performance capability in order to operate in MNPS designated
airspace. In addition, aircraft must be certified by their State of
Registry for MNPS operation.

MINIMUM NAVIGATION PERFORMANCE SPECIFICATIONS AIRSPACE
Designated airspace in which MNPS procedures are applied between MNPS
certified and equipped aircraft. Under certain conditions, non MNPS
aircraft can operate in MNPSA. However, standard oceanic separation
minima is provided between the non MNPS aircraft and other
traffic. Currently, the only designated MNPSA is described as follows:
Between FL 275 and FL 400; Between latitudes 27- N and the North Pole;
In the east, the eastern boundaries of the CTA's Santa Maria Oceanic,
Shanwick Oceanic, and Reykjavik; In the west, the western boundaries
of CTA's Reykjavik and Gander Oceanic and New York Oceanic excluding
the area west of 60- W and south of 38- 30' N.

MINIMUM OBSTRUCTION CLEARANCE ALTITUDE
The lowest published altitude in effect between radio fixes on VOR
airways, off airway routes, or route segments which meets obstacle
clearance requirements for the entire route segment and which assures
acceptable navigational signal coverage only within 25 statute (22
nautical) miles of a VOR.

MINIMUM RECEPTION ALTITUDE
The lowest altitude at which an intersection can be determined. 

MINIMUM SAFE ALTITUDE
The minimum altitude specified in Part 91 for various aircraft
operations.  Altitudes depicted on approach charts which provide at
least 1,000 feet of obstacle clearance for emergency use within a
specified distance from the navigation facility upon which a procedure
is predicated. These altitudes will be identified as Minimum Sector
Altitudes or Emergency Safe Altitudes and are established as follows:
a. Minimum Sector Altitudes. Altitudes depicted on approach charts
which provide at least 1,000 feet of obstacle clearance within a
25-mile radius of the navigation facility upon which the procedure is
predicated. Sectors depicted on approach charts must be at least 90
degrees in scope. These altitudes are for emergency use only and do
not necessarily assure acceptable navigational signal coverage.
b. Emergency Safe Altitudes. Altitudes depicted on approach charts
which provide at least 1,000 feet of obstacle clearance in
nonmountainous areas and 2,000 feet of obstacle clearance in
designated mountainous areas within a 100-mile radius of the
navigation facility upon which the procedure is predicated and
normally used only in military procedures. These altitudes are
identified on published procedures as ``Emergency Safe Altitudes.''

MINIMUM SAFE ALTITUDE WARNING
A function of the ARTS III computer that aids the controller by
alerting him when a tracked Mode C equipped aircraft is below or is
predicted by the computer to go below a predetermined minimum safe
altitude.

MINIMUM SECTOR ALTITUDE [ICAO]
The lowest altitude which may be used under emergency conditions which
will provide a minimum clearance of 300 m (1,000 feet) above all
obstacles located in an area contained within a sector of a circle of
46 km (25 NM) radius centered on a radio aid to navigation.

MINIMUMS
Weather condition requirements established for a particular operation
or type of operation; e.g., IFR takeoff or landing, alternate airport
for IFR flight plans, VFR flight, etc.

MINIMUM VECTORING ALTITUDE
The lowest MSL altitude at which an IFR aircraft will be vectored by a
radar controller, except as otherwise authorized for radar approaches,
departures, and missed approaches. The altitude meets IFR obstacle
clearance criteria. It may be lower than the published MEA along an
airway or J route segment. It may be utilized for radar vectoring only
upon the controller's determination that an adequate radar return is
being received from the aircraft being controlled. Charts depicting
minimum vectoring altitudes are normally available only to the
controllers and not to pilots.

MINUTES IN TRAIL
A specified interval between aircraft expressed in time. This method
would more likely be utilized regardless of altitude.

MIS
(See METEOROLOGICAL IMPACT STATEMENT).

MISSED APPROACH
A maneuver conducted by a pilot when an instrument approach cannot be
completed to a landing. The route of flight and altitude are shown on
instrument approach procedure charts. A pilot executing a missed
approach prior to the Missed Approach Point (MAP) must continue along
the final approach to the MAP. The pilot may climb immediately to the
altitude specified in the missed approach procedure.  A term used by
the pilot to inform ATC that he is executing the missed approach.  At
locations where ATC radar service is provided, the pilot should
conform to radar vectors when provided by ATC in lieu of the published
missed approach procedure.

MISSED APPROACH POINT
A point prescribed in each instrument approach procedure at which a
missed approach procedure shall be executed if the required visual
reference does not exist.

MISSED APPROACH PROCEDURE [ICAO]
The procedure to be followed if the approach cannot be continued.

MISSED APPROACH SEGMENT
(See SEGMENTS OF AN INSTRUMENT APPROACH PROCEDURE).

MLDI
(See METER LIST DISPLAY INTERVAL).

MLS
(See MICROWAVE LANDING SYSTEM).

MLS CATEGORIES
MLS Category I. An MLS approach procedure which provides for an
approach to a height above touchdown of not less than 200 feet and a
runway visual range of not less than 1,800 feet.
MLS Category II. Undefined until data gathering/analysis completion.
MLS Category III. Undefined until data gathering/analysis completion.

MM
(See MIDDLE MARKER).

MNPS
(See MINIMUM PERFORMANCE SPECIFICATION).

MNPSA
(See MINIMUM PERFORMANCE SPECIFICATIONS AIRSPACE).

MOA
(See MILITARY OPERATIONS AREA).

MOCA
(See MINIMUM OBSTRUCTION CLEARANCE ALTITUDE).

MODE
The letter or number assigned to a specific pulse spacing of radio
signals transmitted or received by ground interrogator or airborne
transponder components of the Air Traffic Control Radar Beacon System
(ATCRBS). Mode A (military Mode 3) and Mode C (altitude reporting) are
used in air traffic control.

MODE (SSR MODE) [ICAO]
The letter or number assigned to a specific pulse spacing of the
interrogation signals transmitted by an interrogator. There are 4
modes, A, B, C and D specified in Annex 10, corresponding to four
different interrogation pulse spacings.

MODE C INTRUDER ALERT
A function of certain air traffic control automated systems designed
to alert radar controllers to existing or pending situations between a
tracked target (known IFR or VFR aircraft) and an untracked target
(unknown IFR or VFR aircraft) that requires immediate
attention/action.

MONITOR
(When used with communication transfer) listen on a specific frequency
and stand by for instructions. Under normal circumstances do not
establish communications.

MOVEMENT AREA
The runways, taxiways, and other areas of an airport/heliport which
are utilized for taxiing/hover taxiing, air taxiing, takeoff, and
landing of aircraft, exclusive of loading ramps and parking areas. At
those airports/heliports with a tower, specific approval for entry
onto the movement area must be obtained from ATC.

MOVEMENT AREA [ICAO]
That part of an aerodrome to be used for the takeoff, landing and
taxiing of aircraft, consisting of the manoeuvring area and the
apron(s).

MOVING TARGET INDICATOR
An electronic device which will permit radar scope presentation only
from targets which are in motion. A partial remedy for ground clutter.

MRA
(See MINIMUM RECEPTION ALTITUDE).

MSA
(See MINIMUM SAFE ALTITUDE).

MSAW
(See MINIMUM SAFE ALTITUDE WARNING).

MTI
(See MOVING TARGET INDICATOR).

MTR
(See MILITARY TRAINING ROUTES).

MULTICOM
A mobile service not open to public correspondence used to provide
communications essential to conduct the activities being performed by
or directed from private aircraft.

MULTIPLE RUNWAYS
The utilization of a dedicated arrival runway(s) for departures and a
dedicated departure runway(s) for arrivals when feasible to reduce
delays and enhance capacity.

MVA
(See MINIMUM VECTORING ALTITUDE).

NAS
(See NATIONAL AIRSPACE SYSTEM).

NAS STAGE A
The en route ATC system's radar, computers and computer programs,
controller plan view displays (PVDs/Radar Scopes), input/output
devices, and the related communications equipment which are integrated
to form the heart of the automated IFR air traffic control
system. This equipment performs Flight Data Processing (FDP) and Radar
Data Processing (RDP). It interfaces with automated terminal systems
and is used in the control of en route IFR aircraft.

NATIONAL AIRSPACE SYSTEM
The common network of U.S. airspace; air navigation facilities,
equipment and services, airports or landing areas; aeronautical
charts, information and services; rules, regulations and procedures,
technical information, and manpower and material. Included are system
components shared jointly with the military.

NATIONAL BEACON CODE ALLOCATION PLAN AIRSPACE
Airspace over United States territory located within the North
American continent between Canada and Mexico, including adjacent
territorial waters outward to about boundaries of oceanic control
areas (CTA)/Flight Information Regions (FIR).

NATIONAL FLIGHT DATA CENTER
A facility in Washington D.C., established by FAA to operate a central
aeronautical information service for the collection, validation, and
dissemination of aeronautical data in support of the activities of
government, industry, and the aviation community. The information is
published in the National Flight Data Digest.

NATIONAL FLIGHT DATA DIGEST
A daily (except weekends and Federal holidays) publication of flight
information appropriate to aeronautical charts, aeronautical
publications, Notices to Airmen, or other media serving the purpose of
providing operational flight data essential to safe and efficient
aircraft operations.

NATIONAL SEARCH AND RESCUE PLAN
An interagency agreement which provides for the effective utilization
of all available facilities in all types of search and rescue
missions.

NAVAID
(See NAVIGATIONAL AID).

NAVAID CLASSES
VOR, VORTAC, and TACAN aids are classed according to their operational
use. The three classes of NAVAID's are: Terminal.  Low altitude.  High
altitude.

NAVIGABLE AIRSPACE
Airspace at and above the minimum flight altitudes prescribed in the
FAR's including airspace needed for safe takeoff and landing.

NAVIGATIONAL AID
Any visual or electronic device airborne or on the surface which
provides point to point guidance information or position data to
aircraft in flight.

NBCAP AIRSPACE
(See NATIONAL BEACON CODE ALLOCATION PLAN AIRSPACE).

NDB
(See NONDIRECTIONAL BEACON).

NEGATIVE
``No,'' or ``permission not granted,'' or ``that is not correct.''

NEGATIVE CONTACT
Used by pilots to inform ATC that:
Previously issued traffic is not in sight. It may be followed by the
pilot's request for the controller to provide assistance in avoiding
the traffic.  They were unable to contact ATC on a particular
frequency.

NFDC
(See NATIONAL FLIGHT DATA CENTER).

NFDD
(See NATIONAL FLIGHT DATA DIGEST).

NIGHT
The time between the end of evening civil twilight and the beginning
of morning civil twilight, as published in the American Air Almanac,
converted to local time.

NIGHT [ICAO]
The hours between the end of evening civil twilight and the beginning
of morning civil twilight or such other period between sunset and
sunrise as may be specified by the appropriate authority.

NO GYRO APPROACH
A radar approach/vector provided in case of a malfunctioning gyro
compass or directional gyro. Instead of providing the pilot with
headings to be flown, the controller observes the radar track and
issues control instructions ``turn right/left'' or ``stop turn'' as
appropriate.

NO GYRO VECTOR
(See NO GYRO APPROACH).

NONAPPROACH CONTROL TOWER
Authorizes aircraft to land or takeoff at the airport controlled by
the tower or to transit the Class D airspace. The primary function of
a nonapproach control tower is the sequencing of aircraft in the
traffic pattern and on the landing area. Nonapproach control towers
also separate aircraft operating under instrument flight rules
clearances from approach controls and centers. They provide ground
control services to aircraft, vehicles, personnel, and equipment on
the airport movement area.

NONCOMMON ROUTE/PORTION
That segment of a North American Route between the inland navigation
facility and a designated North American terminal.

NONCOMPOSITE SEPARATION
Separation in accordance with minima other than the composite
separation minimum specified for the area concerned.

NONDIRECTIONAL BEACON
An L/MF or UHF radio beacon transmitting nondirectional signals
whereby the pilot of an aircraft equipped with direction finding
equipment can determine his bearing to or from the radio beacon and
``home'' on or track to or from the station. When the radio beacon is
installed in conjunction with the Instrument Landing System marker, it
is normally called a Compass Locator.

NONMOVEMENT AREAS
Taxiways and apron (ramp) areas not under the control of air traffic.

NONPRECISION APPROACH
(See NONPRECISION APPROACH PROCEDURE).

NONPRECISION APPROACH PROCEDURE
A standard instrument approach procedure in which no electronic
glideslope is provided; e.g., VOR, TACAN, NDB, LOC, ASR, LDA, or SDF
approaches.

NONRADAR
Precedes other terms and generally means without the use of radar,
such as: Nonradar Approach. Used to describe instrument approaches for
which course guidance on final approach is not provided by ground
based precision or surveillance radar. Radar vectors to the final
approach course may or may not be provided by ATC. Examples of
nonradar approaches are VOR, NDB, TACAN, and ILS/MLS approaches.
Nonradar Approach Control. An ATC facility providing approach control
service without the use of radar.  Nonradar Arrival. An aircraft
arriving at an airport without radar service or at an airport served
by a radar facility and radar contact has not been established or has
been terminated due to a lack of radar service to the airport.
Nonradar Route. A flight path or route over which the pilot is
performing his own navigation. The pilot may be receiving radar
separation, radar monitoring, or other ATC services while on a
nonradar route.  Nonradar Separation. The spacing of aircraft in
accordance with established minima without the use of radar; e.g.,
vertical, lateral, or longitudinal separation.

NONRADAR SEPARATION [ICAO]
The separation used when aircraft position information is derived from
sources other than radar.

NOPAC
(See NORTH PACIFIC).

NORDO
(See LOST COMMUNICATIONS).

NORTH AMERICAN ROUTE
A numerically coded route preplanned over existing airway and route
systems to and from specific coastal fixes serving the North
Atlantic. North American Routes consist of the following: Common
Route/Portion. That segment of a North American Route between the
inland navigation facility and the coastal fix.  NonCommon
Route/Portion. That segment of a North American Route between the
inland navigation facility and a designated North American terminal.
Inland Navigation Facility. A navigation aid on a North American Route
at which the common route and/or the noncommon route begins or ends.
Coastal Fix. A navigation aid or intersection where an aircraft
transitions between the domestic route structure and the oceanic route
structure.

NORTH MARK
A beacon data block sent by the host computer to be displayed by the
ARTS on a 360 degree bearing at a locally selected radar azimuth and
distance. The North Mark is used to ensure correct range/azimuth
orientation during periods of CENRAP.

NORTH PACIFIC
An organized route system between the Alaskan west coast and Japan.

NOTAM
(See NOTICE TO AIRMEN).

NOTICE TO AIRMEN
A notice containing information (not known sufficiently in advance to
publicize by other means) concerning the establishment, condition, or
change in any component (facility, service, or procedure of, or hazard
in the National Airspace System) the timely knowledge of which is
essential to personnel concerned with flight operations.

NOTAM(D).  A NOTAM given (in addition to local dissemination) distant
dissemination beyond the area of responsibility of the Flight Service
Station. These NOTAM's will be stored and available until canceled.

NOTAM(L). A NOTAM given local dissemination by voice and other means,
such as telautograph and telephone, to satisfy local user
requirements.  FDC NOTAM. A NOTAM regulatory in nature, transmitted by
USNOF and given system wide dissemination.

NOTAM [ICAO]
A notice containing information concerning the establishment,
condition or change in any aeronautical facility, service, procedure
or hazard, the timely knowledge of which is essential to personnel
concerned with flight operations.  Class I Distribution. Distribution
by means of telecommunication.  Class II Distribution. Distribution by
means other than telecommunications.

NOTICES TO AIRMEN PUBLICATION
A publication issued every 14 days, designed primarily for the pilot,
which contains current NOTAM information considered essential to the
safety of flight as well as supplemental data to other aeronautical
publications. The contraction NTAP is used in NOTAM text.

NTAP
(See NOTICES TO AIRMEN PUBLICATION).

NUMEROUS TARGETS VICINITY (LOCATION)
A traffic advisory issued by ATC to advise pilots that targets on the
radar scope are too numerous to issue individually.

OALT
(See OPERATIONAL ACCEPTABLE LEVEL OF TRAFFIC).

OBSTACLE
An existing object, object of natural growth, or terrain at a fixed
geographical location or which may be expected at a fixed location
within a prescribed area with reference to which vertical clearance is
or must be provided during flight operation.

OBSTACLE FREE ZONE
The OFZ is a three dimensional volume of airspace which protects for
the transition of aircraft to and from the runway.  The OFZ clearing
standard precludes taxiing and parked airplanes and object
penetrations, except for frangible NAVAID locations that are fixed by
function.  Additionally, vehicles, equipment, and personnel may be
authorized by air traffic control to enter the area using the
provisions of Order 7110.65, Air Traffic Control, paragraph 3-5.  The
runway OFZ and when applicable, the inner-approach OFZ, and the
inner-transitional OFZ, comprise the OFZ.  Runway OFZ. The runway OFZ
is a defined volume of airspace centered above the runway.  The runway
OFZ is the airspace above a surface whose elevation at any point is
the same as the elevation of the nearest point on the runway
centerline.  The runway OFZ extends 200 feet beyond each end of the
runway.  The width is as follows: (a)For runways serving large
airplanes, the greater of:
  (1)400 feet, or
  (2)180 feet, plus the wingspan of the most demanding airplane, plus
20 feet per 1,000 feet of airport elevation.
(b))For runways serving only small airplanes:
  (1)300 feet for precision instrument runways.
  (2)250 feet for other runways serving small airplanes with approach
speeds of 50 knots, or more.
  (3)120 feet for other runways serving small airplanes with approach
speeds of less than 50 knots.  Inner-approach OFZ. The inner-approach
OFZ is a defined volume of airspace centered on the approach area.
The inner-approach OFZ applies only to runways with an approach
lighting system.  The inner-approach OFZ begins 200 feet from the
runway threshold at the same elevation as the runway threshold and
extends 200 feet beyond the last light unit in the approach lighting
system.  The width of the inner-approach OFZ is the same as the runway
OFZ and rises at a slope of 50 (horizontal) to 1 (vertical) from the
beginning.  Inner-transitional OFZ. The inner transitional surface OFZ
is a defined volume of airspace along the sides of the runway and
inner-approach OFZ and applies only to precision instrument runways.

OBSTRUCTION
Any object/obstacle exceeding the obstruction standards specified by
Part 77, Subpart C.

OBSTRUCTION LIGHT
A light or one of a group of lights, usually red or white, frequently
mounted on a surface structure or natural terrain to warn pilots of
the presence of an obstruction.

OCEANIC AIRSPACE
Airspace over the oceans of the world, considered international
airspace, where oceanic separation and procedures per the
International Civil Aviation Organization are applied. Responsibility
for the provisions of air traffic control service in this airspace is
delegated to various countries, based generally upon geographic
proximity and the availability of the required resources.

OCEANIC DISPLAY AND PLANNING SYSTEM
An automated digital display system which provides flight data
processing, conflict probe, and situation display for oceanic air
traffic control.

OCEANIC NAVIGATIONAL ERROR REPORT
A report filed when an aircraft exiting oceanic airspace has been
observed by radar to be off course. ONER reporting parameters and
procedures are contained in Order 7110.82, Monitoring of Navigational
Performance In Oceanic Areas.

OCEANIC PUBLISHED ROUTE
A route established in international airspace and charted or described
in flight information publications, such as Route Charts, DOD Enroute
Charts, Chart Supplements, NOTAM's, and Track Messages.

OCEANIC TRANSITION ROUTE
An ATS route established for the purpose of transitioning aircraft
to/from an organized track system.

ODAPS
(See OCEANIC DISPLAY AND PLANNING SYSTEM).

OFF COURSE
A term used to describe a situation where an aircraft has reported a
position fix or is observed on radar at a point not on the ATC
approved route of flight.

OFFSHORE CONTROL AREA
That portion of airspace between the U.S 12-mile limit and the oceanic
CTA/FIR boundary within which air traffic control is exercised. These
areas are established to permit the application of domestic procedures
in the provision of air traffic control services. Offshore control
area is generally synonymous with Federal Aviation Regulations, Part
71, Subpart E, ``Control Areas and Control Area Extensions.''

OFF ROUTE VECTOR
A vector by ATC which takes an aircraft off a previously assigned
route. Altitudes assigned by ATC during such vectors provide required
obstacle clearance.

OFFSET PARALLEL RUNWAYS
Staggered runways having centerlines which are parallel.

OFT
(See OUTER FIX TIME).

OM
(See OUTER MARKER).

OMEGA
An RNAV system designed for long range navigation based upon ground
based electronic navigational aid signals.

ONER
(See OCEANIC NAVIGATIONAL ERROR REPORT).

OPERATIONAL
(See DUE REGARD).

ON COURSE
Used to indicate that an aircraft is established on the route
centerline.  Used by ATC to advise a pilot making a radar approach
that his aircraft is lined up on the final approach course.

ON COURSE INDICATION
An indication on an instrument, which provides the pilot a visual
means of determining that the aircraft is located on the centerline of
a given navigational track, or an indication on a radar scope that an
aircraft is on a given track.

OPERATIONAL ACCEPTABLE LEVEL OF TRAFFIC
An air traffic activity level associated with the designed capacity
for a sector or airport. The OALT considers dynamic changes in
staffing, personnel experience levels, equipment outages, operational
configurations, weather, traffic complexity, aircraft performance
mixtures, transitioning flights, adjacent airspace, handoff/point out
responsibilities, and other factors that may affect an air traffic
operational position or system element. The OALT is normally
considered to be the total number of aircraft that any air traffic
functional position can accommodate for a defined period of time under
a given set of circumstances.

OPPOSITE DIRECTION AIRCRAFT
Aircraft are operating in opposite directions when:
They are following the same track in reciprocal directions; or
Their tracks are parallel and the aircraft are flying in reciprocal
directions; or Their tracks intersect at an angle of more than 135«.

OPTION APPROACH
An approach requested and conducted by a pilot which will result in
either a touch and go, missed approach, low approach, stop and go, or
full stop landing.

ORGANIZED TRACK SYSTEM
A movable system of oceanic tracks that traverses the North Atlantic
between Europe and North America the physical position of which is
determined twice daily taking the best advantage of the winds aloft.

ORGANIZED TRACK SYSTEM
A series of ATS routes which are fixed and charted; i.e., CEP, NOPAC,
or flexible and described by NOTAM; i.e., NAT TRACK MESSAGE.

OTR
(See OCEANIC TRANSITION ROUTE).

OTS
(See ORGANIZED TRACK SYSTEM).

OUT
The conversation is ended and no response is expected.

OUTER AREA (associated with  Class C airspace)
Nonregulatory airspace surrounding designated Class C airspace
airports wherein ATC provides radar vectoring and sequencing on a full
time basis for all IFR and participating VFR aircraft. The service
provided in the outer area is called Class C service which includes:
IFR/IFR standard IFR separation; IFR/VFR traffic advisories and
conflict resolution; and VFR/VFR traffic advisories and, as
appropriate, safety alerts. The normal radius will be 20 nautical
miles with some variations based on site specific requirements. The
outer area extends outward from the primary Class C airspace airport
and extends from the lower limits of radar/radio coverage up to the
ceiling of the approach control's delegated airspace excluding the
Class C charted area and other airspace as appropriate.

OUTER COMPASS LOCATOR
(See COMPASS LOCATOR).

OUTER FIX
A general term used within ATC to describe fixes in the terminal area,
other than the final approach fix. Aircraft are normally cleared to
these fixes by an Air Route Traffic Control Center or an Approach
Control Facility. Aircraft are normally cleared from these fixes to
the final approach fix or final approach course.

OUTER FIX
An adapted fix along the converted route of flight, prior to the meter
fix, for which crossing times are calculated and displayed in the
metering position list.

OUTER FIX TIME
A calculated time to depart the outer fix in order to cross the vertex
at the ACLT. The time reflects descent speed adjustments and any
applicable delay time that must be absorbed prior to crossing the
meter fix.

OUTER MARKER
A marker beacon at or near the glideslope intercept altitude of an ILS
approach. It is keyed to transmit two dashes per second on a 400 Hz
tone, which is received aurally and visually by compatible airborne
equipment. The OM is normally located four to seven miles from the
runway threshold on the extended centerline of the runway.

OVER
My transmission is ended; I expect a response.

OVERHEAD MANEUVER
A series of predetermined maneuvers prescribed for aircraft (often in
formation) for entry into the visual flight rules (VFR) traffic
pattern and to proceed to a landing.  An overhead maneuver is not an
instrument flight rules (IFR) approach procedure.  An aircraft
executing an overhead maneuver is considered VFR and the IFR flight
plan is cancelled when the aircraft reaches the ``initial point'' on
the initial approach portion of the maneuver.  The pattern usually
specifies the following: The radio contact required of the pilot.  The
speed to be maintained.  An initial approach 3 to 5 miles in length.
An elliptical pattern consisting of two 180 degree turns.  A break
point at which the first 180 degree turn is started.  The direction of
turns.  Altitude (at least 500 feet above the conventional pattern).
A ``Roll out'' on final approach not less than 1/4 mile from the
landing threshold and not less than 300 feet above the ground.

OVERLYING CENTER
The ARTCC facility that is responsible for arrival/departure
operations at a specific terminal.

P TIME
(See PROPOSED DEPARTURE TIME).

PAN PAN
The international radio telephony urgency signal. When repeated three
times, indicates uncertainty or alert followed by the nature of the
urgency.

PAR
(See PRECISION APPROACH RADAR).

PAR [ICAO]
(See ICAO Term PRECISION APPROACH RADAR).

PARALLEL ILS APPROACHES
Approaches to parallel runways by IFR aircraft which, when established
inbound toward the airport on the adjacent final approach courses, are
radar separated by at least 2 miles.

PARALLEL MLS APPROACHES
(See PARALLEL ILS APPROACHES).

PARALLEL OFFSET ROUTE
A parallel track to the left or right of the designated or established
airway/route. Normally associated with Area Navigation (RNAV)
operations.

PARALLEL RUNWAYS
Two or more runways at the same airport whose centerlines are
parallel. In addition to runway number, parallel runways are
designated as L (left) and R (right) or, if three parallel runways
exist, L (left), C (center), and R (right).

PATWAS
(See PILOTS AUTOMATIC TELEPHONE WEATHER ANSWERING SERVICE).

PBCT
(See PROPOSED BOUNDARY CROSSING TIME).

PERMANENT ECHO
Radar signals reflected from fixed objects on the earth's surface;
e.g., buildings, towers, terrain. Permanent echoes are distinguished
from ``ground clutter'' by being definable locations rather than large
areas. Under certain conditions they may be used to check radar
alignment.

PHOTO RECONNAISSANCE
Military activity that requires locating individual photo targets and
navigating to the targets at a preplanned angle and altitude. The
activity normally requires a lateral route width of 16 NM and altitude
range of 1,500 feet to 10,000 feet AGL.

PIDP
(See PROGRAMMABLE INDICATOR DATA PROCESSOR).

PILOT BRIEFING
A service provided by the FSS to assist pilots in flight
planning. Briefing items may include weather information, NOTAMS,
military activities, flow control information, and other items as
requested.

PILOT IN COMMAND
The pilot responsible for the operation and safety of an aircraft
during flight time.

PILOTS AUTOMATIC TELEPHONE WEATHER ANSWERING SERVICE
A continuous telephone recording containing current and forecast
weather information for pilots.

PILOT'S DISCRETION
When used in conjunction with altitude assignments, means that ATC has
offered the pilot the option of starting climb or descent whenever he
wishes and conducting the climb or descent at any rate he wishes. He
may temporarily level off at any intermediate altitude. However, once
he has vacated an altitude, he may not return to that altitude.

PILOT WEATHER REPORT
A report of meteorological phenomena encountered by aircraft in
flight.

PIREP
(See PILOT WEATHER REPORT).

POINT OUT
(See RADAR POINT OUT).

POLAR TRACK STRUCTURE
A system of organized routes between Iceland and Alaska which overlie
Canadian MNPS Airspace.

POSITION REPORT
A report over a known location as transmitted by an aircraft to ATC. 

POSITION SYMBOL
A computer generated indication shown on a radar display to indicate
the mode of tracking.

POSITIVE CONTROL
The separation of all air traffic within designated airspace by air
traffic control.

PRACTICE INSTRUMENT APPROACH
An instrument approach procedure conducted by a VFR or an IFR aircraft
for the purpose of pilot training or proficiency demonstrations.

PREARRANGED COORDINATION
A standardized procedure which permits an air traffic controller to
enter the airspace assigned to another air traffic controller without
verbal coordination.  The procedures are defined in a facility
directive which ensures standard separation between aircraft.

PRECIPITATION
Any or all forms of water particles (rain, sleet, hail, or snow) that
fall from the atmosphere and reach the surface.

PRECISION APPROACH
(See PRECISION APPROACH PROCEDURE).

PRECISION APPROACH PROCEDURE
A standard instrument approach procedure in which an electronic
glideslope/glidepath is provided; e.g., ILS/MLS and PAR.

PRECISION APPROACH RADAR
Radar equipment in some ATC facilities operated by the FAA and/or the
military services at joint use civil/military locations and separate
military installations to detect and display azimuth, elevation, and
range of aircraft on the final approach course to a runway. This
equipment may be used to monitor certain nonradar approaches, but is
primarily used to conduct a precision instrument approach (PAR)
wherein the controller issues guidance instructions to the pilot based
on the aircraft's position in relation to the final approach course
(azimuth), the glidepath (elevation), and the distance (range) from
the touchdown point on the runway as displayed on the radar scope.
The abbreviation ``PAR'' is also used to denote preferential arrival
routes in ARTCC computers.

PRECISION APPROACH RADAR [ICAO]
Primary radar equipment used to determine the position of an aircraft
during final approach, in terms of lateral and vertical deviations
relative to a nominal approach path, and in range relative to
touchdown.

PRECISION RUNWAY MONITOR
Provides air traffic controllers with high precision secondary
surveillance data for aircraft on final approach to closely spaced
parallel runways.  High resolution color monitoring displays (FMA) are
required to present surveillance track data to controllers along with
detailed maps depicting approaches and no transgression zone.

PREFERENTIAL ROUTES
Preferential routes (PDR's, PAR's, and PDAR's) are adapted in ARTCC
computers to accomplish inter/intrafacility controller coordination
and to assure that flight data is posted at the proper control
positions. Locations having a need for these specific inbound and
outbound routes normally publish such routes in local facility
bulletins, and their use by pilots minimizes flight plan route
amendments. When the workload or traffic situation permits,
controllers normally provide radar vectors or assign requested routes
to minimize circuitous routing. Preferential routes are usually
confined to one ARTCC's area and are referred to by the following
names or acronyms: Preferential Departure Route (PDR). A specific
departure route from an airport or terminal area to an en route point
where there is no further need for flow control. It may be included in
a Standard Instrument Departure (SID) or a Preferred IFR Route.
Preferential Arrival Route (PAR). A specific arrival route from an
appropriate en route point to an airport or terminal area. It may be
included in a Standard Terminal Arrival (STAR) or a Preferred IFR
Route. The abbreviation ``PAR'' is used primarily within the ARTCC and
should not be confused with the abbreviation for Precision Approach
Radar.  Preferential Departure and Arrival Route (PDAR). A route
between two terminals which are within or immediately adjacent to one
ARTCC's area. PDAR's are not synonymous with Preferred IFR Routes but
may be listed as such as they do accomplish essentially the same
purpose.

PREFERRED IFR ROUTES
Routes established between busier airports to increase system
efficiency and capacity. They normally extend through one or more
ARTCC areas and are designed to achieve balanced traffic flows among
high density terminals. IFR clearances are issued on the basis of
these routes except when severe weather avoidance procedures or other
factors dictate otherwise. Preferred IFR Routes are listed in the
Airport/Facility Directory. If a flight is planned to or from an area
having such routes but the departure or arrival point is not listed in
the Airport/Facility Directory, pilots may use that part of a
Preferred IFR Route which is appropriate for the departure or arrival
point that is listed. Preferred IFR Routes are correlated with SID's
and STAR's and may be defined by airways, jet routes, direct routes
between NAVAID's, Waypoints, NAVAID radials/DME, or any combinations
thereof.

PRE FLIGHT PILOT BRIEFING
(See PILOT BRIEFING).

PREVAILING VISIBILITY
(See VISIBILITY).

PRM
(See PRECISION RUNWAY MONITOR).

PROCEDURE TURN
The maneuver prescribed when it is necessary to reverse direction to
establish an aircraft on the intermediate approach segment or final
approach course. The outbound course, direction of turn, distance
within which the turn must be completed, and minimum altitude are
specified in the procedure. However, unless otherwise restricted, the
point at which the turn may be commenced and the type and rate of turn
are left to the discretion of the pilot.

PROCEDURE TURN [ICAO]
A manoeuvre in which a turn is made away from a designated track
followed by a turn in the opposite direction to permit the aircraft to
intercept and proceed along the reciprocal of the designated track.

PROCEDURE TURN INBOUND
That point of a procedure turn maneuver where course reversal has been
completed and an aircraft is established inbound on the intermediate
approach segment or final approach course. A report of ``procedure
turn inbound'' is normally used by ATC as a position report for
separation purposes.

PROFILE DESCENT
An uninterrupted descent (except where level flight is required for
speed adjustment; e.g., 250 knots at 10,000 feet MSL) from cruising
altitude/level to interception of a glideslope or to a minimum
altitude specified for the initial or intermediate approach segment of
a nonprecision instrument approach. The profile descent normally
terminates at the approach gate or where the glideslope or other
appropriate minimum altitude is intercepted.

PROGRAMMABLE INDICATOR DATA PROCESSOR
The PIDP is a modification to the AN/TPX-42 interrogator system
currently installed in fixed RAPCON's. The PIDP detects, tracks, and
predicts secondary radar aircraft targets. These are displayed by
means of computer generated symbols and alphanumeric characters
depicting flight identification, aircraft altitude, ground speed, and
flight plan data. Although primary radar targets are not tracked, they
are displayed coincident with the secondary radar targets as well as
with the other symbols and alphanumerics. The system has the
capability of interfacing with ARTCC's.

PROGRESS REPORT
(See POSITION REPORT).

PROGRESSIVE TAXI
Precise taxi instructions given to a pilot unfamiliar with the airport
or issued in stages as the aircraft proceeds along the taxi route.

PROHIBITED AREA
(See SPECIAL USE AIRSPACE).

PROHIBITED AREA [ICAO]
An airspace of defined dimensions, above the land areas or territorial
waters of a State, within which the flight of aircraft is prohibited.

PROPOSED BOUNDARY CROSSING TIME
Each center has a PBCT parameter for each internal airport. Proposed
internal flight plans are transmitted to the adjacent center if the
flight time along the proposed route from the departure airport to the
center boundary is less than or equal to the value of PBCT or if
airport adaptation specifies transmission regardless of PBCT.

PROPOSED DEPARTURE TIME
The time a scheduled flight will depart the gate (scheduled operators)
or the actual runway off time for nonscheduled operators. For EDCT
purposes, the ATCSCC adjusts the ``P'' time for scheduled operators to
reflect the runway off times.

PROTECTED AIRSPACE
The airspace on either side of an oceanic route/track that is equal to
one half the lateral separation minimum except where reduction of
protected airspace has been authorized.

PT
(See PROCEDURE TURN).

PTS
(See POLAR TRACK STRUCTURE).

PUBLISHED ROUTE
A route for which an IFR altitude has been established and published;
e.g., Federal Airways, Jet Routes, Area Navigation Routes, Specified
Direct Routes.

QUEUING
(See STAGING/QUEUING).

QLOW
(See QUOTA FLOW CONTROL).

QNE
The barometric pressure used for the standard altimeter setting (29.92
inches Hg.).

QNH
The barometric pressure as reported by a particular station.

QUADRANT
A quarter part of a circle, centered on a NAVAID, oriented clockwise
from magnetic north as follows: NE quadrant 000-089, SE quadrant
090-179, SW quadrant 180-269, NW quadrant 270-359.

QUICK LOOK
A feature of NAS Stage A and ARTS which provides the controller the
capability to display full data blocks of tracked aircraft from other
control positions.

QUOTA FLOW CONTROL
A flow control procedure by which the Central Flow Control Function
(CFCF) restricts traffic to the ARTC Center area having an impacted
airport, thereby avoiding sector/area saturation.

RADAR
A device which, by measuring the time interval between transmission
and reception of radio pulses and correlating the angular orientation
of the radiated antenna beam or beams in azimuth and/or elevation,
provides information on range, azimuth, and/or elevation of objects in
the path of the transmitted pulses.  Primary Radar. A radar system in
which a minute portion of a radio pulse transmitted from a site is
reflected by an object and then received back at that site for
processing and display at an air traffic control facility.  Secondary
Radar/Radar Beacon (ATCRBS). A radar system in which the object to be
detected is fitted with cooperative equipment in the form of a radio
receiver/transmitter (transponder). Radar pulses transmitted from the
searching transmitter/receiver (interrogator) site are received in the
cooperative equipment and used to trigger a distinctive transmission
from the transponder. This reply transmission, rather than a reflected
signal, is then received back at the transmitter/receiver site for
processing and display at an air traffic control facility.

RADAR [ICAO]
A radio detection device which provides information on range, azimuth
and/or elevation of objects.  Primary Radar. Radar system which uses
reflected radio signals.  Secondary Radar. Radar system wherein a
radio signal transmitted from a radar station initiates the
transmission of a radio signal from another station.

RADAR ADVISORY
The provision of advice and information based on radar observations.

RADAR ALTIMETER
(See RADIO ALTIMETER).

RADAR APPROACH
An instrument approach procedure which utilizes Precision Approach
Radar (PAR) or Airport Surveillance Radar (ASR).

RADAR APPROACH [ICAO]
An approach, executed by an aircraft, under the direction of a radar
controller.

RADAR APPROACH CONTROL FACILITY
A terminal ATC facility that uses radar and nonradar capabilities to
provide approach control services to aircraft arriving, departing, or
transiting airspace controlled by the facility I20(See APPROACH
CONTROL SERVICE). Provides radar ATC services to aircraft operating in
the vicinity of one or more civil and/or military airports in a
terminal area. The facility may provide services of a ground
controlled approach (GCA); i.e., ASR and PAR approaches. A radar
approach control facility may be operated by FAA, USAF, US Army, USN,
USMC, or jointly by FAA and a military service. Specific facility
nomenclatures are used for administrative purposes only and are
related to the physical location of the facility and the operating
service generally as follows: Army Radar Approach Control (ARAC)
(Army).  Radar Air Traffic Control Facility (RATCF) (Navy/FAA).  Radar
Approach Control (RAPCON) (Air Force/FAA).  Terminal Radar Approach
Control (TRACON) (FAA).  Tower/Airport Traffic Control Tower (ATCT)
(FAA). (Only those towers delegated approach control authority.).

RADAR ARRIVAL
An aircraft arriving at an airport served by a radar facility and in
radar contact with the facility.

RADAR BEACON
(See RADAR).

RADAR CONTACT
Used by ATC to inform an aircraft that it is identified on the radar
display and radar flight following will be provided until radar
identification is terminated. Radar service may also be provided
within the limits of necessity and capability. When a pilot is
informed of ``radar contact,'' he automatically discontinues reporting
over compulsory reporting points.  The term used to inform the
controller that the aircraft is identified and approval is granted for
the aircraft to enter the receiving controllers airspace.

RADAR CONTACT LOST
Used by ATC to inform a pilot that radar data used to determine the
aircraft's position is no longer being received, or is no longer
reliable and radar service is no longer being provided.  The loss may
be attributed to several factors including the aircraft merging with
weather or ground clutter, the aircraft operating below radar line of
sight coverage, the aircraft entering an area of poor radar return,
failure of the aircraft transponder, or failure of the ground radar
equipment. (See Clutter) (See Radar Contact)

RADAR CLUTTER [ICAO]
The visual indication on a radar display of unwanted signals.

RADAR CONTACT [ICAO] 
The situation which exists when the radar blip or radar position
symbol of a particular aircraft is seen and identified on a radar
display.

RADAR ENVIRONMENT
An area in which radar service may be provided.

RADAR FLIGHT FOLLOWING
The observation of the progress of radar identified aircraft, whose
primary navigation is being provided by the pilot, wherein the
controller retains and correlates the aircraft identity with the
appropriate target or target symbol displayed on the radar scope.

RADAR IDENTIFICATION
The process of ascertaining that an observed radar target is the radar
return from a particular aircraft.

RADAR IDENTIFICATION [ICAO]
The process of correlating a particular radar blip or radar position
symbol with a specific aircraft.

RADAR IDENTIFIED AIRCRAFT
An aircraft, the position of which has been correlated with an
observed target or symbol on the radar display.

RADAR MONITORING
(See RADAR SERVICE).

RADAR NAVIGATIONAL GUIDANCE
(See RADAR SERVICE).

RADAR POINT OUT
An action taken by a controller to transfer the radar identification
of an aircraft to another controller if the aircraft will or may enter
the airspace or protected airspace of another controller and radio
communications will not be transferred.

RADAR REQUIRED
A term displayed on charts and approach plates and included in FDC
Notams to alert pilots that segments of either an instrument approach
procedure or a route are not navigable because of either the absence
or unusability of a NAVAID. The pilot can expect to be provided radar
navigational guidance while transiting segments labeled with this
term.

RADAR ROUTE
A flight path or route over which an aircraft is
vectored. Navigational guidance and altitude assignments are provided
by ATC.

RADAR SEPARATION
(See RADAR SERVICE).

RADAR SERVICE
A term which encompasses one or more of the following services based
on the use of radar which can be provided by a controller to a pilot
of a radar identified aircraft.  Radar Monitoring. The radar flight
following of aircraft, whose primary navigation is being performed by
the pilot, to observe and note deviations from its authorized flight
path, airway, or route. When being applied specifically to radar
monitoring of instrument approaches; i.e., with precision approach
radar (PAR) or radar monitoring of simultaneous ILS/MLS approaches, it
includes advice and instructions whenever an aircraft nears or exceeds
the prescribed PAR safety limit or simultaneous ILS/MLS no
transgression zone.  Radar Navigational Guidance. Vectoring aircraft
to provide course guidance.  Radar Separation. Radar spacing of
aircraft in accordance with established minima.

RADAR SERVICE [ICAO]
Term used to indicate a service provided directly by means of radar.
Radar Monitoring. The use of radar for the purpose of providing
aircraft with information and advice relative to significant
deviations from nominal flight path.  Radar Separation. The separation
used when aircraft position information is derived from radar sources.

RADAR SERVICE TERMINATED
Used by ATC to inform a pilot that he will no longer be provided any
of the services that could be received while in radar contact. Radar
service is automatically terminated, and the pilot is not advised in
the following cases: An aircraft cancels its IFR flight plan, except
within Class B airspace, Class C airspace, a TRSA, or where Basic
Radar service is provided.  An aircraft conducting an instrument,
visual, or contact approach has landed or has been instructed to
change to advisory frequency.  An arriving VFR aircraft, receiving
radar service to a tower controlled airport within Class B airspace,
Class C airspace, a TRSA, or where sequencing service is provided, has
landed; or to all other airports, is instructed to change to tower or
advisory frequency.  An aircraft completes a radar approach.

RADAR SURVEILLANCE
The radar observation of a given geographical area for the purpose of
performing some radar function.

RADAR TRAFFIC ADVISORIES
Advisories issued to alert pilots to known or observed radar traffic
which may affect the intended route of flight of their aircraft.

RADAR TRAFFIC INFORMATION SERVICE
(See TRAFFIC ADVISORIES).

RADAR VECTORING [ICAO]
Provision of navigational guidance to aircraft in the form of specific
headings, based on the use of radar.

RADAR WEATHER ECHO INTENSITY LEVELS
Existing radar systems cannot detect turbulence. However, there is a
direct correlation between the degree of turbulence and other weather
features associated with thunderstorms and the radar weather echo
intensity. The National Weather Service has categorized radar weather
echo intensity for precipitation into six levels. These levels are
sometimes expressed during communications as ``VIP LEVEL'' 1 through 6
(derived from the component of the radar that produces the information
Video Integrator and Processor). The following list gives the ``VIP
LEVELS'' in relation to the precipitation intensity within a
thunderstorm: Level 1. WEAK Level 2. MODERATE Level 3. STRONG Level
4. VERY STRONG Level 5. INTENSE Level 6. EXTREME

RADIAL
A magnetic bearing extending from a VOR/VORTAC/TACAN navigation
facility.

RADIO
A device used for communication.
Used to refer to a flight service station; e.g., ``Seattle Radio'' is
used to call Seattle FSS.

RADIO ALTIMETER
Aircraft equipment which makes use of the reflection of radio waves
from the ground to determine the height of the aircraft above the
surface.

RADIO BEACON
(See NONDIRECTIONAL BEACON).

RADIO DETECTION AND RANGING
(See RADAR).

RADIO MAGNETIC INDICATOR
An aircraft navigational instrument coupled with a gyro compass or
similar compass that indicates the direction of a selected NAVAID and
indicates bearing with respect to the heading of the aircraft.

RAMP
(See APRON).

RANDOM ALTITUDE
An altitude inappropriate for direction of flight and/or not in
accordance with paragraph 4-60.

RANDOM ROUTE
Any route not established or charted/published or not otherwise
available to all users.

RC
(See ROAD RECONNAISSANCE).

RCAG
(See REMOTE COMMUNICATIONS AIR/GROUND FACILITY).

RCC
(See RESCUE COORDINATION CENTER).

RCO
(See REMOTE COMMUNICATIONS OUTLET).

RCR
(See RUNWAY CONDITION READING).

READ BACK
Repeat my message back to me.

RECEIVING CONTROLLER
A controller/facility receiving control of an aircraft from another
controller/facility.

RECEIVING FACILITY
(See RECEIVING CONTROLLER).

REDUCE SPEED TO (SPEED)
(See SPEED ADJUSTMENT).

REIL
(See RUNWAY END IDENTIFIER LIGHTS).

RELEASE TIME
A departure time restriction issued to a pilot by ATC (either directly
or through an authorized relay) when necessary to separate a departing
aircraft from other traffic.

RELEASE TIME [ICAO]
Time prior to which an aircraft should be given further clearance or
prior to which it should not proceed in case of radio failure.

REMOTE COMMUNICATIONS AIR/GROUND FACILITY
An unmanned VHF/UHF transmitter/receiver facility which is used to
expand ARTCC air/ground communications coverage and to facilitate
direct contact between pilots and controllers. RCAG facilities are
sometimes not equipped with emergency frequencies 121.5 mHz and 243.0
mHz.

REMOTE COMMUNICATIONS OUTLET
An unmanned communications facility remotely controlled by air traffic
personnel. RCO's serve FSS's. RTR's serve terminal ATC facilities. An
RCO or RTR may be UHF or VHF and will extend the communication range
of the air traffic facility. There are several classes of RCO's and
RTR's. The class is determined by the number of transmitters or
receivers. Classes A through G are used primarily for air/ground
purposes. RCO and RTR class O facilities are nonprotected outlets
subject to undetected and prolonged outages. RCO (O's) and RTR (O's)
were established for the express purpose of providing ground to ground
communications between air traffic control specialists and pilots
located at a satellite airport for delivering en route clearances,
issuing departure authorizations, and acknowledging instrument flight
rules cancellations or departure/landing times. As a secondary
function, they may be used for advisory purposes whenever the aircraft
is below the coverage of the primary air/ground frequency.

REMOTE TRANSMITTER/RECEIVER
(See REMOTE COMMUNICATIONS OUTLET).

REPORT
Used to instruct pilots to advise ATC of specified information; e.g.,
``Report passing Hamilton VOR.''

REPORTING POINT
A geographical location in relation to which the position of an
aircraft is reported.

REPORTING POINT [ICAO]
A specified geographical location in relation to which the position of
an aircraft can be reported.

REQUEST FULL ROUTE CLEARANCE
Used by pilots to request that the entire route of flight be read
verbatim in an ATC clearance. Such request should be made to preclude
receiving an ATC clearance based on the original filed flight plan
when a filed IFR flight plan has been revised by the pilot, company,
or operations prior to departure.

RESCUE COORDINATION CENTER
A search and rescue (SAR) facility equipped and manned to coordinate
and control SAR operations in an area designated by the SAR plan. The
U.S. Coast Guard and the U.S. Air Force have responsibility for the
operation of RCC's.

RESCUE CO ORDINATION CENTRE [ICAO]
A unit responsible for promoting efficient organization of search and
rescue service and for co ordinating the conduct of search and rescue
operations within a search and rescue region.

RESTRICTED AREA
(See SPECIAL USE AIRSPACE).

RESTRICTED AREA [ICAO]
An airspace of defined dimensions, above the land areas or territorial
waters of a State, within which the flight of aircraft is restricted
in accordance with certain specified conditions.

RESUME OWN NAVIGATION
Used by ATC to advise a pilot to resume his own navigational
responsibility. It is issued after completion of a radar vector or
when radar contact is lost while the aircraft is being radar vectored.

RMI
(See RADIO MAGNETIC INDICATOR).

RNAV
(See AREA NAVIGATION).

RNAV [ICAO]
(See ICAO Term AREA NAVIGATION).

RNAV APPROACH
An instrument approach procedure which relies on aircraft area
navigation equipment for navigational guidance.

ROAD RECONNAISSANCE
Military activity requiring navigation along roads, railroads, and
rivers. Reconnaissance route/route segments are seldom along a
straight line and normally require a lateral route width of 10 NM to
30 NM and an altitude range of 500 feet to 10,000 feet AGL.

ROGER
I have received all of your last transmission. It should not be used
to answer a question requiring a yes or a no answer.

ROLLOUT RVR
(See VISIBILITY).

ROUTE
A defined path, consisting of one or more courses in a horizontal
plane, which aircraft traverse over the surface of the earth.

ROUTE SEGMENT
As used in Air Traffic Control, a part of a route that can be defined
by two navigational fixes, two NAVAID's, or a fix and a NAVAID.

ROUTE SEGMENT [ICAO]
A portion of a route to be flown, as defined by two consecutive
significant points specified in a flight plan.

RSA
(See RUNWAY SAFETY AREA).

RTR
(See REMOTE TRANSMITTER/RECEIVER).

RUNWAY
A defined rectangular area on a land airport prepared for the landing
and takeoff run of aircraft along its length. Runways are normally
numbered in relation to their magnetic direction rounded off to the
nearest 10 degrees; e.g., Runway 01, Runway 25.

RUNWAY [ICAO]
A defined rectangular area on a land aerodrome prepared for the
landing and takeoff of aircraft.

RUNWAY CENTERLINE LIGHTING
(See AIRPORT LIGHTING).

RUNWAY CONDITION READING
Numerical decelerometer readings relayed by air traffic controllers at
USAF and certain civil bases for use by the pilot in determining
runway braking action. These readings are routinely relayed only to
USAF and Air National Guard Aircraft.

RUNWAY END IDENTIFIER LIGHTS
(See AIRPORT LIGHTING).

RUNWAY GRADIENT
The average slope, measured in percent, between two ends or points on
a runway. Runway gradient is depicted on Government aerodrome sketches
when total runway gradient exceeds 0.3%.

RUNWAY HEADING
The magnetic direction that corresponds with the runway centerline
extended, not the painted runway number. When cleared to ``fly or
maintain runway heading,'' pilots are expected to fly or maintain the
heading that corresponds with the extended centerline of the departure
runway. Drift correction shall not be applied; e.g., Runway 4, actual
magnetic heading of the runway centerline 044, fly 044.

RUNWAY IN USE/ACTIVE RUNWAY/DUTY RUNWAY
Any runway or runways currently being used for takeoff or
landing. When multiple runways are used, they are all considered
active runways. In the metering sense, a selectable adapted item which
specifies the landing runway configuration or direction of traffic
flow. The adapted optimum flight plan from each transition fix to the
vertex is determined by the runway configuration for arrival metering
processing purposes.

RUNWAY LIGHTS
(See AIRPORT LIGHTING).

RUNWAY MARKINGS
(See AIRPORT MARKING AIDS).

RUNWAY OVERRUN
In military aviation exclusively, a stabilized or paved area beyond
the end of a runway, of the same width as the runway plus shoulders,
centered on the extended runway centerline.

RUNWAY PROFILE DESCENT
An instrument flight rules (IFR) air traffic control arrival procedure
to a runway published for pilot use in graphic and/or textual form and
may be associated with a STAR. Runway Profile Descents provide routing
and may depict crossing altitudes, speed restrictions, and headings to
be flown from the en route structure to the point where the pilot will
receive clearance for and execute an instrument approach procedure. A
Runway Profile Descent may apply to more than one runway if so stated
on the chart.

RUNWAY SAFETY AREA
A defined surface surrounding the runway prepared, or suitable, for
reducing the risk of damage to airplanes in the event of an
undershoot, overshoot, or excursion from the runway.  The dimensions
of the RSA vary and can be determined by using the criteria contained
within Advisory Circular 150/5300-13, Chapter 3.  Figure 3-1 in
Advisory Circular 150/5300-13 depicts the RSA.  The design standards
dictate that the RSA shall be: Cleared, graded, and have no
potentially hazardous ruts, humps, depressions, or other surface
variations; Drained by grading or storm sewers to prevent water
accumulation; Capable, under dry conditions, of supporting snow
removal equipment, aircraft rescue and firefighting equipment, and the
occasional passage of aircraft without causing structural damage to
the aircraft; and, Free of objects, except for objects that need to be
located in the runway safety area because of their function. These
objects shall be constructed on low impact resistant supports
(frangible mounted structures) to the lowest practical height with the
frangible point no higher than 3 inches above grade.  RUNWAY USE
PROGRAM A noise abatement runway selection plan designed to enhance
noise abatement efforts with regard to airport communities for
arriving and departing aircraft. These plans are developed into runway
use programs and apply to all turbojet aircraft 12,500 pounds or
heavier; turbojet aircraft less than 12,500 pounds are included only
if the airport proprietor determines that the aircraft creates a noise
problem. Runway use programs are coordinated with FAA offices, and
safety criteria used in these programs are developed by the Office of
Flight Operations. Runway use programs are administered by the Air
Traffic Service as ``Formal'' or ``Informal'' programs.  Formal Runway
Use Program. An approved noise abatement program which is defined and
acknowledged in a Letter of Understanding between Flight Operations,
Air Traffic Service, the airport proprietor, and the users. Once
established, participation in the program is mandatory for aircraft
operators and pilots as provided for in Part 91.129.  Informal Runway
Use Program. An approved noise abatement program which does not
require a Letter of Understanding, and participation in the program is
voluntary for aircraft operators/pilots.

RUNWAY VISIBILITY VALUE
(See VISIBILITY).

RUNWAY VISUAL RANGE
(See VISIBILITY).

SAFETY ALERT
A safety alert issued by ATC to aircraft under their control if ATC is
aware the aircraft is at an altitude which, in the controller's
judgment, places the aircraft in unsafe proximity to terrain,
obstructions, or other aircraft. The controller may discontinue the
issuance of further alerts if the pilot advises he is taking action to
correct the situation or has the other aircraft in sight.
Terrain/Obstruction Alert. A safety alert issued by ATC to aircraft
under their control if ATC is aware the aircraft is at an altitude
which, in the controller's judgment, places the aircraft in unsafe
proximity to terrain/obstructions; e.g., ``Low Altitude Alert, check
your altitude immediately.''  Aircraft Conflict Alert. A safety alert
issued by ATC to aircraft under their control if ATC is aware of an
aircraft that is not under their control at an altitude which, in the
controller's judgment, places both aircraft in unsafe proximity to
each other. With the alert, ATC will offer the pilot an alternate
course of action when feasible; e.g., ``Traffic Alert, advise you turn
right heading zero niner zero or climb to eight thousand
immediately.''

SAIL BACK
A maneuver during high wind conditions (usually with power off) where
float plane movement is controlled by water rudders/opening and
closing cabin doors.

SAME DIRECTION AIRCRAFT
Aircraft are operating in the same direction when: They are following
the same track in the same direction; or Their tracks are parallel and
the aircraft are flying in the same direction; or Their tracks
intersect at an angle of less than 45 degrees.

SAR
(See SEARCH AND RESCUE).

SAY AGAIN
Used to request a repeat of the last transmission. Usually specifies
transmission or portion thereof not understood or received; e.g.,
``Say again all after ABRAM VOR.''

SAY ALTITUDE
Used by ATC to ascertain an aircraft's specific altitude/flight
level. When the aircraft is climbing or descending, the pilot should
state the indicated altitude rounded to the nearest 100 feet.

SAY HEADING
Used by ATC to request an aircraft heading. The pilot should state the
actual heading of the aircraft.

SDF
(See SIMPLIFIED DIRECTIONAL FACILITY).

SEA LANE
A designated portion of water outlined by visual surface markers for
and intended to be used by aircraft designed to operate on water.

SEARCH AND RESCUE
A service which seeks missing aircraft and assists those found to be
in need of assistance. It is a cooperative effort using the facilities
and services of available Federal, state and local agencies. The
U.S. Coast Guard is responsible for coordination of search and rescue
for the Maritime Region, and the U.S. Air Force is responsible for
search and rescue for the Inland Region. Information pertinent to
search and rescue should be passed through any air traffic facility or
be transmitted directly to the Rescue Coordination Center by
telephone.

SEARCH AND RESCUE FACILITY
A facility responsible for maintaining and operating a search and
rescue (SAR) service to render aid to persons and property in
distress. It is any SAR unit, station, NET, or other operational
activity which can be usefully employed during an SAR Mission; e.g., a
Civil Air Patrol Wing, or a Coast Guard Station.

SECTIONAL AERONAUTICAL CHARTS
(See AERONAUTICAL CHART).

SECTOR LIST DROP INTERVAL
A parameter number of minutes after the meter fix time when arrival
aircraft will be deleted from the arrival sector list.

SEE AND AVOID
A visual procedure wherein pilots of aircraft flying in visual
meteorological conditions (VMC), regardless of type of flight plan,
are charged with the responsibility to observe the presence of other
aircraft and to maneuver their aircraft as required to avoid the other
aircraft. Right of way rules are contained in Part 91.

SEGMENTED CIRCLE
A system of visual indicators designed to provide traffic pattern
information at airports without operating control towers.

SEGMENTS OF AN INSTRUMENT APPROACH PROCEDURE
An instrument approach procedure may have as many as four separate
segments depending on how the approach procedure is structured.
Initial Approach. The segment between the initial approach fix and the
intermediate fix or the point where the aircraft is established on the
intermediate course or final approach course.  Intermediate
Approach. The segment between the intermediate fix or point and the
final approach fix.  Final Approach. The segment between the final
approach fix or point and the runway, airport, or missed approach
point.  Missed Approach. The segment between the missed approach point
or the point of arrival at decision height and the missed approach fix
at the prescribed altitude.

SELECTED GROUND DELAYS
A traffic management procedure whereby selected flights are issued
ground delays to better regulate traffic flows over a particular fix
or area.

SEPARATION
In air traffic control, the spacing of aircraft to achieve their safe
and orderly movement in flight and while landing and taking off.

SEPARATION [ICAO]
Spacing between aircraft, levels or tracks.

SEPARATION MINIMA
The minimum longitudinal, lateral, or vertical distances by which
aircraft are spaced through the application of air traffic control
procedures.

SERVICE
A generic term that designates functions or assistance available from
or rendered by air traffic control.  For example, Class C service
would denote the ATC services provided within a Class C airspace area.

SEVERE WEATHER AVOIDANCE PLAN
An approved plan to minimize the affect of severe weather on traffic
flows in impacted terminal and/or ARTCC areas. SWAP is normally
implemented to provide the least disruption to the ATC system when
flight through portions of airspace is difficult or impossible due to
severe weather.

SEVERE WEATHER FORECAST ALERTS
Preliminary messages issued in order to alert users that a Severe
Weather Watch Bulletin (WW) is being issued. These messages define
areas of possible severe thunderstorms or tornado activity. The
messages are unscheduled and issued as required by the National Severe
Storm Forecast Center at Kansas City, Missouri.

SFA
(See SINGLE FREQUENCY APPROACH).

SFO
(See SIMULATED FLAMEOUT).

SHF
(See SUPER HIGH FREQUENCY).

SHORT RANGE CLEARANCE
A clearance issued to a departing IFR flight which authorizes IFR
flight to a specific fix short of the destination while air traffic
control facilities are coordinating and obtaining the complete
clearance.

SHORT TAKEOFF AND LANDING AIRCRAFT AIRCRAFT
An aircraft which, at some weight within its approved operating
weight, is capable of operating from a STOL runway in compliance with
the applicable STOL characteristics, airworthiness, operations, noise,
and pollution standards.

SIAP
(See STANDARD INSTRUMENT APPROACH PROCEDURE).

SIDESTEP MANEUVER
A visual maneuver accomplished by a pilot at the completion of an
instrument approach to permit a straight in landing on a parallel
runway not more than 1,200 feet to either side of the runway to which
the instrument approach was conducted.

SIGMET
A weather advisory issued concerning weather significant to the safety
of all aircraft. SIGMET advisories cover severe and extreme
turbulence, severe icing, and widespread dust or sandstorms that
reduce visibility to less than 3 miles.

SIGMET INFORMATION [ICAO]
Information issued by a meteorological watch office concerning the
occurrence or expected occurrence of specified en route weather
phenomena which may affect the safety of aircraft operations.

SIGNIFICANT METEOROLOGICAL INFORMATION
(See SIGMET).

SIGNIFICANT POINT
A point, whether a named intersection, a NAVAID, a fix derived from a
NAVAID(s), or geographical coordinate expressed in degrees of latitude
and longitude, which is established for the purpose of providing
separation, as a reporting point, or to delineate a route of flight.

SIMPLIFIED DIRECTIONAL FACILITY
A NAVAID used for nonprecision instrument approaches. The final
approach course is similar to that of an ILS localizer except that the
SDF course may be offset from the runway, generally not more than 3
degrees, and the course may be wider than the localizer, resulting in
a lower degree of accuracy.

SIMULATED FLAMEOUT
A practice approach by a jet aircraft (normally military) at idle
thrust to a runway. The approach may start at a relatively high
altitude over a runway (high key) and may continue on a relatively
high and wide downwind leg with a high rate of descent and a
continuous turn to final. It terminates in a landing or low
approach. The purpose of this approach is to simulate a flameout.

SIMULTANEOUS ILS APPROACHES
An approach system permitting simultaneous ILS/MLS approaches to
airports having parallel runways separated by at least 4,300 feet
between centerlines. Integral parts of a total system are ILS/MLS,
radar, communications, ATC procedures, and appropriate airborne
equipment.

SIMULTANEOUS MLS APPROACHES
(See SIMULTANEOUS ILS APPROACHES).

SIMULTANEOUS OPERATIONS ON INTERSECTING RUNWAYS
Operations which include simultaneous takeoffs and landings and/or
simultaneous landings when a landing aircraft is able and is
instructed by the controller to hold short of the intersecting runway
or designated hold short point.  Pilots are expected to promptly
inform the controller if the hold short clearance cannot be accepted.

SINGLE DIRECTION ROUTES
Preferred IFR Routes which are sometimes depicted on high altitude en
route charts and which are normally flown in one direction only.

SINGLE FREQUENCY APPROACH
A service provided under a letter of agreement to military single
piloted turbojet aircraft which permits use of a single UHF frequency
during approach for landing. Pilots will not normally be required to
change frequency from the beginning of the approach to touchdown
except that pilots conducting an en route descent are required to
change frequency when control is transferred from the air route
traffic control center to the terminal facility. The abbreviation
``SFA'' in the DOD FLIP IFR Supplement under ``Communications''
indicates this service is available at an aerodrome.

SINGLE PILOTED AIRCRAFT
A military turbojet aircraft possessing one set of flight controls,
tandem cockpits, or two sets of flight controls but operated by one
pilot is considered single piloted by ATC when determining the
appropriate air traffic service to be applied.

SLASH
A radar beacon reply displayed as an elongated target.

SLDI
(See SECTOR LIST DROP INTERVAL).

SLOT TIME
(See METER FIX TIME/SLOT TIME).

SLOW TAXI
To taxi a float plane at low power or low RPM.

SN
(See SYSTEM STRATEGIC NAVIGATION).

SPEAK SLOWER
Used in verbal communications as a request to reduce speech rate.

SPECIAL EMERGENCY
A condition of air piracy or other hostile act by a person(s) aboard
an aircraft which threatens the safety of the aircraft or its
passengers.

SPECIAL INSTRUMENT APPROACH PROCEDURE
(See INSTRUMENT APPROACH PROCEDURE).

SPECIAL USE AIRSPACE
Airspace of defined dimensions identified by an area on the surface of
the earth wherein activities must be confined because of their nature
and/or wherein limitations may be imposed upon aircraft operations
that are not a part of those activities. Types of special use airspace
are: Alert Area. Airspace which may contain a high volume of pilot
training activities or an unusual type of aerial activity, neither of
which is hazardous to aircraft. Alert Areas are depicted on
aeronautical charts for the information of nonparticipating
pilots. All activities within an Alert Area are conducted in
accordance with Federal Aviation Regulations, and pilots of
participating aircraft as well as pilots transiting the area are
equally responsible for collision avoidance.  Controlled Firing
Area. Airspace wherein activities are conducted under conditions so
controlled as to eliminate hazards to nonparticipating aircraft and to
ensure the safety of persons and property on the ground.  Military
Operations Area (MOA). An MOA is an airspace assignment of defined
vertical and lateral dimensions established outside Class A airspace
to separate/segregate certain military activities from IFR traffic and
to identify for VFR traffic where these activities are conducted.
Prohibited Area. Designated airspace within which the flight of
aircraft is prohibited.  Restricted Area. Airspace designated under
Part 73, within which the flight of aircraft, while not wholly
prohibited, is subject to restriction. Most restricted areas are
designated joint use and IFR/VFR operations in the area may be
authorized by the controlling ATC facility when it is not being
utilized by the using agency. Restricted areas are depicted on en
route charts. Where joint use is authorized, the name of the ATC
controlling facility is also shown.  Warning Area. Airspace which may
contain hazards to nonparticipating aircraft in international
airspace.

SPECIAL VFR CONDITIONS
Meteorlogical conditions that are less than those required for basic
VFR flight in Class B, C, D, or E surface areas and in which some
aircraft are permitted flight under visual flight rules.

SPECIAL VFR FLIGHT [ICAO]
A VFR flight cleared by air traffic control to operate within Class B,
C, D, and E surface areas in meterological conditions below VMC.

SPECIAL VFR OPERATIONS
Aircraft operating in accordance with clearances within Class B, C, D,
and E surface areas in weather conditions less than the basic VFR
weather minima. Such operations must be requested by the pilot and
approved by ATC.

SPEED
(See AIRSPEED).

SPEED ADJUSTMENT
An ATC procedure used to request pilots to adjust aircraft speed to a
specific value for the purpose of providing desired spacing. Pilots
are expected to maintain a speed of plus or minus 10 knots or 0.02
mach number of the specified speed.  Examples of speed adjustments
are: ``Increase/reduce speed to mach point (number).''
``Increase/reduce speed to (speed in knots)'' or ``Increase/reduce
speed (number of knots) knots.''

SPEED BRAKES
Moveable aerodynamic devices on aircraft that reduce airspeed during
descent and landing.

SPEED SEGMENTS
Portions of the arrival route between the transition point and the
vertex along the optimum flight path for which speeds and altitudes
are specified. There is one set of arrival speed segments adapted from
each transition point to each vertex. Each set may contain up to six
segments.

SQUAWK (Mode, Code, Function)
Activate specific modes/codes/functions on the aircraft transponder;
e.g., ``Squawk three/alpha, two one zero five, low.''

STAGING/QUEUING
The placement, integration, and segregation of departure aircraft in
designated movement areas of an airport by departure fix, EDCT, and/or
restriction.

STANDARD INSTRUMENT APPROACH PROCEDURE
(See INSTRUMENT APPROACH PROCEDURE).

STANDARD INSTRUMENT DEPARTURE
A preplanned instrument flight rule (IFR) air traffic control
departure procedure printed for pilot use in graphic and/or textual
form. SID's provide transition from the terminal to the appropriate en
route structure.

STANDARD INSTRUMENT DEPARTURE CHARTS
(See AERONAUTICAL CHART).

STANDARD RATE TURN
A turn of three degrees per second.

STANDARD TERMINAL ARRIVAL
A preplanned instrument flight rule (IFR) air traffic control arrival
procedure published for pilot use in graphic and/or textual
form. STAR's provide transition from the en route structure to an
outer fix or an instrument approach fix/arrival waypoint in the
terminal area.

STANDARD TERMINAL ARRIVAL CHARTS
(See AERONAUTICAL CHART).

STAND BY
Means the controller or pilot must pause for a few seconds, usually to
attend to other duties of a higher priority.  Also means to wait as in
``stand by for clearance.'' The caller should reestablish contact if a
delay is lengthy.  ``Stand by'' is not an approval or denial.

STAR
(See STANDARD TERMINAL ARRIVAL).

STATE AIRCRAFT
Aircraft used in military, customs and police service, in the
exclusive service of any government, or of any political subdivision,
thereof including the government of any state, territory, or
possession of the United States or the District of Columbia, but not
including any government owned aircraft engaged in carrying persons or
property for commercial purposes.

STATIC RESTRICTIONS
Those restrictions that are usually not subject to change, fixed, in
place, and/or published.

STATIONARY RESERVATIONS
Altitude reservations which encompass activities in a fixed
area. Stationary reservations may include activities, such as special
tests of weapons systems or equipment, certain U.S. Navy carrier,
fleet, and anti submarine operations, rocket, missile and drone
operations, and certain aerial refueling or similar operations.

STEPDOWN FIX
A fix permitting additional descent within a segment of an instrument
approach procedure by identifying a point at which a controlling
obstacle has been safely overflown.

STEP TAXI
To taxi a float plane at full power or high RPM.

STEP TURN
A maneuver used to put a float plane in a planing configuration prior
to entering an active sea lane for takeoff. The STEP TURN maneuver
should only be used upon pilot request.

STEREO ROUTE
A routinely used route of flight established by users and ARTCC's
identified by a coded name; e.g., ALPHA 2.These routes minimize flight
plan handling and communications.

STOL AIRCRAFT
(See SHORT TAKEOFF AND LANDING AIRCRAFT).

STOP ALTITUDE SQUAWK
Used by ATC to inform an aircraft to turn off the automatic altitude
reporting feature of its transponder. It is issued when the verbally
reported altitude varies 300 feet or more from the automatic altitude
report.

STOP AND GO
A procedure wherein an aircraft will land, make a complete stop on the
runway, and then commence a takeoff from that point.

STOP BURST
(See STOP STREAM).

STOP BUZZER
(See STOP STREAM).

STOPOVER FLIGHT PLAN
A flight plan format which permits in a single submission the filing
of a sequence of flight plans through interim full stop destinations
to a final destination.

STOP SQUAWK (Mode or Code)
Used by ATC to tell the pilot to turn specified functions of the
aircraft transponder off.

STOP STREAM
Used by ATC to request a pilot to suspend electronic countermeasure
activity.

STOPWAY
An area beyond the takeoff runway no less wide than the runway and
centered upon the extended centerline of the runway, able to support
the airplane during an aborted takeoff, without causing structural
damage to the airplane, and designated by the airport authorities for
use in decelerating the airplane during an aborted takeoff.

STRAIGHT IN APPROACH IFR
An instrument approach wherein final approach is begun without first
having executed a procedure turn, not necessarily completed with a
straight in landing or made to straight in landing minimums.

STRAIGHT IN APPROACH VFR
Entry into the traffic pattern by interception of the extended runway
centerline (final approach course) without executing any other portion
of the traffic pattern.

STRAIGHT IN LANDING
A landing made on a runway aligned within 30« of the final approach
course following completion of an instrument approach.

STRAIGHT IN LANDING MINIMUMS
(See LANDING MINIMUMS).

STRAIGHT IN MINIMUMS
(See STRAIGHT IN LANDING MINIMUMS).

SUBSTITUTIONS
Users are permitted to exchange CTA's. Normally, the airline
dispatcher will contact the ATCSCC with this request. The ATCSCC shall
forward approved substitutions to the TMU's who will notify the
appropriate terminals. Permissible swapping must not change the
traffic load for any given hour of an EQF program.

SUBSTITUTE ROUTE
A route assigned to pilots when any part of an airway or route is
unusable because of NAVAID status. These routes consist of: Substitute
routes which are shown on U.S. Government charts.  Routes defined by
ATC as specific NAVAID radials or courses.  Routes defined by ATC as
direct to or between NAVAID's.

SUNSET AND SUNRISE
The mean solar times of sunset and sunrise as published in the
Nautical Almanac, converted to local standard time for the locality
concerned. Within Alaska, the end of evening civil twilight and the
beginning of morning civil twilight, as defined for each locality.

SUPER HIGH FREQUENCY
The frequency band between 3 and 30 gigahertz (gHz). The elevation and
azimuth stations of the microwave landing system operate from 5031 mHz
to 5091 mHz in this spectrum.

SUPPLEMENTAL WEATHER SERVICE LOCATION
Airport facilities staffed with contract personnel who take weather
observations and provide current local weather to pilots via telephone
or radio. (All other services are provided by the parent FSS).

SUPPS
Refers to ICAO Document 7030 Regional Supplementary Procedures. SUPPS
contain procedures for each ICAO Region which are unique to that
Region and are not covered in the worldwide provisions identified in
the ICAO Air Navigation Plan. Procedures contained in chapter 8 are
based in part on those published in SUPPS.

SURFACE AREA
The airspace contained by the lateral boundary of the Class B, C, D,
or E airspace designated for an airport that begins at the surface and
extends upward.

SURPIC
A description of surface vessels in the area of a Search and Rescue
incident including their predicted positions and their
characteristics.

SURVEILLANCE APPROACH
An instrument approach wherein the air traffic controller issues
instructions, for pilot compliance, based on aircraft position in
relation to the final approach course (azimuth), and the distance
(range) from the end of the runway as displayed on the controller's
radar scope. The controller will provide recommended altitudes on
final approach if requested by the pilot.

SWAP
(See SEVERE WEATHER AVOIDANCE PLAN).

SWSL
(See SUPPLEMENTAL WEATHER SERVICE LOCATION).

SYSTEM STRATEGIC NAVIGATION
Military activity accomplished by navigating along a preplanned route
using internal aircraft systems to maintain a desired track. This
activity normally requires a lateral route width of 10 NM and altitude
range of 1,000 feet to 6,000 feet AGL with some route segments that
permit terrain following.

TACAN
(See TACTICAL AIR NAVIGATION).

TACAN ONLY AIRCRAFT
An aircraft, normally military, possessing TACAN with DME but no VOR
navigational system capability. Clearances must specify TACAN or
VORTAC fixes and approaches.

TACTICAL AIR NAVIGATION
An ultra high frequency electronic rho theta air navigation aid which
provides suitably equipped aircraft a continuous indication of bearing
and distance to the TACAN station.

TAILWIND
Any wind more than 90 degrees to the longitudinal axis of the runway.
The magnetic direction of the runway shall be used as the basis for
determining the longitudinal axis.

TAKEOFF AREA
(See LANDING AREA).

TAKE-OFF DISTANCE AVAILABLE [ICAO]
The length of the take-off run available plus the length of the
clearway, if provided.

TAKE-OFF RUN AVAILABLE [ICAO]
The length of runway declared available and suitable for the ground
run of an aeroplane take-off.

TARGET
The indication shown on a radar display resulting from a primary radar
return or a radar beacon reply.

TARGET [ICAO] In radar: 
1. Generally, any discrete object which reflects or retransmits energy
back to the radar equipment.
2. Specifically, an object of radar search or surveillance.

TARGET RESOLUTION
A process to ensure that correlated radar targets do not touch. Target
resolution shall be applied as follows: Between the edges of two
primary targets or the edges of the ASR-9 primary target symbol.
Between the end of the beacon control slash and the edge of a primary
target.  Between the ends of two beacon control slashes.  MANDATORY
TRAFFIC ADVISORIES AND SAFETY ALERTS SHALL BE ISSUED WHEN THIS
PROCEDURE IS USED.

TARGET SYMBOL
A computer generated indication shown on a radar display resulting
from a primary radar return or a radar beacon reply.

TAXI
The movement of an airplane under its own power on the surface of an
airport (Part 135.100-Note). Also, it describes the surface movement
of helicopters equipped with wheels.

TAXI INTO POSITION AND HOLD
Used by ATC to inform a pilot to taxi onto the departure runway in
takeoff position and hold. It is not authorization for takeoff. It is
used when takeoff clearance cannot immediately be issued because of
traffic or other reasons.

TAXI PATTERNS
Patterns established to illustrate the desired flow of ground traffic
for the different runways or airport areas available for use.

TCAS
(See TRAFFIC ALERT AND COLLISION AVOIDANCE SYSTEM).

TCH
(See THRESHOLD CROSSING HEIGHT).

TCLT
(See TENTATIVE CALCULATED LANDING TIME).

TDZE
(See TOUCHDOWN ZONE ELEVATION).

TELEPHONE INFORMATION BRIEFING SERVICE
A continuous telephone recording of meteorological and/or aeronautical
information.

TENTATIVE CALCULATED LANDING TIME
A projected time calculated for adapted vertex for each arrival
aircraft based upon runway configuration, airport acceptance rate,
airport arrival delay period, and other metered arrival aircraft. This
time is either the VTA of the aircraft or the TCLT/ACLT of the
previous aircraft plus the AAI, whichever is later. This time will be
updated in response to an aircraft's progress and its current
relationship to other arrivals.

TERMINAL AREA
A general term used to describe airspace in which approach control
service or airport traffic control service is provided.

TERMINAL AREA FACILITY
A facility providing air traffic control service for arriving and
departing IFR, VFR, Special VFR, and on occasion en route aircraft.

TERMINAL VFR RADAR SERVICE
A national program instituted to extend the terminal radar services
provided instrument flight rules (IFR) aircraft to visual flight rules
(VFR) aircraft.  The program is divided into four types service
referred to as basic radar service, terminal radar service area (TRSA)
service, Class B service and Class C service.  The type of service
provided at a particular location is contained in the Airport/Facility
Directory.  1.Basic Radar Service: These services are provided for VFR
aircraft by all commissioned terminal radar facilities.  Basic radar
service includes safety alerts, traffic advisories, limited radar
vectoring when requested by the pilot, and sequencing at locations
where procedures have been established for this purpose and/or when
covered by a letter of agreement.  The purpose of this service is to
adjust the flow of arriving IFR and VFR aircraft into the traffic
pattern in a safe and orderly manner and to provide traffic advisories
to departing VFR aircraft.  2.TRSA Service: This service provides, in
addition to basic radar service, sequencing of all IFR and
participating VFR aircraft to the primary airport and separation
between all participating VFR aircraft. The purpose of this service is
to provide separation between all participating VFR aircraft and all
IFR aircraft operating within the area defined as a TRSA.  3.Class C
Service: This service provides, in addition to basic radar service,
approved separation between IFR and VFR aircraft, and sequencing of
VFR aircraft, and sequencing of VFR arrivals to the primary airport.
4.Class B Service: This service provides, in addition to basic radar
service, approved separation of aircraft based on IFR, VFR, and/or
weight, and sequencing of VFR arrivals to the primary airport(s).

TERMINAL RADAR SERVICE AREA
Airspace surrounding designated airports wherein ATC provides radar
vectoring, sequencing, and separation on a full time basis for all IFR
and participating VFR aircraft. Service provided in a TRSA is called
Stage III Service. The AIM contains an explanation of TRSA. TRSA's are
depicted on VFR aeronautical charts. Pilot participation is urged but
is not mandatory.

TERMINAL VERY HIGH FREQUENCY OMNIDIRECTIONAL RANGE STATION
A very high frequency terminal omnirange station located on or near an
airport and used as an approach aid.

TERRAIN FOLLOWING
The flight of a military aircraft maintaining a constant AGL altitude
above the terrain or the highest obstruction. The altitude of the
aircraft will constantly change with the varying terrain and/or
obstruction.

TETRAHEDRON
A device normally located on uncontrolled airports and used as a
landing direction indicator. The small end of a tetrahedron points in
the direction of landing. At controlled airports, the tetrahedron, if
installed, should be disregarded because tower instructions supersede
the indicator.

TF
(See TERRAIN FOLLOWING).

THAT IS CORRECT
The understanding you have is right.

360 OVERHEAD
(See OVERHEAD APPROACH).

THRESHOLD
The beginning of that portion of the runway usable for landing.

THRESHOLD CROSSING HEIGHT
The theoretical height above the runway threshold at which the
aircraft's glideslope antenna would be if the aircraft maintains the
trajectory established by the mean ILS glideslope or MLS glidepath.

THRESHOLD LIGHTS
(See AIRPORT LIGHTING).

TIBS
(See TELEPHONE INFORMATION BRIEFING SERVICE).

TIME GROUP
Four digits representing the hour and minutes from the 24-hour
clock. Time groups without time zone indicators are understood to be
UTC (Coordinated Universal Time); e.g., ``0205.'' The term ``Zulu'' is
used when ATC procedures require a reference to UTC. A time zone
designator is used to indicate local time; e.g., ``0205M.'' The end
and the beginning of the day are shown by ``2400'' and ``0000,''
respectively.

TMPA
(See TRAFFIC MANAGEMENT PROGRAM ALERT).

TMU
(See TRAFFIC MANAGEMENT UNIT).

TODA [ICAO]
(See ICAO Term TAKE-OFF DISTANCE AVAILABLE).

TORA [ICAO]
(See ICAO Term TAKE-OFF RUN AVAILABLE).

TORCHING
The burning of fuel at the end of an exhaust pipe or stack of a
reciprocating aircraft engine, the result of an excessive richness in
the fuel air mixture.

TOTAL ESTIMATED ELAPSED TIME [ICAO]
For IFR flights, the estimated time required from take off to arrive
over that designated point, defined by reference to navigation aids,
from which it is intended that an instrument approach procedure will
be commenced, or, if no navigation aid is associated with the
destination aerodrome, to arrive over the destination aerodrome. For
VFR flights, the estimated time required from takeoff to arrive over
the destination aerodrome.

TOUCH AND GO
An operation by an aircraft that lands and departs on a runway without
stopping or exiting the runway.

TOUCH AND GO LANDING
(See TOUCH AND GO).

TOUCHDOWN
The point at which an aircraft first makes contact with the landing
surface.  Concerning a precision radar approach (PAR), it is the point
where the glide path intercepts the landing surface.

TOUCHDOWN [ICAO]
The point where the nominal glide path intercepts the runway.

TOUCHDOWN RVR
(See VISIBILITY).

TOUCHDOWN ZONE
The first 3,000 feet of the runway beginning at the threshold. The
area is used for determination of Touchdown Zone Elevation in the
development of straight in landing minimums for instrument approaches.

TOUCHDOWN ZONE [ICAO]
The portion of a runway, beyond the threshold, where it is intended
landing aircraft first contact the runway.

TOUCHDOWN ZONE ELEVATION
The highest elevation in the first 3,000 feet of the landing
surface. TDZE is indicated on the instrument approach procedure chart
when straight in landing minimums are authorized.

TOUCHDOWN ZONE LIGHTING
(See AIRPORT LIGHTING).

TOWER
A terminal facility that uses air/ground communications, visual
signaling, and other devices to provide ATC services to aircraft
operating in the vicinity of an airport or on the movement
area. Authorizes aircraft to land or takeoff at the airport controlled
by the tower or to transit the Class D airspace area regardless of
flight plan or weather conditions (IFR or VFR). A tower may also
provide approach control services (radar or nonradar).

TOWER EN ROUTE CONTROL SERVICE
The control of IFR en route traffic within delegated airspace between
two or more adjacent approach control facilities. This service is
designed to expedite traffic and reduce control and pilot
communication requirements.

TOWER TO TOWER
(See TOWER EN ROUTE CONTROL SERVICE).

TPX-42
A numeric beacon decoder equipment/system. It is designed to be added
to terminal radar systems for beacon decoding. It provides rapid
target identification, reinforcement of the primary radar target, and
altitude information from Mode C.

TRACK
The actual flight path of an aircraft over the surface of the earth.

TRACK [ICAO]
The projection on the earth's surface of the path of an aircraft, the
direction of which path at any point is usually expressed in degrees
from North (True, Magnetic, or Grid).

TRAFFIC
A term used by a controller to transfer radar identification of an
aircraft to another controller for the purpose of coordinating
separation action. Traffic is normally issued:
(a) in response to a handoff or point out,
(b) in anticipation of a handoff or point out, or
(c) in conjunction with a request for control of an aircraft.
A term used by ATC to refer to one or more aircraft.

TRAFFIC ADVISORIES
Advisories issued to alert pilots to other known or observed air
traffic which may be in such proximity to the position or intended
route of flight of their aircraft to warrant their attention. Such
advisories may be based on: Visual observation.  Observation of radar
identified and nonidentified aircraft targets on an ATC radar display,
or Verbal reports from pilots or other facilities.  (Identification),
TRAFFIC ALERT. ADVISE YOU TURN LEFT/RIGHT (specific heading if
appropriate), AND/OR CLIMB/DESCEND (specific altitude if appropriate)
IMMEDIATELY. (See SAFETY ALERT).

TRAFFIC ALERT AND COLLISION AVOIDANCE SYSTEM
An airborne collision avoidance system based on radar beacon signals
which operates independent of ground based equipment. TCAS I generates
traffic advisories only. TCAS II generates traffic advisories, and
resolution (collision avoidance) advisories in the vertical plane.

TRAFFIC INFORMATION
(See TRAFFIC ADVISORIES).

TRAFFIC IN SIGHT
Used by pilots to inform a controller that previously issued traffic
is in sight.

TRAFFIC MANAGEMENT PROGRAM ALERT
A term used in a Notice to Airmen (NOTAM) issued in conjunction with a
special traffic management program to alert pilots to the existence of
the program and to refer them to either the Notices to Airmen
publication or a special traffic management program advisory message
for program details. The contraction TMPA is used in NOTAM text.

TRAFFIC MANAGEMENT UNIT
The entity in ARTCC's and designated terminals responsible for direct
involvement in the active management of facility traffic. Usually
under the direct supervision of an assistant manager for traffic
management.

TRAFFIC NO FACTOR
Indicates that the traffic described in a previously issued traffic
advisory is no factor.

TRAFFIC NO LONGER OBSERVED
Indicates that the traffic described in a previously issued traffic
advisory is no longer depicted on radar, but may still be a factor.

TRAFFIC PATTERN
The traffic flow that is prescribed for aircraft landing at, taxiing
on, or taking off from an airport. The components of a typical traffic
pattern are upwind leg, crosswind leg, downwind leg, base leg, and
final approach.  Upwind Leg. A flight path parallel to the landing
runway in the direction of landing.  Crosswind Leg. A flight path at
right angles to the landing runway off its upwind end.  Downwind
Leg. A flight path parallel to the landing runway in the direction
opposite to landing. The downwind leg normally extends between the
crosswind leg and the base leg.  Base Leg. A flight path at right
angles to the landing runway off its approach end. The base leg
normally extends from the downwind leg to the intersection of the
extended runway centerline.  Final Approach. A flight path in the
direction of landing along the extended runway centerline. The final
approach normally extends from the base leg to the runway. An aircraft
making a straight in approach VFR is also considered to be on final
approach.

TRANSCRIBED WEATHER BROADCAST
A continuous recording of meteorological and aeronautical information
that is broadcast on L/MF and VOR facilities for pilots.

TRANSFER OF CONTROL
That action whereby the responsibility for the separation of an
aircraft is transferred from one controller to another.

TRANSFER OF CONTROL [ICAO]
Transfer of responsibility for providing air traffic control service.

TRANSFERRING CONTROLLER
A controller/facility transferring control of an aircraft to another
controller/facility.

TRANSFERRING FACILITY
(See TRANSFERRING CONTROLLER).

TRANSFERRING UNIT/CONTROLLER [ICAO]
Air traffic control unit/air traffic controller in the process of
transferring the responsibility for providing air traffic control
service to an aircraft to the next air traffic control unit/air
traffic controller along the route of flight.

TRANSITION
The general term that describes the change from one phase of flight or
flight condition to another; e.g., transition from en route flight to
the approach or transition from instrument flight to visual flight.  A
published procedure (SID Transition) used to connect the basic SID to
one of several en route airways/jet routes, or a published procedure
(STAR Transition) used to connect one of several en route airways/jet
routes to the basic STAR.

TRANSITIONAL AIRSPACE
That portion of controlled airspace wherein aircraft change from one
phase of flight or flight condition to another.

TRANSITION POINT
A point at an adapted number of miles from the vertex at which an
arrival aircraft would normally commence descent from its en route
altitude. This is the first fix adapted on the arrival speed segments.

TRANSMISSOMETER
An apparatus used to determine visibility by measuring the
transmission of light through the atmosphere. It is the measurement
source for determining runway visual range (RVR) and runway visibility
value (RVV).

TRANSMITTING IN THE BLIND
A transmission from one station to other stations in circumstances
where two way communication cannot be established, but where it is
believed that the called stations may be able to receive the
transmission.

TRANSPONDER
The airborne radar beacon receiver/transmitter portion of the Air
Traffic Control Radar Beacon System (ATCRBS) which automatically
receives radio signals from interrogators on the ground, and
selectively replies with a specific reply pulse or pulse group only to
those interrogations being received on the mode to which it is set to
respond.

TRANSPONDER [ICAO]
A receiver/transmitter which will generate a reply signal upon proper
interrogation; the interrogation and reply being on different
frequencies.

TRANSPONDER CODES
(See CODES).

TRSA
(See TERMINAL RADAR SERVICE AREA).

TURBOJET AIRCRAFT
An aircraft having a jet engine in which the energy of the jet
operates a turbine which in turn operates the air compressor.

TURBOPROP AIRCRAFT
An aircraft having a jet engine in which the energy of the jet
operates a turbine which drives the propeller.

TWEB
(See TRANSCRIBED WEATHER BROADCAST).

TVOR
(See TERMINAL VERY HIGH FREQUENCY OMNIDIRECTIONAL RANGE STATION).

TWO WAY RADIO COMMUNICATIONS FAILURE
(See LOST COMMUNICATIONS).

UDF
(See DIRECTION FINDER).

UHF
(See ULTRAHIGH FREQUENCY).

ULTRAHIGH FREQUENCY
The frequency band between 300 and 3,000 mHz. The bank of radio
frequencies used for military air/ground voice communications. In some
instances this may go as low as 225 mHz and still be referred to as
UHF.

ULTRALIGHT VEHICLE
An aeronautical vehicle operated for sport or recreational purposes
which does not require FAA registration, an airworthiness certificate,
nor pilot certification. They are primarily single occupant vehicles,
although some two place vehicles are authorized for training
purposes. Operation of an ultralight vehicle in certain airspace
requires authorization from ATC.

UNABLE
Indicates inability to comply with a specific instruction, request, or
clearance.

UNDER THE HOOD
Indicates that the pilot is using a hood to restrict visibility
outside the cockpit while simulating instrument flight. An
appropriately rated pilot is required in the other control seat while
this operation is being conducted.

UNICOM
A nongovernment communication facility which may provide airport
information at certain airports. Locations and frequencies of UNICOMs
are shown on aeronautical charts and publications.

UNPUBLISHED ROUTE
A route for which no minimum altitude is published or charted for
pilot use. It may include a direct route between NAVAIDS, a radial, a
radar vector, or a final approach course beyond the segments of an
instrument approach procedure.

UPWIND LEG
(See TRAFFIC PATTERN).

URGENCY
A condition of being concerned about safety and of requiring timely
but not immediate assistance; a potential distress condition.

URGENCY [ICAO]
A condition concerning the safety of an aircraft or other vehicle, or
of person on board or in sight, but which does not require immediate
assistance.

USAFIB
(See ARMY AVIATION FLIGHT INFORMATION BULLETIN).

UVDF
(See DIRECTION FINDER).

VASI
(See VISUAL APPROACH SLOPE INDICATOR).

VDF
(See DIRECTION FINDER).

VDP
(See VISUAL DESCENT POINT).

VECTOR
A heading issued to an aircraft to provide navigational guidance by
radar.

VERIFY
Request confirmation of information; e.g., ``verify assigned
altitude.''

VERIFY SPECIFIC DIRECTION OF TAKEOFF (OR TURNS AFTER TAKEOFF)
Used by ATC to ascertain an aircraft's direction of takeoff and/or
direction of turn after takeoff. It is normally used for IFR
departures from an airport not having a control tower. When direct
communication with the pilot is not possible, the request and
information may be relayed through an FSS, dispatcher, or by other
means.

VERTEX
The last fix adapted on the arrival speed segments. Normally, it will
be the outer marker of the runway in use. However, it may be the
actual threshold or other suitable common point on the approach path
for the particular runway configuration.

VERTEX TIME OF ARRIVAL
A calculated time of aircraft arrival over the adapted vertex for the
runway configuration in use. The time is calculated via the optimum
flight path using adapted speed segments.

VERTICAL SEPARATION
Separation established by assignment of different altitudes or flight
levels.

VERTICAL SEPARATION [ICAO]
Separation between aircraft expressed in units of vertical distance.

VERTICAL TAKEOFF AND LANDING AIRCRAFT
Aircraft capable of vertical climbs and/or descents and of using very
short runways or small areas for takeoff and landings. These aircraft
include, but are not limited to, helicopters.

VERY HIGH FREQUENCY
The frequency band between 30 and 300 mHz. Portions of this band, 108
to 118 mHz, are used for certain NAVAIDS; 118 to 136 mHz are used for
civil air/ground voice communications. Other frequencies in this band
are used for purposes not related to air traffic control.

VERY HIGH FREQUENCY OMNIDIRECTIONAL RANGE STATION
(See VOR).

VERY LOW FREQUENCY
The frequency band between 3 and 30 kHz.

VFR
(See VISUAL FLIGHT RULES).

VFR AIRCRAFT
An aircraft conducting flight in accordance with visual flight rules.

VFR CONDITIONS
Weather conditions equal to or better than the minimum for flight
under visual flight rules. The term may be used as an ATC
clearance/instruction only when: An IFR aircraft requests a
climb/descent in VFR conditions.  The clearance will result in noise
abatement benefits where part of the IFR departure route does not
conform to an FAA approved noise abatement route or altitude.  A pilot
has requested a practice instrument approach and is not on an IFR
flight plan.  All pilots receiving this authorization must comply with
the VFR visibility and distance from cloud criteria in Part 91. Use of
the term does not relieve controllers of their responsibility to
separate aircraft in Class B and Class C airspace or TRSA's as
required by FAA Order 7110.65. When used as an ATC
clearance/instruction, the term may be abbreviated ``VFR;'' e.g.,
``MAINTAIN VFR,'' ``CLIMB/DESCEND VFR,'' etc.

VFR FLIGHT
(See VFR AIRCRAFT).

VFR MILITARY TRAINING ROUTES
Routes used by the Department of Defense and associated Reserve and
Air Guard units for the purpose of conducting low altitude navigation
and tactical training under VFR below 10,000 feet MSL at airspeeds in
excess of 250 knots IAS.

VFR NOT RECOMMENDED
An advisory provided by a flight service station to a pilot during a
preflight or inflight weather briefing that flight under visual flight
rules is not recommended. To be given when the current and/or forecast
weather conditions are at or below VFR minimums. It does not abrogate
the pilot's authority to make his own decision.

VFR ON TOP
ATC authorization for an IFR aircraft to operate in VFR conditions at
any appropriate VFR altitude (as specified in FAR and as restricted by
ATC). A pilot receiving this authorization must comply with the VFR
visibility, distance from cloud criteria, and the minimum IFR
altitudes specified in Part 91. The use of this term does not relieve
controllers of their responsibility to separate aircraft in Class B
and Class C airspace or TRSA's as required by FAA Order 7110.65.

VFR TERMINAL AREA CHARTS
(See AERONAUTICAL CHART).

VHF
(See VERY HIGH FREQUENCY).

VHF OMNIDIRECTIONAL RANGE/TACTICAL AIR NAVIGATION
(See VORTAC).

VIDEO MAP
An electronically displayed map on the radar display that may depict
data such as airports, heliports, runway centerline extensions,
hospital emergency landing areas, NAVAID's and fixes, reporting
points, airway/route centerlines, boundaries, handoff points, special
use tracks, obstructions, prominent geographic features, map alignment
indicators, range accuracy marks, minimum vectoring altitudes.

VISIBILITY
The ability, as determined by atmospheric conditions and expressed in
units of distance, to see and identify prominent unlighted objects by
day and prominent lighted objects by night. Visibility is reported as
statute miles, hundreds of feet or meters.  Flight Visibility. The
average forward horizontal distance, from the cockpit of an aircraft
in flight, at which prominent unlighted objects may be seen and
identified by day and prominent lighted objects may be seen and
identified by night.  Ground Visibility. Prevailing horizontal
visibility near the earth's surface as reported by the United States
National Weather Service or an accredited observer.  Prevailing
Visibility. The greatest horizontal visibility equaled or exceeded
throughout at least half the horizon circle which need not necessarily
be continuous.  Runway Visibility Value (RVV). The visibility
determined for a particular runway by a transmissometer. A meter
provides a continuous indication of the visibility (reported in miles
or fractions of miles) for the runway. RVV is used in lieu of
prevailing visibility in determining minimums for a particular runway.
Runway Visual Range (RVR). An instrumentally derived value, based on
standard calibrations, that represents the horizontal distance a pilot
will see down the runway from the approach end. It is based on the
sighting of either high intensity runway lights or on the visual
contrast of other targets whichever yields the greater visual
range. RVR, in contrast to prevailing or runway visibility, is based
on what a pilot in a moving aircraft should see looking down the
runway. RVR is horizontal visual range, not slant visual range. It is
based on the measurement of a transmissometer made near the touchdown
point of the instrument runway and is reported in hundreds of
feet. RVR is used in lieu of RVV and/or prevailing visibility in
determining minimums for a particular runway.  a. Touchdown RVR. The
RVR visibility readout values obtained from RVR equipment serving the
runway touchdown zone.  b. Mid RVR. The RVR readout values obtained
from RVR equipment located midfield of the runway.  c. Rollout
RVR. The RVR readout values obtained from RVR equipment located
nearest the rollout end of the runway.

VISIBILITY [ICAO]
The ability, as determined by atmospheric conditions and expressed in
units of distance, to see and identify prominent unlighted objects by
day and prominent lighted objects by night.  Flight Visibility. The
visibility forward from the cockpit of an aircraft in flight.  Ground
Visibility. The visibility at an aerodrome as reported by an
accredited observer.  Runway Visual Range [RVR]. The range over which
the pilot of an aircraft on the centre line of a runway can see the
runway surface markings or the lights delineating the runway or
identifying its centre line.

VISUAL APPROACH
An approach wherein an aircraft on an IFR flight plan, operating in
VFR conditions under the control of an air traffic control facility
and having an air traffic control authorization, may proceed to the
airport of destination in VFR conditions.

VISUAL APPROACH [ICAO]
An approach by an IFR flight when either part or all of an instrument
approach procedure is not completed and the approach is executed in
visual reference to terrain.

VISUAL APPROACH SLOPE INDICATOR
(See AIRPORT LIGHTING).

VISUAL DESCENT POINT
A defined point on the final approach course of a nonprecision
straight in approach procedure from which normal descent from the MDA
to the runway touchdown point may be commenced, provided the approach
threshold of that runway, or approach lights, or other markings
identifiable with the approach end of that runway are clearly visible
to the pilot.

VISUAL FLIGHT RULES
Rules that govern the procedures for conducting flight under visual
conditions. The term ``VFR'' is also used in the United States to
indicate weather conditions that are equal to or greater than minimum
VFR requirements. In addition, it is used by pilots and controllers to
indicate type of flight plan.

VISUAL HOLDING
The holding of aircraft at selected, prominent geographical fixes
which can be easily recognized from the air.

VISUAL METEOROLOGICAL CONDITIONS
Meteorological conditions expressed in terms of visibility, distance
from cloud, and ceiling equal to or better than specified minima.

VISUAL SEPARATION
A means employed by ATC to separate aircraft in terminal areas. There
are two ways to effect this separation: The tower controller sees the
aircraft involved and issues instructions, as necessary, to ensure
that the aircraft avoid each other.  A pilot sees the other aircraft
involved and upon instructions from the controller provides his own
separation by maneuvering his aircraft as necessary to avoid it. This
may involve following another aircraft or keeping it in sight until it
is no longer a factor.

VLF
(See VERY LOW FREQUENCY).

VMC
(See VISUAL METEOROLOGICAL CONDITIONS).

VOR
A ground based electronic navigation aid transmitting very high
frequency navigation signals, 360 degrees in azimuth, oriented from
magnetic north. Used as the basis for navigation in the National
Airspace System. The VOR periodically identifies itself by Morse Code
and may have an additional voice identification feature. Voice
features may be used by ATC or FSS for transmitting
instructions/information to pilots.

VORTAC
A navigation aid providing VOR azimuth, TACAN azimuth, and TACAN
distance measuring equipment (DME) at one site.

VORTICES
Circular patterns of air created by the movement of an airfoil through
the air when generating lift. As an airfoil moves through the
atmosphere in sustained flight, an area of area of low pressure is
created above it. The air flowing from the high pressure area to the
low pressure area around and about the tips of the airfoil tends to
roll up into two rapidly rotating vortices, cylindrical in
shape. These vortices are the most predominant parts of aircraft wake
turbulence and their rotational force is dependent upon the wing
loading, gross weight, and speed of the generating aircraft. The
vortices from medium to heavy aircraft can be of extremely high
velocity and hazardous to smaller aircraft.

VOR TEST SIGNAL
(See VOT).

VOT
A ground facility which emits a test signal to check VOR receiver
accuracy. Some VOT's are available to the user while airborne, and
others are limited to ground use only.

VR
(See VFR MILITARY TRAINING ROUTES).

VTA
(See VERTEX TIME OF ARRIVAL).

VTOL AIRCRAFT
(See VERTICAL TAKEOFF AND LANDING AIRCRAFT).

WA
(See AIRMET).

WAKE TURBULENCE
Phenomena resulting from the passage of an aircraft through the
atmosphere. The term includes vortices, thrust stream turbulence, jet
blast, jet wash, propeller wash, and rotor wash both on the ground and
in the air.

WARNING AREA
(See SPECIAL USE AIRSPACE).

WAYPOINT
A predetermined geographical position used for route/instrument
approach definition, or progress reporting purposes, that is defined
relative to a VORTAC station or in terms of latitude/longitude
coordinates.

WEATHER ADVISORY
In aviation weather forecast practice, an expression of hazardous
weather conditions not predicted in the area forecast, as they affect
the operation of air traffic and as prepared by the NWS.

WHEN ABLE
When used in conjunction with ATC instructions, gives the pilot the
latitude to delay compliance until a condition or event has been
reconciled. Unlike ``pilot discretion,'' when instructions are
prefaced ``when able,'' the pilot is expected to seek the first
opportunity to comply. Once a maneuver has been initiated, the pilot
is expected to continue until the specifications of the instructions
have been met. ``When able,'' should not be used when expeditious
compliance is required.

WILCO
I have received your message, understand it, and will comply with it.

WIND SHEAR
A change in wind speed and/or wind direction in a short distance
resulting in a tearing or shearing effect. It can exist in a
horizontal or vertical direction and occasionally in both.

WING TIP VORTICES
(See VORTICES).

WORDS TWICE
As a request: ``Communication is difficult. Please say every phrase
twice.''  As information: ``Since communications are difficult, every
phrase in this message will be spoken twice.''

WORLD AERONAUTICAL CHARTS
(See AERONAUTICAL CHART).

WS
(See SIGMET).

WST
(See CONVECTIVE SIGMET).